## Slide 1: WF on WRC-19 outcome and impact on RAN4 specifications
NTT DOCOMO, INC.,
3GPP TSG-RAN WG4 Meeting #94-e-Bis R4-2005738
Online Meeting, 20-30 Apr 2020

## Slide 2: Background(1/4)
Adding new NS values to existing bands.
  If a new NS values for an existing band after devices supporting the band come out on the market, If a network cannot know with which NS values each of the UEs can deal, this generates the following issues.
  For configuring EN-DC
    After initial access via LTE, when a NW configure EN-DC with a band, that process can fail if the NW signals NS values which are not supported by the UE.
  For HO for SA and NSA
    If the source gNB does not convey the NS values each UE can support to the target gNB, then the HO process can fail
  Proposals, such as the introduction of a feature for UEs to report newly introduced NS values for existing bands and careful timing of the release in which new NS values are introduced, have been discussed

## Slide 3: Background(2/4)
Handling of regulation to change from a loose limit to stringent one with transition period
  This generates the following issues
  Invoked larger A-MPR from the changeover date
    A relaxed limit will continue to apply to UEs ‘brought into use’ before changeover date.
    If the UEs can deal with a different NS_Y for a stringent limit than NS_X for relaxed one, they will follow NS_Y from the changeover date since the network will start to use NS_Y with 1st priority. Then larger A-MPR is applicable even though that is not necessary for those UEs manufactured before the date.
  Allows UEs violating regulation to work if the NS value for stringent one is optional support
    Since the UEs ‘brought into use’ before the date and after the date may not support the NS values for stringent one, it is indistinguishable from them. Thus a network would allow for UEs not meeting a stringent limit to work. Note the detail is captured in the Annex.

## Slide 4: Background(3/4)
NS value mapping and A-MPR issues
  If -8dBm/200MHz is still needed or not
  If 1dBm/200MHz for n257 and 7dBm/1GHz should be included into NS_200 or not.
  The current spec defines -10dBm/100MHz for n258 as independent requirement from EESS protection.
  Necessity of A-MPR re-evaluation based on the updated NS values and associated limits.

## Slide 5: Background(4/4)
Common understanding of which regulatory requirements TS38.101-2 should address (for information only):
  Note: Necessity of -8dBm/200MHz is FFS.
  Note: Some must be met simultaneously like 1/2/4 and 1/3/4 for Europe.
Region3/ | Requirement 1 | Requirement 2 | Requirement 3 | Requirement 4 | Requirement 5 | Requirement 6
Global, US, Japan | Protected range: spurious Band applicability: all Limit: -13 dBm/MHz | Protected range: 23.6 - 24.0 GHz Band applicability: n258, n257 Limit: +1 dBm/200 MHz | Protected range: 23.6 - 24.0 GHz Band applicability: n258, n257 Limit: -5 dBm/200 MHz | N/A | Protected range: 36.0 to 37.0 GHz Band applicability: n260, n259 Limit: +7 dBm/1000 MHz | Protected range: 36.0 to 37.0 GHz Band applicability: n260, n259 Limit: -13 dBm/1 MHz
Europe |  |  |  | Protected range: 7.25 GHz ≤ f ≤ 2nd harmonic Band applicability: all bands Limit: -10 dBm/100 MHz |  | 

## Slide 6: WF
The followings are package agreements.
  How to resolve the issues identified in the background slides:
    Alt 1: Explicit signaling
      1-1/1-3: The introduction of a feature for a UE to report newly supported NS value(s) for a legacy band to a network
      1-2: reusing modifiedMPR feature
    Alt 2: delay introduction of new NS values(s)
    RAN4 to select a solution based on these alternatives during RAN4 #95e.
    If RAN4 cannot select one of them in RAN4#95e, send an LS to RAN2 to ask which is more suitable solution as signaling mechanism.
  NS mapping and associated A-MPR
  After the process on how to resolve the newly introduced NS issues and NS mapping is agreed, each band will be handled independently without waiting for the completion of the other bands.

## Slide 7: Alt 1-1/1-2/1-3: A NS reporting feature
Common to Alt 1-1/1-2/1-3: A feature for a UE to report newly supported NS value(s) for a legacy band to a network is introduced in the following way.
  NS reporting is release-independent if no backward compatibility issue identified
  Reporting newly introduced NS values is optional unless otherwise stated
  UEs shall support all NS values in a certain band corresponding to the applicable emissions requirements and report new NS values when it is ‘brought into use’ or similar regulatory wording. Specific NS values to be mandatory is further discussed.
    The detailed reasons are captured in the Annex in this WF
  A note is added to NS values for changed emissions limits (example shown: -5dBm/200MHz after 1st Sep 2027 ) in a following way.
    This NS value will apply to UEs brought into use after 1st Sep 2027 and these UEs need to support the new NS. The new NS and associated limit will not apply to UEs which have been brought into use prior to this date. For those legacy UEs, the previous NS and associated limit will continue to apply after the date.
    The above note can be updated in R4#95-e meeting. Note: some more informative note may be added to share a drawback to implement NS for -5dBm/200MHz before the changeover date.
Alt 1-3: In Alt 1-3, supporting of NS values is optional.

## Slide 8: Alt 2: delay introduction of new NS
Agree that it is mandatory for a UE designed against Rel-X to support all NS values defined in the Rel-X version of the specification
Introduce new NS value(s) into the specification at the start of Rel-X
  The timing of Rel-X, given the regulation transition period is FFS
  To accommodate differences in regional transition periods, different sets of NS values(s) can be introduced at Rel-X and Rel-Y, respectively
  Perform the necessary A-MPR studies prior to the beginning of Rel-X to ensure new NS value(s) can be specified at the start of Rel-X
Investigate whether the knowledge of the UE’s release is sufficient to mitigate the EN-DC initial access, EN-DC HO, and SA HO issues identified in the background

## Slide 9: NS mapping and associated A-MPR
NS mapping: Two options are captured in the slides 8 & 9.
  Adopt one of the two based on necessity of -8dBm/200MHz.
    At least Ericsson should provide a specific reference(s) on necessity of -8dBm/200MHz.
    Author memo: it would be great if Ericsson could provide the reference(s) during the R4#94bis-e. Better to chose one of the two during R4#94bis.
  +1dBm/200MHz for n257 & 7dBm/1GHz for n259 are introduced into NS_200, respectively, at least if no A-MPR is needed.
  The same mapping for single CC is applied to that for CA.
A-MPR
  A-MPR values for NS values captured in slide 8 & 9 are concluded in RAN4#95-e based on technical analysis.

## Slide 10: Option 1: -8dBm/200MHz stays
 | n257 | n258 | n259 | n260
NS_200 | 1dBm/200MHz into general | No change | 7dBm/1GHz into general | No change
NS_201 | -8dBm/200MHz + -10dBm/100MHz | -8dBm/200MHz + -10dBm/100MHz |  | 
NS_202 | -10dBm/100MHz + 1dBm/200MHz | -10dBm/100MHz + 1dBm/200MHz |  | 
NS_203 |  | 1dBm/200MHz |  | 
NS_204 | -5dBm/200MHz | -5dBm/200MHz |  | 
NS_205 |  |  |  | 7dBm/1GHz + -13dBm/MHz
NS_206 | -5dBm/200MHz + -10dBm/100MHz | -5dBm/200MHz + -10dBm/100MHz |  | 
Note: n261 is omitted since the band has no connection with lower/upper EESS protection.

## Slide 11: Option 2: -8dBm/200MHz isn’t necessary
 | n257 | n258 | n259 | n260
NS_200 | 1dBm/200MHz into general | No change | 7dBm/1GHz into general | No change
NS_201 | FFS | FFS |  | 
NS_202 | -10dBm/100MHz + 1dBm/200MHz | -10dBm/100MHz + 1dBm/200MHz |  | 
NS_203 |  | 1dBm/200MHz |  | 
NS_204 | -5dBm/200MHz | -5dBm/200MHz |  | 
NS_205 |  |  |  | 7dBm/1GHz + -13dBm/MHz
Note: n261 is omitted since the band has no connection with lower/upper EESS protection.

## Slide 12: Annex: Mandatory reason for NS values for -5dBm/200MHz from the changeover date
If UEs ‘brought into use’ after the changeover date do not support the new NS values for -5dBm/200MHz, a network capable of n257/n258 is not able to distinguish the following UEs.
  UEs without the NS values manufactured before the date
  UEs without the NS values manufactured after the date
That means that both above UEs are dealing with NS_200.
In other words, the latter UEs violating the regulation under the network is enabled since the network still use NS_200 to enable UEs manufacture before the date in addition to the new NS values.
Note that it is ok for UEs ‘brought into use’ before the changeover date to support the new NS values for -5dBm/200MHz. Those UEs, however, will unnecessarily use larger A-MPR from the date.