## Slide 1: WF on supporting a new channel bandwidth added to an existing operating bands in a manner of release independence from Rel-15
ZTE
3GPP TSG-RAN WG4 #95e Meeting
Electronic Meeting, May 25th – Jun 5th 2020
R4-2008384

## Slide 2: Background – Illustration of “Release independent support” (1)
A new feature “Pancake” introduced and claim release independent from Release-M
N
M
M+1
“Pancake supported”
“Pancake” requirements specified in TS 38.307 of Rel-N

## Slide 3: Background – Illustration of “Release independent support” (2)
Features listed in TS 38.307, each with a corresponding separate clause
  Operating band
  UE power class
  CA configuration
  SUL configuration
It just works perfectly fine for the above features listed in clauses in TS 38.307
But…

## Slide 4: Background – Illustration of the potential issue (3)
For a “sub-feature” associated with “listed features” in TS 38.307, there could be an issue with release independent support from Rel-15, e.g., new channel bandwidth adding to an existing operating band:
  “Sub-feature” is not listed in a separate clause in TS 38.307
  “Existing operating band” means “requirements” to be fulfilled is NOT from Rel-N, but Rel-15 where the existing operating band was introduced
A new feature “Pancake” introduced and claim release independent from Release-M
N
M
M+1
“Pancake supported”
“Pancake” requirements specified in TS 38.307 of Rel-M

## Slide 5: Background – Illustration of the potential issue (4)
And the requirements to be fulfilled for “Operating bands” in TS 38.307 Rel-15 are empty  No requirements to be fulfilled!

## Slide 6: Wayforward (1)
For a new channel bandwidth added to an existing operating band in Rel-15, the release independent support from Rel-15 to the new channel bandwidth should be captured in TS 38.307 Rel-15

## Slide 7: Wayforward (2)
How to capture in TS 38.307 Rel-15 ?
  Option 1: Fill in the blank for the two tables on operating bands as in Rel-16
  Option 2: Add a sentence indicating “new channel bandwidth to an existing operating band” should be treated as a new “operating band” equivalently
  Option 3: Create a new table for “UE channel bandwidth”
  Option 4: Other options not precluded