## Slide 1: WF on NR-U ACS and blocking requirements
Apple
R4-2008435
3GPP TSG-RAN WG4 Meeting #95-e
Electronic meeting, 25 May – 5 June 2020

## Slide 2: Background
1st Round discussion open issues:
Interefer Bandwidth
  Fixed 20 MHz for single carrier and for intra-band contiguous carrier aggregation for ACS and blocking
ACS value
  For baseline 20 MHz wanted + 20 MHz interferer: 18 – 20 dB and 24 – 27 dB
    Can companies accept 22 dB as compromise value?
    Scale the ACS value by 10log(bandwidth/20MHz) for bandwidth greater than 20 MHz
  Case 1 with wanted signal at REFSENS+14. Is case 2 needed? At what power level?
  For CA, scaling according to aggregated bandwidth of CC’s or according to maximum aggregated in the bandwidth class?
Blocking
  In-band blocking baseline 20 MHz wanted + 20 MHz interferer: REFSENS + 9 dB
  Out-of-band blocking range 3 exception to -20 dBm for Finterferer > 4200 MHz

## Slide 3: WF - ACS requirement
Single Carrier:
  ACS value is TBD at 20 MHz CBW
  Interferer BW is 20 MHz for all CBW
  Scale the ACS value by 10log(bandwidth/20MHz) for BW larger than 20 MHz.
  Case 1: Wanted signal power is REFSENS + 14 dB
  Case 2: [Not specified]
Intra-band contiguous CA:
  Interferer BW is 20 MHz (BW Classes B, C, D, E, I, M, N, O)
  [ACS level of intra-band CA set according to the actual configured aggregated bandwidth]

## Slide 4: WF - Blocking requirements
In-band Blocking
  Wanted signal power is REFSENS + 9 dB at 20 MHz CBW
  Interferer BW is 20 MHz for single carrier and for intra-band contiguous CA (BW Classes B, C, D, E, I, M, N, O)
  [For intra-band contiguous CA the wanted signal power level per CC scaling is according to the actual configured aggregated bandwidth]
Out of Band Blocking
  Range 3 exception to -20 dBm for Finterferer > 4200 MHz
  The wanted signal power level is fixed at REFSENS + 9 dB for single carrier and intra-band contiguous CA