## Slide 1: WF on FR2 inter-band DL CA
MediaTek Inc.
R4-2008487
3GPP TSG-RAN WG4 Meeting #95-e
Online, 25th May - 5th June 2020

## Slide 2: Background and wording alignment
UE band pairs capability [1]
  CBM = common beam management between the band pair
  IBM = independent beam management between the band pairs
    Network assumes IBM UE supports both co-located and non-co-located deployments
Network deployment scenarios [1]
  co-located deployment
  non-co-located deployment
Network does not assume CBM UE supports non-co-located deployment [1]
  This doesn’t mean the network cannot configure CBM UE in non-co-located deployment [1]
Network assumes IBM UE supports both co-located and non-co-located deployments. [1]

## Slide 3: Background and wording alignment (cont’d)
Network: co-located deployment
Network: non-co-located deployment
L
H
L
H
IBM UE
CBM UE
L
H
L+H
IBM UE
L
H
Illustration by L+H band pair example for reference only

## Slide 4: Capability signalling
Introduce UE IBM/CBM capability per band pair
  Introduce frequency separation class for band combinations with bands within one band group, regardless of CBM or IBM, is FFS
Whether Introduce support of co-located and/or non-co-located deployment capability per band pair or not?
  No
    It implies:
      UE CBM band pair shall support co-located deployment and meet corresponding requirement
      UE IBM band pair shall support co-located and non-co-located deployment, and meet corresponding requirement

## Slide 5: EIS requirements for co-located & non-co-located deployment
About common coverage EIS requirement, that consider co-located deployment
  Alt-1 Inter-band DL CA common coverage EIS requirement shall be defined for IBM and CBM band pairs, respectively
    It implies “while UEs meet inter-band DL CA common coverage requirement (#1), it means the UEs support co-located network deployment.”
  Alt-2 Inter-band DL CA common coverage EIS requirement shall be defined for IBM bands pairs only
    It implies “while IBM UEs meet inter-band DL CA common coverage requirement (#1), it means the IBM UEs support co-located network deployment.
    It implies “while CBM UEs meet spherical coverage requirements of each band in single carrier mode, it means the CBM UEs support co-located network deployment”

## Slide 6: EIS requirements for co-located & non-co-located deployment (cont’d)
About non-common coverage EIS requirement, that consider non-co-located deployment
  No matter UE capability is IBM or CBM, no need to define non-common spherical coverage requirement (#2)
    For IBM UE, while it meets common coverage EIS requirement, it implies the IBM UE also can support non-co-located deployment.
    For CBM UE, network does not assume CBM UE supports non-co-located deployment [1]. Hence, no corresponding requirement is required.

## Slide 7: EIS requirements for co-located & non-co-located deployment (cont’d)
Overview table for reference only |  | 
 | Network scenario: Co-located deployment | Network scenario: Non-co-located deployment
UE IBM band pair | (#1) Inter-band DL CA common coverage EIS requirement: Shall be defined | (#2) Inter-band DL CA non-common coverage EIS requirement: No need to define
UE CBM band pair | (#1) Inter-band DL CA common coverage EIS requirement Alt-1: shall be defined Alt-2: no need to define | (#2) Inter-band DL CA non-common coverage EIS requirement: No need to define (*) (*) Network does not assume CBM UE supports non-co-located deployment [1]

## Slide 8: (#1) Inter-band DL CA common coverage EIS requirement
Adopt requirement on common area of where both bands meet their respective single CC EIS spherical coverage requirements (separate inter-band CA relaxations may apply)
Equivalent requirement values are FFS
Illustrations for reference only
The area of sphere pass CC1 requirement
The area of sphere pass CC2 requirement
The area of sphere pass CC1+CC2 inter-band DL CA common coverage EIS requirement

## Slide 9: Equivalent inter-band DL CA EIS requirement framework
Equivalent inter-band DL CA EIS requirement framework:
  Inter-band DL CA peak EIS = Single-band EIS_peak + MBR_peak + inter-band DL CA relaxation_peak
  Inter-band DL CA spherical EIS = Single-band EIS_spherical + MBR_spherical + inter-band DL CA relaxation_spherical
The inter-band DL CA relaxation value would consider such as extra hardware component loss/beam squint loss/common coverage loss in discussion stage

## Slide 10: Inter-band DL CA relaxation value portfolio
About different band pairs, relaxation value is defined:
  Alt-1: per band pair
    Ex: “n257+n260” and “n258+n260” may have different relaxation value
  Alt-2: per band pair type among existed bands (i.e. intra-group and inter-group concept)
    Ex: all L(28)+H(39) band pairs apply same relaxation value. Ex: “n257(L)+n260(H)” and “n258(L)+n260(H)” have same relaxation
About UE IBM/CBM capability, relaxation value is defined:
  Alt-1: as one relaxation value that covers both IBM/CBM capability
  Alt-2: as separate relaxation values for same band pair/ band pair type (depends on first bullet) depending on IBM or CBM capability, respectively
If inter-band DL CA relaxation value of specific band pair is not defined yet, it means that there is no corresponding inter-band DL CA requirement.

## Slide 11: Inter-band DL CA relaxation value evaluation
Example for reference only |  | 
For L+H band pair type inter-band DL CA relaxation value |  | 
Loss components (dB) | Relexation_peak | Relexation_Spherical
Extra hardware component loss |  | 
Beam squint loss |  | 
Common coverage loss |  | 
Other loss |  | 
Proposal |  | 
Companies are encouraged to provide inter-band DL CA band pair requests from market demand
Companies are encouraged to show what loss components are included of the proposed inter-band DL CA relaxation value
  If the specific loss component is not applicable for specific proposal from technical judgement, to show “0 dB” is suggested rather than remove the whole loss component.

## Slide 12: PSD difference
PSD for CBM band pair
  Minimize PSD difference at baseband in test condition for L+L, H+H
  FFS for L+H
PSD for IBM band pair is FFS

## Slide 13: References
 | Tdoc # | Title | Source
[1] | R4-2005736 | WF on inter-band DL CA_v3 GTW | Qualcomm