## Slide 1: WF on gNB requirements for NR positioning
Ericsson
3GPP TSG-RAN WG4 Meeting # 95-e
Electronic Meeting, May 25-June 05, 2020
Agenda: 6.8
R4-2008668

## Slide 2: Selection of option for gNB measurement accuracy requirements
FFS: gNB measurements for which accuracy shall be defined.
Candidate options:
  Option 1:
    Define accuracy for SRS-RSRP and gNB Rx-Tx time difference
  Option 2:
    Define accuracy for SRS-RSRP, gNB Rx-Tx time difference and UL RTOA

## Slide 3: Optionality of gNB accuracy requirements
FFS: whether gNB positioning measurement accuracy is optional or mandatory if gNB supports the positioning measurement.
Candidate options:
  Option 1:
    Mandatory for gNB to meet accuracy for supported positioning measurement
  Option 2:
    Optional for gNB to meet accuracy for supported positioning measurement
FFS: whether to defer the decision until gNB accuracy work has progressed e.g. gNB accuracy is being specified in the specification.

## Slide 4: Side conditions for gNB measurement accuracy
Issue-1: FFS: One set or separate set of side conditions (e.g. SINR) for defining gNB positioning measurement accuracy.
  Option 1:
    One set of side conditions to meet accuracy for UE in serving as well as in neighbour cells
  Option 2:
    Separate side conditions to meet accuracy for UE in serving and for UE in neighbour cells
Issue-2: FFS: Methodology for deriving gNB positioning measurement accuracy.
  Candidate options for deriving side conditions:
    Option 1:
      Side conditions based on clause 7.2, TS 36.111
    Option 2:
      Side conditions for serving cell is derived from system simulations
      Side conditions for neighbor cell is based on clause 7.2, TS 36.111.

## Slide 5: Beam configuration for gNB measurement accuracy
FFS: Antenna beam configuration assumption in gNB for defining gNB positioning measurement accuracy.
Candidate options:
  Option 1:
    Fixed antenna beams are assumed in gNB for deriving accuracy
  Option 2:
    Accuracy does not depend on antenna beam configuration in gNB i.e. do not assume fixed gNB antenna beams

## Slide 6: PRS/SRS configurations for gNB measurement accuracy
Issue-1: PRS->Accuracy is defined and met for all PRS configurations.
Issue-2: SRS->FFS: whether accuracy is defined and met for all or subset of SRS configurations:
Candidate options:
  Option 1:
    Accuracy is defined and met for all SRS configurations.
  Option 2:
    Accuracy is defined for all SRS configurations but is met only for subset of SRS configurations declared by the manufacturer
  Option 3:
    Accuracy is defined and met for subset of SRS configurations.

## Slide 7: Applicability of gNB Rx-Tx accuracy under TA change
In both serving and neighbour cells of the UE, gNB Rx-Tx accuracy shall not apply if UE transmit timing changes due to gNB sending TA during the measurement period.

## Slide 8: Accuracy for different BS types (1-C, 1-H, 1-O, 2-O)
FFS: whether gNB positioning measurement accuracy requirement depends on BS type (1-C, 1-H, 1-O, 2-O).
Candidate options:
  Option 1:
    Same accuracy requirement applies for all BS types
  Option 2:
    Accuracy requirement depends on BS type