## Slide 1: WF on NR-U BS OBUE
ZTE, Nokia
R4-20xxxxx
3GPP TSG-RAN WG4 #95e
25th May. - 5th June. 2020

## Slide 2: Background
  In RAN4#93, R4-1915979 WF NR-U spectrum emission mask was approved where agreed mask is mainly defined in relative mask method instead of absolute mask method. For NR-U BS SEM defined in TS 38.104, it should be defined as absolute levels, therefore some further discuss how to implement that.
  To be more specific, there are two major issues needed to further discussion,
  10MHz SEM mask;
  scaling factor for absolute SEM considering different channel bandwidth supported by NR-U.

## Slide 3: Relative SEM for transmission bandwidths without non-transmitted channels for up- and down-link [approved in R4-1915979]
N = Nominal Transmission Bandwidth

## Slide 4: Applicability for 10MHz, 20MHz, 60MHz and 80MHz
  For 10MHz, 20MHz, 40MHz, 60MHz and 80MHz, it should follow the relative mask defined in Slide#3 with below exception
    For 10MHz, the 1st breaking point should be 0.5N+0.5/-0.5N-0.5 instead of 0.5N+1/-0.5N-1 which is coming from LAA spec.
Notes: Huawei: Mask for 10MHz LAA mask also?
ZTE: no need to align with LAA mask. In LAA we have 10 dB further decreasing , for NR-U not that case.
E///: previously we have agreement to use bran mask for NR-U.

## Slide 5: Scaling factor for absolute SEM for NR-U
Backgroung information
  for LAA 20MHz absolute mask, scaling factor [-32.6dB] for PSD calculation is dervied in the following way:
  -10*log10(18MHz/100KHz)-10dB for 1st adjacent emission mask where 10dB is coming from WiFi mask alignment.
  for LAA 10MHz absolute mask, scaling factor [-29.5dB]for PSD calculation is dervied in the following way:
  -10*log10(9MHz/100KHz)-10dB for 1st adjacent emission mask where 10dB is coming from WiFi mask alignment.
Agreement for NR-U:
  Prated,c,AC-10*log10(BWChannel/100KHz)
  BWChannel is used as this is independent of SCS. See definition in 38.104.

## Slide 6: Absolute SEM for transmission bandwidths without non-transmitted channels for up- and down-link [20,40,60,80MHz]

## Slide 7: Absolute SEM for transmission bandwidths without non-transmitted channels for up- and down-link [10MHz]

## Slide 8: Absolute SEM for transmission bandwidths with single non-transmitted channels for up- and down-link [60,80MHz]

## Slide 9: Absolute SEM for transmission bandwidths with two non-transmitted channels for up- and down-link [80MHz]

## Slide 10: Absolute SEM for transmission bandwidths with non-transmitted channels on the edge of transmitted channels for UL and DL [40,60,80MHz]
Notes: Nokia: -20dBm come from LAA， in UE we take [ ] on -20dBm for further check. Better aligned with in BS. Originally from regulatory.
Huawei: measurement BW [2MHz] already with [], not sure whether [] needed or for requirements [-20dBm].
Nokia: 38.104 CR quite heavy and lots of changes. How to handle this big running CR?
Session chair recommendation: Use single big CR for final agreed to introduce NR-U into TS38.104 core specifications.
For this meeting, there are overlapped CR from E/// , Nokia, ZTE; big CR to merge all the agreements ?
37.107 CR?
All the formal CRs will be agreed a package to BS specifications (38.104,37.104,36.104,37.107)
For 6GHz hold on the decision, pending on the decision on NR-U sys parameter discussion.
Whether need to support 1-H BS type for NR-U?
-> Further check this .
Nokia/E///: we think NR-U 1-C, 1-H.

## Slide 11: References:
  [1]R4-2007411,NR-U BS UEM requirement, ZTE Corporation
  [2]R4-2007412, CR for NR-U BS UEM requirement, ZTE Corporation
  [3]R4-2007480, CR for NR-U BS UEM requirement, Nokia