## Slide 1: 3GPP TSG-RAN WG4 Meeting #95-e R4-2008810 Electronic Meeting, 25th May – 5th June., 2020
Huawei, HiSilicon
Way forward on NR URLLC BS performance requirements

## Slide 2: Background
The following WFs were approved:
  R4-1915913: Way forward on NR URLLC demodulation and CSI requirements, RAN4 #93
  R4-2002429: Way forward for NR BS URLLC performance requirements, RAN4 #94-e
  R4-2005528: Way forward for NR BS URLLC performance requirements, RAN4 #94bis-e

## Slide 3
Agreements:
  SCS/CBW: 15 KHz for 5/10 MHz, 30 KHz for 10/40 MHz with test applicability rule.
  Whether to define requirements for FR2：Yes with test applicability rule.
      3a: The performance requirements are only applicable for BS only supporting FR2 or supporting both FR1 and FR2
PUSCH demodulation requirements for high reliability with higher BLER and/or confidence level:

## Slide 4: PUSCH demodulation requirements for high reliability with higher BLER and/or confidence level:
PUSCH aggregation factor for 15 kHz SCS:
    Option 1: No requirement for 15 kHz SCS.
    Option 2: Only configure n2 for FDD and no requirement for TDD.
    Option 3: Configure n2 for FDD and n8 for TDD with note.
      Note: The intention of this configuration is to have two effective transmissions of the transport block. To achieve this for the standard TDD pattern captured in this table, a value of n8 is necessary, while for FDD a value of n2 is necessary.
Whether to clarify the safety statement
  Option 1: No need to specify any safety statements in specification
  Option 2: Yes
    Option 1a: Since the URLLC features of 5G NR will potentially be used in safety critical applications, the ultimately chosen statistical testing methodology for testing of these features must be verified by an independent body of experts/statisticians, before requirements and test can be used as basis for safety critical implementations. All statistical analysis and discussions provided in this meeting are to be taken as a best effort and is not to be taken as due diligence
    Option 1b: If the URLLC features of 5G NR would be used in safety or mission critical applications, the ultimately chosen statistical testing methodology for testing of these features must be verified by an independent body of experts/statisticians. It is also important to bear in mind that the demodulation requirements do not take account of all aspects of system operation (for example RF, transmitter, internal interfaces, higher layer protocol software etc.).

## Slide 5: PUSCH demodulation requirements for high reliability with higher BLER and/or confidence level:
Test applicability rule for FR1 and FR2 if BS declare to support both FR1 and FR2:
  Option 1: Tests shall be done for either FR1 or FR2
  Option 2: Tests shall be done for both , and only 1 SCS will be tested for each frequency band with test applicability rule.
  Option 3: Tests shall be done for both, all supported SCS will be tested for FR1 and only 1 SCS need to be tested for FR2.
SCS/BW for FR2 (only if FR2 is defined)
  60 KHz:
    Option 1: 50 MHz
    Option 2: 50 MHz and 100 MHz
  120 KHz
    Option 1: 100 MHz
    Option 2: 50 MHz and 100 MHz

## Slide 6: Simulation assumptions for PUSCH demodulation requirements for high reliability with higher BLER and/or confidence level for FR1
Parameter |  | Value
Frequency range |  | FR1
Transform precoding |  | Disabled
Antenna configuration |  | 1x2, ULA Low
PUSCH configuration | Mapping type | Type A and Type B
 | Starting symbol (S) | 0
 | Length (L) | 14
 | PUSCH aggregation factor | n2 for 30 kHz SCS FFS 15 kHz SCS
PUSCH DMRS configuration | DMRS Type | Type 1
 | DM-RS duration | Single-symbol DM-RS
 | Number of additional DMRS | 1
Propagation condition |  | TDLB100-400
MCS Table |  | Table 3, MCS 5
SCS and BW |  | 15 kHz for 5/10 MHz 30 kHz for 10/40 MHz
Frequency domain resource |  | Full Bandwidth
TDD pattern |  | 15 kHz SCS: 3D1S1U, S=10:2:2 30 kHz SCS: 7D1S2U, S=6:4:4
Maximum number of HARQ transmissions |  | 4
Testing metric |  | Target BLER: 10-2 (Calculate the target BLER after all transmission)

## Slide 7: PUSCH demodulation requirements for low latency
BS FR1 URLLC demodulation requirements for PUSCH mapping Type B
Agreements:
  Test metrics: 70% throughput
  SCS/CBW: 15 KHz for 5/10 MHz, 30 KHz for 10/40 MHz with test applicability rule.
  Whether to define requirements for FR2：Yes with test applicability rule.
      3a: The performance requirements are only applicable for BS only supporting FR2 or supporting both FR1 and FR2.
  Symbol length: 2os with higher [MCS10] from table 3.

## Slide 8: BS demodulation requirements for low latency
BS URLLC demodulation requirements for PUSCH mapping Type B
  Test applicability rule for FR1 and FR2 if BS declare to support both FR1 and FR2:
    Option 1: Tests shall be done for either FR1 or FR2
    Option 2: Tests shall be done for both , and only 1 SCS will be tested for each frequency band with test applicability rule.
    Option 3: Tests shall be done for both, all supported SCS will be tested for FR1 and only 1 SCS need to be tested for FR2.
  SCS/CBW for FR2 (only if FR2 is agreed)
    60 KHz:
      Option 1: 50 MHz
      Option 2: 50 MHz and 100 MHz
    120 KHz
      Option 1: 100 MHz
      Option 2: 50 MHz and 100 MHz

## Slide 9: Simulation assumptions for PUSCH demodulation requirements for mapping Type B for FR1
Parameter |  | Value
Frequency range |  | FR1
Transform precoding |  | Disabled
Antenna configuration |  | 1x2, ULA Low
PUSCH configuration | PUSCH mapping type | Type B
 | Start symbol | 0
 | Allocation length | 2
 | PUSCH aggregation factor | 1
PUSCH DMRS configuration | DMRS Type | Type 1
 | DM-RS duration | Single-symbol DM-RS
 | Number of additional DMRS | 0
SCS and BW |  | 15 kHz for 5/10 MHz 30 kHz for 10/40 MHz
TDD pattern |  | 15 kHz SCS: 3D1S1U, S=10:2:2 30 kHz SCS: 7D1S2U, S=6:4:4
MCS Table |  | Table 3, MCS 10
Propagation condition |  | TDLC300-100 Low
Maximum number of HARQ transmissions |  | 1
Frequency domain resource assignment |  | Full bandwidth For MCS5
Test metric |  | 70% TP

## Slide 10: PUSCH demodulation requirements test applicability and specification layout
Agreements:
  Introduce new sections within the existing PUSCH requirements for each separate feature when incorporate URLLC requirements into the specification.
  Test applicability rule for different URLLC features: The BS declares support of features listed below independently.
      The alternative 64QAM MCS table.
      PUSCH aggregation
      PUSCH mapping Type A and Type B (update the existing test applicability rule)
        The updated test applicability rule for PUSCH mapping type (considering only performance for low latency with Type B defined): Unless otherwise stated, PUSCH requirement tests shall apply only for the mapping type declared to be supported. If both mapping type A and type B are declared to be supported, the tests shall be done for either type A or type B.

## Slide 11: PUSCH demodulation requirements CR work split
Specifacation | Requirements title | CR Specifacation | Frequency range | CR work | CR Responsibility
BS demodulation (38.104/38.141-1/38.141-2) | FRC for all test cases | 38.104 | FR1 | FRC | Nokia
 |  |  | FR2 | FFS | FFS
 |  | 38.141-1 | FR1 | FRC | Ericsson
 |  | 38.141-2 | FR1 | FRC | Huawei, HiSilicon
 |  |  | FR2 | FFS | FFS
 | Test methodology | 38.104? | N/A | Test methodology | Nokia
 |  | 38.141-1 | N/A | Test methodology | Ericsson
 |  | 38.141-2 | N/A | Test methodology | Nokia/Huawei, HiSilicon
 | Test applicability for all test cases | 38.141-1 | FR1 | Test applicability | Huawei, HiSilicon
 |  | 38.141-2 | FR1 | Test applicability | Ericsson
 |  |  | FR2 | FFS | FFS
 | Requirements for PUSCH with ultra-low BLER target (10-5) | 38.104 | FR1 | Requirements | Nokia
 |  |  | FR2 | FFS | FFS
 |  | 38.141-1 | FR1 | Requirements/Measurement of Performance requirements Annex C.3 / Measurement system set-up Annex D | Ericsson
 |  | 38.141-2 | FR1 | Requirements / Measurement of Performance requirements Annex C.3 | Ericsson
 |  |  | FR2 | FFS | FFS
 | Requirements for PUSCH with aggregation factor configured | 38.104 | FR1 | Requirements | Huawei, HiSilicon
 |  |  | FR2 | FFS | FFS
 |  | 38.141-1 | FR1 | Requirements/Measurement of Performance requirements Annex C.3 / Measurement system set-up Annex D | Huawei, HiSilicon
 |  | 38.141-2 | FR1 | Requirements / Measurement of Performance requirements Annex C.3 | DoCoMo
 |  |  | FR2 | FFS | FFS
 | Requirements for PUSCH for mapping Type B with low number of symbols | 38.104 | FR1 | Requirements | Nokia
 |  |  | FR2 | FFS | FFS
 |  | 38.141-1 | FR1 | Requirements/Measurement of Performance requirements Annex C.3 / Measurement system set-up Annex D | Huawei, HiSilicon
 |  | 38.141-2 | FR1 | Requirements / Measurement of Performance requirements Annex C.3 | DoCoMo
 |  |  | FR2 | FFS | FFS