## Slide 1: WF on FR2 Beam Correspondence
Apple Inc.
R4-2011678
3GPP TSG-RAN WG4 Meeting #96-e
Online Meeting, Aug 2020
Agenda: 7.12.1.2

## Slide 2
As summarized in [1], there are three major topics under discussion:
  Topic #1 covers aspects related to beam correspondence based on SSB (including definition of the requirement and applicability rules).
  Topic #2 covers aspects related to beam correspondence based on CSI-RS (including definition of the requirement and applicability rules).
  Topic #3 covers aspects related to capability signaling, proposed TP to TR38.831, and proposed CRs to TS38.101-2.
Since some of the open issues can impact others and can be considered “core open issues,” it might be meaningful to try to prioritize the GTW discussion on these issues, which are listed in the following slides
Background
Notes: Ericsson: added text in blue

## Slide 3
Issue 1-1-1: Whether and how much performance relaxation, ∆p, relative to the condition which assumes both SSB and CSI-RS are present, is necessary
  Alt 1-1-1-1: ∆p = 0 dB (compared to R15 bit 1 or bit 0 UE?)
  Alt 1-1-1-2: 0 < ∆p ≤ 3 dB
  Alt 1-1-1-3: ∆p = 0 dB is optional to support, and 0 < ∆p ≤ 3 dB is the baseline to support
Agreements:
  Alt 1-1-1-1: ∆p = 0 dB, an optional capability
    If a R16 UE indicates it doesn’t support BC based on SSB, network can expect the UE to fulfill BC based on R15 BC requirements.
    R16 will continue to have bit 1 and bit 0 UEs
BC based on SSB – requirement definition
Notes: Ericsson: added text in blue

## Slide 4
Issue 2-1-1: The method to achieve CSI-RS based condition which will use SSB for P1 procedure
  Alt 2-1-1-1: SSB and CSI-RS are present, but SSB’s PSD is backed-off by X dB from CSI-RS
  Alt 2-1-1-2: decrease SSB power until UE SSB based SS-SINR measurement reporting is ≤ [-3] dB
  Alt 2-1-1-3: as proposed in R4-2010119 (Qualcomm)
  Alt 2-1-1-4: as proposed in R4-2010198 (Samsung)
  Alt 2-1-1-5: Update side conditions as proposed in R4-2011479 (Huawei) and take Alt 2-1-1-1
  Alt 2-1-1-6: Further study is needed
Agreements:
  Continue to focus on Alt 2-1-1-1 with all relevant details including the value of X and other P1 CSI-RS configurations to be worked out
BC based on CSI-RS – requirement definition
Notes: Ericsson: added text in blue

## Slide 5
Issue 3-1-1: How to introduce capability signaling for enhanced BC requirements
  Alt 3-1-1-1: A single unified capability for both BC based on SSB and BC based on CSI-RS (and introduce requirements for both)
  Alt 3-1-1-2: Separate capabilities for BC based on SSB and BC based on CSI-RS (and introduce requirements for both)
  Alt 3-1-1-3: A single capability only for BC based on SSB (and introduce requirements for BC based on SSB only)
Agreements:
  Alt 3-1-1-2: Separate capabilities for BC based on SSB and BC based on CSI-RS (and introduce requirements for both)
    R16 will continue to have bit 1 and bit 0 UEs for BC based on CSI-RS
    BC based on CSI-RS is optional
Capability aspects
Notes: Ericsson: added text in blue

## Slide 6
[1] | R4-2011549 | Email discussion summary for [96e][116] NR_RF_FR2_req_enh_Part_2 | Moderator(Apple Inc.)
References