## Slide 1: WF on NR SCC UL power drop behavior in FR2
Anritsu, []
R4-2011695
3GPP TSG-RAN WG4 Meeting #96-e
Online, 17th – 28th Aug 2020
Agenda: 4.2.2
E-mail title: [96e][103] NR_NewRAT_UE_RF_Part_2
Sub-topic: 2-1
WI: NR_newRAT-Core

## Slide 2: Background
By the report from [4], there is a case that an FR2 EN-DC UE stops transmitting NR SCC UL signals during the TRx measurement even though it is for a CA test and the DUT correctly followed a design with the current descriptions in TS 38.101-2 [1] and TS 38.213 [2]. Considering an objective of the CA test, it should be clarified if it is a correct behavior that the UE operates as a single carrier mode during the verification of CA performances.
Extract from TS 38.213 [2] clause 7.5
In case of same priority order and for operation with carrier aggregation, the UE prioritizes power allocation for transmissions on the primary cell of the MCG or the SCG over transmissions on a secondary cell. In case of same priority order and for operation with two UL carriers, the UE prioritizes power allocation for transmissions on the carrier where the UE is configured to transmit PUCCH. If PUCCH is not configured for any of the two UL carriers, the UE prioritizes power allocation for transmissions on the non-supplementary UL carrier.

## Slide 3: Outcome of the 1st round discussion
From the 1st round discussion summary [3], majority views in RAN4 are as follows.
- Current UE behavior (i.e. Prioritize PCC and drop the SCC UL power during the CA operation) is not infringing TS 38.213 [2].
RAN4 requirement of configured transmitted power for CA (TS 38.101-2 [1] clause 6.2A) is not mandating UE to transmit UL signals with an equal PSD.
⇒ There is a conflicting situation that the minimum requirement were derived based on the assumption of equal PSD as the worst case condition while the actual UE behavior is allowed to scale down the power of SCC during the maximum output power condition.

## Slide 4: Way forward
- Companies are encouraged to bring views regarding conditions which should be suggested to RAN5 to measure each CA test case.
Option 1: Equal PSD between CCs.
Option 2: Measure the UE as is even SCC output may be scaled down under CA mode.
Other options are not precluded.
Study of the methodologies to reproduce the conditions above is RAN5 work.

## Slide 5: Reference
[1] TS 38.101-2, “User Equipment (UE) radio transmission and reception; Part 2: Range 2 Standalone”, V16.4.0, 2020-06
[2] TS 38.213, “NR; Physical layer procedures for control”, 16.2.0, 2020-06
[3] R4-2011536, “Email discussion summary for [96e][103] NR_NewRAT_UE_RF_Part_2”, Moderator (Apple Inc.), RAN4 #96-e, Online-meeting
[4] R4-2009656, “NR SCC UL power drop behaviour with EN-DC UE in FR2”, Anritsu corp. RAN4 #96-e, Online meeting