## Slide 1: WF on A-MPR for NS_33
Agenda item: 7.3.1
Source: Huawei, HiSilicon…
3GPP TSG-RAN WG4 Meeting #96-e R4-2011703
Electronic Meeting, 17 August – 28 August, 2020

## Slide 2: Background
Referring to the WF [1], there are some remaining issues which are listed in slide 6 and 7 about PSFCH and S-SSB AMPR for NS_33 .
In this meeting, companies provide their contributions [2][3][4] to address these remaining issues.
There are options to specify the A-MPR for NS_33 for PSFCH/S-SSB for PC3 UE in the first round discussion.
  Option 1: A-MPR for NS_33 from QC (R4-2010028) are adopted and specified.
  Option 2: A-MPR for NS_33 from LGE (R4-2010135) are adopted and specified.
  Option 3: A-MPR for NS_33 from Huawei (R4-2010929) are adopted and specified.

## Slide 3: Reference
[1] R4-2009168 WF on remaining issues for TS38.101-1 and TS38.101-3 for NR V2X, LG Electronics, Huawei, HiSilicon, CATT
[2] R4-2010028 V2X A-MPR tables for SSSB, PFSCH, Qualcomm Incorporated
[3] R4-2010135 Remaining MPR/A-MPR requirements for NR V2X UE, LG Electronics France
[4] R4-2010929 Discussion on remaining AMPR requirements for PC3 V2X UE, Huawei, HiSilicon

## Slide 4: WF about A-MPR for simultaneous PSFCH by NS_33
Table 6.2E.3.1-3: A-MPR for simultaneous PSFCH by NS_33
Channel Bandwidth, MHz | Carrier Frequency (MHz) | RB allocation | PSFCH A-MPRbase (dB) |  |  | A-MPRstep (dB)
 |  |  | 0 ≤ NGap / NRB < 0.15 | 0.15≤ NGap / NRB < 0.3 | 0.3≤ NGap / NRB ≤ 1 | 
10 MHz | 5860 | 1 | 19 |  |  | 1
 |  | >1 | 22 |  |  | 1
 | 5870, 5880, 5890, 5900, 5910, 5920 | 1 | 5 |  |  | 0.8
 |  | >1 | 14 | 7 | 18.5 | 0.8
Note 1: NGap is the gap (in units of RBs) between RBstart and RBend for simultaneous PSFCH transmission with contiguous and non-contiguous RB allocation. (NGap = RBend - RBstart) |  |  |  |  |  | 

## Slide 5: WF about A-MPR for S-SSB transmission by NS_33
Table 6.2E.3.1-4: A-MPR for S-SSB transmission by NS_33
Carrier Frequency (MHz) | RBStart * 12*SCS [MHz] | A-MPRBase (dB) | AMPRStep (dB)
5860 | ≤1.0 | ≤ 25 | 0.6
 | >1.0 and ≤2.0 | ≤ 19 | 
 | >2.0 and ≤3.24 | ≤ 12 | 
 | >3.24 and ≤3.6 | ≤ 10 | 
 | >3.6 | ≤ 9 | 
5870, 5880, 5890, 5900, 5910, 5920 | ≤1.0 | ≤ 7 | 0.85
 | >1.0 and ≤1.6 | ≤ 6.5 | 
 | >1.6 and ≤2.6 | ≤ 5.8 | 
 | >2.6 and ≤3.24 | ≤ 4.5 | 
 | >3.24 and ≤4.32 | ≤ 5.5 | 
 | >4.32 | ≤ 6.5 |