## Slide 1: WF on A-MPR requirements for NS_52
Qualcomm, LG Electronics...
3GPP TSG-RAN WG4#96-e Meeting R4-2011704
Electronic Meeting, 17th August – 28th August, 2020

## Slide 2: Background
In this meeting, RAN4 discussed the NS_52 A-MPR requirements for PSSCH_PSCCH and PFSCH for NR V2X UE as follows.
Issue 1-1-2: A-MPR for NS_52 for PSSCH_PSCCH and PFSCH transmitted channel for PC3 UE
  To derive A-MPR requirements, the worst A-MPR values from interested companies are chosen.
Tentative agreement:
  NS_52(FCC) will be captured in TS38.101-1.
Recommendations for 2nd round:
  WF assigned to complete A-MPR for remaining NS_52 channels based on the tentative agreement. The detailed table format and A-MPR level will be proposed in WF.

## Slide 3: WF on PSSCH_PSCCH A-MPR for PC3 NR V2X UE at n47
For FCC regulation at 40MHz with NS_52
  Option 2
Carrier frequency(MHz) | Modulation | A-MPR(dB) |  | 
 |  | Region 1 | Region 2 | Region 3
5885 | QPSK | ≤ 13.5 | ≤ 8.0 | ≤ 5.5
 | 16QAM |  | ≤ 8.0 | ≤ 5.5
 | 64QAM |  | ≤ 8.5 | ≤ 5.5
 | 256QAM |  | ≤ 8.5 | ≤ 6.0

## Slide 4: Definition of regions for PSSCH_PSCCH NS_52 A-MPR
Option 2
Channel Bandwidth, MHz | Carrier frequency(MHz) | A-MPR parameters |  | A-MPR
 |  | RBstart or RBend | LCRB | 
40 | 5885 | RBstart≤floor(NRB*0.2) or RBend ≥NRB- floor(NRB*0.2) | LCRB ≤floor(NRB*0.2) | Region 1
 |  | The RB allocation is in Region 2 allocation for all other allocations which are not an Region1 or Region3 allocation. |  | Region 2
 |  | floor(NRB /3.5)≤ RBstart ≤NRB –floor(NRB /3.5) – LCRB | LCRB ≤ceil(NRB/3.5) | Region 3

## Slide 5: WF on PSFCH A-MPR for PC3 NR V2X UE at n47
For FCC regulation at 40MHz with NS_52
  For PSFCH all submissions have the same values given below
Channel Bandwidth [MHz] | Carrier frequency [MHz] | A-MPR (dB)
40 MHz | 5885 | ≤23.5

## Slide 6: Conclusion
Proposed WF is as follows:
  A-MPR for PSSCH_PSCCH  Select option 2
  Definition of regions for PSSCH_PSCCH  Select option2
  A-MPR for PSFCH  Select A-MPR table in slide 5

## Slide 7: References
# | TDoc | Title | Source | Type | Agenda item
1 | R4-2010135 | Remaining MPR/A-MPR requirements for NR V2X UE | LG Electronics France | other | 7.3.3.1
2 | R4-2010113 | TP on V2X A-MPR for SSSB, PFSCH, PSSCH, PSCCH | Qualcomm Incorporated | other | 7.3.3.1
3 | R4-2010929 | Discussion on remaining AMPR requirements for PC3 V2X UE | Huawei, HiSilicon | other | 7.3.3.1