## Slide 1: WF on NR V2X FRC parameters
Huawei, HiSilicon, LG Electronics
R4-2011709
3GPP TSG-RAN WG4 #96-e
Electronic Meeting, 17-28 Aug, 2020

## Slide 2: Background
All companies agree that necessary overhead should be considered for TBS determination in FRC table
Parameters without controversy are listed as below in 1st round discussion
  PSSCH symbol number in a slot
    12 OFDM symbols (excluding the first OFDM symbol in one SL slot used for AGC)
  PSCCH resource
    10 PRBs in frequency domain
    3 symbols in time domain
  DMRS
    Only one DMRS pattern is configure in SL resource pool
      2 DMRS symbols , i.e, symbol4 and symbol 10 (copy from 38.211 Table 8.4.1.1.2-1)
    FDMed with PSSCH within DMRS symbol
    Frequency density is ½
  Maximum number of HARQ transmissions
    1 (without re-transmission)

## Slide 3: Way forward
Other parameters as below should be considered in FRC table
Slot number in 10ms
Subcarriers per resource block
CRC
  TB-CRC
    Option 1: L=24
    Option 2: L =16 for TBS <3824, otherwise L=24
  Additional CRC sequence L=24 is attacked for each CB when CB number is larger than 1
X-overhead : 0
  PT-RS disable
  CRI-RS disable
PSFCH
  PSFCH period is 0
MCS
  QPSK: MCS 4
  64QAM: MCS 24
  256QAM: MCS 23
NR Band / SCS / Channel bandwidth / Duplex mode |  |  |  |  |  | 
V2X Band | SCS (kHz) | 10 MHz (dBm) | 20 MHz (dBm) | 30 MHz (dBm) | 40 MHz (dBm) | Duplex Mode
n38 | 15 | 50 | 105 | 160 | 216 | TDD
 | 30 | 24 | 50 | 75 | 105 | 
 | 60 | 10 | 24 | 36 | 50 | 
n47 | 15 | 50 | 105 | 160 | 216 | HD
 | 30 | 24 | 50 | 75 | 105 | 
 | 60 | 10 | 24 | 36 | 50 | 

## Slide 4: Way forward
Another parameter as below should be considered in FRC table
2nd stage SCI
  Option 1: Assume no 2nd stage SCI overhead
    Note: Simplify the test complexity, but not aligned with RAN1 specification.
  Option 2: assume 2nd stage SCI overhead existed
    Option 2-1: fixed to 240 REs for QPSK, 96 REs for 64QAM and 256QAM
      Note: Simplify the test complexity, but not aligned with RAN1 specification.
    Option 2-2:
      payload size of SCI 2-A is baseline (35bits SCI-2A + 24 CRC).
      Beta offset for 2nd stage SCI is 1.125 for QPSK
      Note 1: when beta offset for 2nd stage SCI is 1.125 and PSSCH MCS is 4, the actual code rate for 2nd stage SCI is 0.267, which will decrease the cover of 2nd stage SCI. the design of two stage SCI is to reduce the complexity of blind decoding, not for saving 2nd stage SCI overhead.
      Note 2: There is no beta offset configuration for 64QAM and 256 QAM.
    Option 2-3:
      payload size of SCI 2-A is baseline (35bits SCI-2A + 24 CRC)
      A beta offset of second stage SCI is selected to make sure that the code-rate of 2-A is approximate to SCI 1-A. A new row for beta offset and value should be added in FRC table.
      vacant resource elements value is determined based on NRB and DMRS frequency density, which is used to determine binary Channel Bits per Slot for PSSCH data mapping.
      Based on the principle of SCI2-A RE determination defined in 38.212
      Note: the overhead of 2nd stage SCI is aligned with RAN1 spec

## Slide 5: Way forward
FRC reference table (SCS 15 kHz and QPSK as example)
Transport block CRC:
Option 2: L =16 for TBS <3824, otherwise L=24
Beta offset for 2nd stage SCI:
    Option 2-3:
    payload size of SCI 2-A is baseline (35bits SCI-2A + 24 CRC)
    A beta offset of second stage SCI is selected to make sure that the code-rate of 2-A is approximate to SCI 1-A. A new row for beta offset value should be added in FRC table.
    Based on the principle of SCI2-A RE determination defined in 38.212
Fixed reference channel for V2X receiver requirements (SCS 15 kHz, QPSK)
Parameter | Unit | Value |  |  | 
Channel bandwidth | MHz | 10 | 20 | 30 | 40
Subcarrier spacing | kHz | 15 | 15 | 15 | 15
Allocated resource blocks |  | 50 | 105 | 160 | 216
MCS Table for TBS determination | QPSK |  |  |  | 
Modulation |  | QPSK | QPSK | QPSK | QPSK
MCS Index |  | 4 | 4 | 4 | 4
Transport Block Size | bits | - | - | - | -
Transport block CRC | Bits | option2 | option2 | option2 | option2
Number of Code Blocks per slot |  | 1 | 1 | 2 | 3
Beta offset for 2nd stage SCI |  | Option 2-3 | Option 2-3 | Option 2-3 | Option 2-3
γ value when 2nd stage SCI rate match |  | Option 2-3 | Option 2-3 | Option 2-3 | Option 2-3
Binary Channel Bits per subframe | Bits |  |  |  | 
Max. Throughput averaged over 1 period of 100ms | Mbps |  |  |  | 

## Slide 6
Reference
[1] R4-2010137, Correction on 5G V2X UE RF requirements for 5G V2X service in TS38.101-1 in rel-16, LG Electronics
[2] R4-2010015, V2X RX issues, Qualcomm Incorporated
[3] R4-2010822, On NR V2X reference measurement channels, Huawei, HiSilicon