## Slide 1: WF on BS impact of NR V2X
3GPP TSG-RAN WG4 Meeting #96-e
Electronic Meeting, 17th – 28th August, 2020
Agenda item: 7.3.2
Document for: Approval
R4-2011712
CATT, …

## Slide 2: Background
The BS impact of NR V2X was discussed for four RAN4 meetings with no agreement reached.
As per the WID on NR V2X [1] approved in RAN#87e, the impact on TS 38.104 has been added as indicated below.
In Rel-14, Band 47 is specified in the section of operating bands in both TS 36.101 and TS 36.104.
In current TS 38.104, the co-existence spurious emission requirement is only specified to protect UE Rx in Band 47 for LTE V2X without band n47 for NR V2X.
Impacted existing TS/TR {One line per specification. Create/delete lines as needed} |  |  | 
TS/TR No. | Description of change | Target completion plenary# | Remarks
… | … | … | …
38.101-1 | Introduction of NR V2X solutions | RAN#88 | Core part
38.101-2 | Introduction of NR V2X solutions | RAN#88 | Core part
38.101-3 | Introduction of NR V2X solutions | RAN#88 | Core part
38.101-4 | Introduction of NR V2X solutions | RAN#90 | Performance part
38.104 | Introduction of NR V2X bands | RAN#88 | Core part

## Slide 3: BS impact of NR V2X (1)
  Whether or not to specify the frequency band n47 for NR V2X in 38.104
  Option 1: To introduce the frequency band n47 for NR V2X in 38.104.
  Option 2: Do not introduce the frequency band n47 for NR V2X in 38.104.
    Note: Band 47 is introduced for LTE V2X in 36.104. It is not expected to keep it empty in 38.104
  Recommendations for 2nd round: Considering a majority of companies support option 1, the opponent is encouraged to provide technical argument to convince the proponent.

## Slide 4: BS impact of NR V2X (2)
  Whether or not to specify co-existence spurious emission requirement in 38.104 for the protection of V2X UE Rx in band n47.
  Option 1: To specify co-existence spurious emission requirement to protect V2X UE Rx in band 47.
  Option 2: Do not specify co-existence spurious emission requirement to protect V2X UE Rx in band 47.
    Note: The band 47 has been already protected by specifying co-existence spurious emission in 38.104. No new thing is added here if to protect band n47.
  Recommendations for 2nd round: Considering the majority of companies support option 1, the opponent is encouraged to provide technical argument to convince the proponent.

## Slide 5: BS impact of NR V2X (3)
  If no consensus reached in this meeting, what kind of procedure can be taken about this sub-topic?
  Option 1: Decide whether or not to introduce BS impact in RAN plenary.
  Option 2: No action.
    Note: The impact of NR V2X on TS 38.104 has been added in RAN#87e.
  Recommendations for 2nd round: Option 1 will be used based on the majority view.

## Slide 6: BS impact of NR V2X (4)
  How to deal with the corresponding parts in 36.104 and 38.104 if band n47 and co-existence spurious emission protection for band n47 is not agreed for NR V2X? Companies are encouraged to add potential options.

## Slide 7: Reference
[1] RP-200129, Revised WID on 5G V2X with NR sidelink, LG Electronics, RAN#87e
[2] R4-2011542, Email discussion summary for [96e][109] 5G_V2X_NRSL_SysParameters, vivo, RAN4#96e
[4] R4-1704054, CR on BS for protection of V2X UE in TS 36.104, Huawei, RAN4#82bis
[5] R4-2009827_On BS impact of NR V2X, CATT, RAN4#96-e
[6] R4-2009825, CR for TS38.104, Introduce BS impact of NR V2X, CATT, vivo, RAN4#96