## Slide 1: WF on NR-V2X switching period
3GPP TSG-RAN WG4 Meeting #96-e
Electronic Meeting, 17th – 28th August, 2020
Agenda item: 7.3.4.1
Document for: Approval
R4-2011714
CATT, …

## Slide 2: Background (1)
  The following scheduling restriction was agreed in RRM session as per 38.133:
  When switch from E-UTRA V2X sidelink to NR V2X sidelink occurs in NR slot ‘n’,
  - UE is not expected to transmit or receive on NR V2X sidelink on the slot ‘n’.
  When switch from NR V2X sidelink to E-UTRA V2X sidelink occurs in NR slot ‘n-1’,
  - UE is not expected to transmit or receive on NR V2X sidelink on the slot ‘n-1’.
  When switch from NR V2X sidelink to E-UTRA V2X sidelink occurs in E-UTRA subframe ‘n’,
  - UE is not expected to transmit or receive on E-UTRA V2X sidelink on the subframe ‘n’.
  When switch from E-UTRA V2X sidelink to NR V2X sidelink occurs in E-UTRA subframe ‘n-1’,
  - UE is not expected to transmit or receive E-UTRA on V2X sidelink on the subframe ‘n-1’.

## Slide 3: Background (2)
  The following options for switching period were discussed in the 1st round as per [1]:
  Option 1: Switching period is placed at NR slot and the guard symbol at LTE side can also be utilized
  Option 2: The whole switching time including switching period as well as transient periods shall be placed at the previous E-UTRA sub-frame or NR slot
  Option 3: Do not specify switching time RF requirement, use RRM requirement in 38.133 clause 12.9.1 to verify the LTE-NR Tx switching requirement.
  Option 4: LTE-NR Tx Switching time requirement is specified as a package in the following:
    Switching time requirement in RF spec (38.101) is 150us
    If UE supports this feature: “Support of fewer than 14 consecutive sidelink symbols in a slot”, the switching time requirement can be verified by configuring smaller number of consecutive symbols in a slot, and UE has to satisfy the 150us switching time requirement.
    If UE doesn’t support this feature: “Support of fewer than 14 consecutive sidelink symbols in a slot”, the switching time requirement is considered as satisfied when UE satisfied the corresponding scheduling restriction requirement in 38.133 clause 12.9.1.

## Slide 4: Switching period
  The candidate options for the 2nd round:
    Option 1: Switching period is placed at NR slot and the guard symbol at LTE side can also be utilized.
    Option 1a: The whole switching time including transient period should be placed at NR slot.
    Option 2: The whole switching time including switching period shall be placed at the previous E-UTRA sub-frame or NR slot.
    Option2a: Switching period is placed at the last slot/SF of the RAT UE switches from or placed at the first slot/SF of the RAT UE switches to. Choosing which RAT to place the switching period in is up to UE implementation [Qualcomm]
    Option 3: Do not specify switching time RF requirement, use RRM requirement in 38.133 clause 12.9.1 to verify the LTE-NR Tx switching requirement.
    Option 4: LTE-NR Tx Switching time requirement is specified as a package in the following:
      Switching time requirement in RF spec (38.101) is 150us
      If UE supports this feature: “Support of fewer than 14 consecutive sidelink symbols in a slot”, the switching time requirement can be verified by configuring smaller number of consecutive symbols in a slot, and UE has to satisfy the 150us switching time requirement.
      If UE doesn’t support this feature: “Support of fewer than 14 consecutive sidelink symbols in a slot”, the switching time requirement is considered as satisfied when UE satisfied the corresponding scheduling restriction requirement in 38.133 clause 12.9.1.
    Option 5: Option2a + Option 3 [Qualcomm]
    Note 1: Option 1a is revised based on option 1. As per the scheduling restriction agreed in RRM session, the cross-boundary switching time seems not a wise choice.
    Note 2: The switching time in RF session is seemingly not a crucial issue because the switching time 150us is much less than one NR slot / LTE subframe. The switching time in RF session can be considered as satisfied when the scheduling restriction in RRM session applies.
  Recommended WF for 2nd round: FFS
    Focus on the switching period position.
    Discuss whether the priority between LTE V2X and NR V2X exists.
    Decide the switching period position.
  Recommended WF for 2nd round : Option 5: Option2a (switching period position) + Option 3 (switching time) [Qualcomm]

## Slide 5: Reference
[1] R4-2011543, Email discussion summary for [96e][110] 5G_V2X_NRSL_UE_Concurrent, Huawei, RAN4#96e
[2] R4-2009829, Switching period for NR V2X in ITS band, CATT, RAN4#96e
[3] R4-2010138, Correction on NR V2X inter-band con-current UE RF requirements in TS38.101-3, LG Electronics, RAN4#96e
[4] R4-2010290, Further discussion on con-current operation for NR V2X, vivo, RAN4#96e
[5] R4-2010457, On switching period for NR V2X in ITS band, CATT, RAN4#96e
[6] R4-2010605, On remaining issue for con-current operation, Xiaomi, RAN4#96e
[7] R4-2010819, On switching period for LTE SL and NR SL, Huawei, HiSilicon, RAN4#96e
[8] R4-2010014, V2X TX Issues, Qualcomm, RAN4#96e