## Slide 1: WF on MPE enhancements
OPPO
3GPP TSG-RAN WG4 Meeting #96e R4-2011734
Electronic Meeting, August 17th – 28th, 2020

## Slide 2: PMPR reporting values
Issue 1-1: PMPR report bits
  Option 1: 2 bits (4 values)
  Option 2: 3-bits (8 values)
Agreement: Define PMPR reporting with 2 bits.
Issue 1-2: PMPR values if report with 2 bits
  Option 1: {3 ≤ P-MPR < 6, 6 ≤ P-MPR < 9, 9 ≤ P-MPR < 12, P-MPR ≥ 12}
Agreement: Define PMPR values {3 ≤ P-MPR < 6, 6 ≤ P-MPR < 9, 9 ≤ P-MPR < 12, P-MPR ≥ 12}

## Slide 3: Absolute PMPR trigger threshold
Issue 2-1: How many values are needed for absolute PMPR trigger threshold
  Option 1: 3 values, e.g. {1dB, 3dB, 6dB}
  Option 2: 4 values, e.g. {3dB, 6dB, 9dB, 12dB}
  Option 3: 8 values, e.g. {3dB, 6dB, 9dB, 12dB, 15dB, 18dB, 21dB, infinity}
Agreement:
{3dB, 6dB, 9dB, 12dB} is adopted as the absolute PMPR trigger threshold for “2-bits PMPR”.
Clarify to RAN2 that the absolute triggered threshold is optionally configured by NW.
If the field is absent, the absolute event-triggered PMPR reporting is not enabled by the network.
Issue 2-2: Whether 0dB absolute PMPR threshold shall also be defined
  Option 1: Yes
  Option 2: No
Agreement: 0dB absolute PMPR threshold is not defined.

## Slide 4: Relative PMPR trigger threshold
Issue 3-1: Whether to overturn the previous agreement “Relative PMPR threshold is introduced as an additional complimentary to the previously agreed absolute P-MPR threshold”
  Option 1: Yes, remove relative PMPR threshold
  Option 2: No, keep relative PMPR threshold
Agreement: Relative PMPR threshold is kept.
Issue 3-2: Relative PMPR threshold
  Option 1: {3dB, 6dB, 9dB, infinity}
  Option 2: {1, 3, 6, 9}dB, 12dB can also be considered
Agreement:
Define relative PMPR threshold as {1dB, 3dB, 6dB, infinity};
Clarify to RAN2 that the relative triggered threshold is optionally configured by NW.

## Slide 5: Relation between Absolute and Relative PMPR trigger threshold
Issue 4-1: Whether it is agreeable that “relative event-triggered reporting is only sent after the first P-MPR is reported based on absolute event-triggered reporting”
Agreement: It is agreed that “relative event-triggered reporting is only sent after the first P-MPR is reported based on absolute event-triggered reporting”.
Issue 4-2: Whether it is agreeable that “relative P-MPR triggered reporting has its own relative configurable threshold(s) and the first relative triggered report is compared to the absolute P-MPR triggered reporting and after that it can be compared to the previous relative P-MPR triggered report”
Agreement: It is agreed that “relative P-MPR triggered reporting has its own relative configurable threshold(s) and the first relative triggered report is compared to the absolute P-MPR triggered reporting and after that it can be compared to the previous relative P-MPR triggered report”.
Issue 4-3: Whether it is agreeable that “Separate relative configurable thresholds are defined for a case that needed P-MPR increases and needed P-MPR decreases”
No agreement.

## Slide 6: Absolute prohibit timer
Issue 5-1: Absolute prohibit timer values
  Option 1: {10, 20, 50, 100, 150, 200, 500, 1000} ms
  Other view
Agreement:
PMPR absolute prohibit timer values are defined as {sf0, sf10, sf20, sf50, sf100, sf200, sf500, sf1000}, i.e. same as PHR reporting prohibit timer.

## Slide 7: Relation between PMPR and PHR
Issue 6-1: Whether it is agreeable that “P-MPR value in the reporting needs to be consistent with PHR in the time domain”.
  Option A: Yes
  Other view
Agreement:
It is agreed that “P-MPR value in the reporting needs to be consistent with PHR in the time domain”.

## Slide 8: RAN4 spec changes
Issue 7-1: Whether it is needed to change 38.101-2 for PMPR reporting, and how to change 38.101-2 for PMPR reporting？
  Option 1: No need to change 38.101-2
  Option 2: Introduce requirements to TS38.101-2
  Option 3: Change 38.101-2 as below…
  Option 4: Change 38.101-2 as below…
Agreement:
It is agreed that Option 4 can be used as starting point for the changes to 38.101-2, and take following into account.
  Revise “for scheduling decisions” to “for network’s decision making”.
  Make it clear that P-MPR reporting is an optional feature and if UE supports this feature then PMPR will be reported when the trigger conditions are met.
It is RAN4 understanding that PMPR reporting should be per CC basis, i.e. UE will report PMPR at each affected UL carrier.