## Slide 1: WF on structure of NR CA reference sensitivity requirements in 38.101-1
Agenda item: 4.2.1
Source: Huawei, HiSilicon…
3GPP TSG-RAN WG4 Meeting #96-e R4-2011754
Electronic Meeting, 17 August – 28 August, 2020

## Slide 2: Background
In this meeting, RAN4 received the LS [2] on structure of NR CA reference sensitivity requirements in 38.101-1 from RAN5. Company provided their contribution and draft replied LS [1].
The actions are listed below in RAN5 LS:
  1. To inform if the requirement structure in clause 7.3A.4 listing only aggressor and victim will be retained in future.
  2. To consider the possibility of doing the same in 7.3A.5 and 7.3A.6.
  3. consider the possibility of moving (some of) the SDL requirements in 7.3A.2.4 to 7.3 so they can be treated as single carrier requirement.

## Slide 3: Reference
[1] R4-2010928 Discussion and reply draft LS on structure of NR CA reference sensitivity requirements in 38.101-1, Huawei, HiSilicon
[2] R5-202804 LS on structure of NR CA reference sensitivity requirements in 38.101-1, Ericsson
[3] R4-2001071 Discussion on improvement of Reference sensitivity exception table in 38.101-1 and 38.101-3, Huawei, HiSilicon

## Slide 4: WF on the structure of NR CA REFSENS
It’s agreed to inform RAN5 that the requirement structure in both clause 7.3A.4 and 7.3A.6 listing only aggressor and victim will be retained in future.
FFS whether Band combination specific manner will be used to specify IMD exception requirements in clause 7.3A.5 instead of NR CA configurations, referring to R4-2001072.
FFS whether to move (some of) the SDL requirements in 7.3A.2.4 to 7.3 and some clarification can be added into the specifications as below.
  The REFSENS requirements for SDL bands need to be tested with other bands under the inter-band CA configurations which UE supports.