## Slide 1: Way Forward on Rel-16 TxD
Samsung, …
3GPP TSG-RAN WG4 Meeting # 96-e
Electronic Meeting, 17 – 28 Aug, 2020
R4-2011768

## Slide 2: Summing the Powers and Emissions
RAN4 agree to define requirements for MOP and emission so that power is measured correctly for all implementations, including UE with transparent TxD:
  Use “requirements are defined as the sum of powers from both connectors”.
    This shall be interpreted as: Measure the power and emissions per connector and then sum them up afterwards.
    RAN4 will clean-up all requirements related to summing the powers and emissions, including UL MIMO, UL full power transmission requirement.

## Slide 3: EVM Requirement for Transparent TxD
Background:
  In RAN4#95e, RAN4 agree to define EVM for transparent TxD as:
RAN4 further study new test method and EVM definition proposed in R4-2011519:
  FFS whether or not to use new EVM definition to replace above definition.
RAN4 agree the location in Specification to capture EVM definition for transparent TxD, as
  Annex F

## Slide 4: Declaration for Default TX Connector
  RAN4 further study the following options for declaration of default Tx connector:
  Option 1a: TE needs to detect all antenna connectors for ACK and NACK and any other expected response from UE
  Option 1b: TE needs to detect all declared TX antenna connectors for ACK and NACK and any other expected response from UE
  Option 2: UE declares which connector is primary TX connector from which ACK and NACK and any other expected response from UE is transmitted in all cases
  Option 2a: Per instructed as test mode, UE should keep its default connector (based on UE declaration) unchanged from which ACK and NACK and any other expected response from UE is transmitted in all test cases
  Option 3: Regardless of the above options, it should be clarified only tested Tx connector is used as 1Tx transmission.

## Slide 5: UE Behavior under Conformance Testing
  RAN4 further study the following options for UE behavior under conformance testing:
  Option 1a: UE will keep the tx diversity status unchanged in conformance testing.
  Option 1b: Test mode signalling is implemented to instruct UE to keep TX div status unchanged
  Option 2: TE will detect and sum for every power step and change in condition from all connector

## Slide 6: Power Splitting Behavior
RAN4 agree UE behaviour for power splitting as:
  Option 1: Only allow equal power split between connectors
    Excludes 17+17+20 dBm implementations
    Excludes power control optimizations
  Option 1a: Per instructed as test mode, UE should keep equal power split between connectors in all cases.
  Option 2: Allow any power split between connectors

## Slide 7: MPR Requirement for Transparent TxD
RAN4 agree MPR defined for TxD is applied to the total output power rather than at each antenna connector

## Slide 8: Signaling for Transparent TxD
Whether and how RAN4 introduce signalling for transparent TxD:
  Option 1: Use ModifiedMPRbehavior bits to signal additional relaxations.
  Option 2: Introducing a new (capability) signalling for TxD
  Option 3: Introducing a new power class (e.g. PC2.5) for TxD
  Option 4: No need for TxD signalling

## Slide 9: Applicability of Transparent TxD Requirement
The applicability of the newly introduced test procedure (if any) and specific requirement (if any) for transparent TxD UE :
  FFS whether or not applicable to UE implementation without transparent TxD
  Whether or not a UE implementation use transparent TxD
    Follow capability signalled by UE if UE capability is introduced.
    Based on UE vendor declaration if UE capability is not introduced.
  If requirements are embedded in to general requirements or distinguished in to TxD dedicated requirements is FFS

## Slide 10: CDD-related Requirement
For transparent TxD UE, necessity of CDD related requirements, e.g. requirement on TAE+CDD, is need to be further studied:
  FFS the necessity of CDD related requirement, by considering:
    Factors to determine the value of CDD in UE implementation
    Testability
    Other factors are not excluded.