## Slide 1: WF on handling new channel BW’s for EN-DC and NR CA band combinations with MSD
Qualcomm, MediaTek, CHTTL, [ZTE], […]
­­­3GPP TSG-RAN WG4 Meeting #96-e R4-2011777
Electronic Meeting, 17th – 28th August 2020

## Slide 2: Background (1/2)
In TS38.101-1, new channel BWs were and continue to be added to various NR bands that could impact ENDC and NRCA requirements
  25M, 30M, 40M, 50M was added to n1 in release 16
  20M was added to n5 in release 16
  Impact of higher BWs already present in release 15, but not vetted correctly such as n40.
  35MHz for NR band n3, n7, n8, n25, n66, n71
  45MHz for NR band n3, n25, n66.
  90M, 100M BWs to be added for n40.
Stand alone REFSENS and AMPR requirements were derived and agreed for new Channel BWs in TS38.101-1.
However, new channel BWs can impact ENDC in TS38101-1 and NRCA REFSENS in TS38.101-1 due to TX distortion, even if UL configuration is restricted as described in detail in [1]
  Impacted Examples of ENDC combinations are DC_3_n1, DC_1_n40, DC_28_n5

## Slide 3: Background (2/2)
MSD values were derived highlighted below as follows for DC_1_n40 [2] and DC_3_n1 [3] using the conditions for UL configuration as described in Notes 1-3 in Table 7.3B.2.3.4-2 of TS38.101-3.
CIM3, CIM5 and Image become a factor for large BWs since the separation between the UL allocation and TXLO increases.
So, using the conditions of notes 1-3 will result in considerably large MSD values as highlighted below.
It was mentioned that Tables can get messy and confusing with the added notes
E-UTRA or NR Band / Channel bandwidth of the affected DL band / MSD |  |  |  |  |  |  |  |  |  |  |  |  |  | 
UL band | DL band | 5 MHz (dB) | 10 MHz (dB) | 15 MHz (dB) | 20 MHz (dB) | 25 MHz (dB) | 30 MHz (dB) | 40 MHz (dB) | 50 MHz (dB) | 60 MHz (dB) | 80 MHz (dB) | 90 MHz (dB) | 100 MHz (dB) | 
n13 | 3 | 3.0 | 2.3 | 2 | 1.8 |  |  |  |  |  |  |  |  | 
n13,5 | 3 | [4.5] | [4.1] | [3.9] | [3.8] |  |  |  |  |  |  |  |  | 
n13,6 | 3 | [16.9] | []16.0 | [14.3] | [13.2] |  |  |  |  |  |  |  |  | 
NOTE 3: These requirements apply when the uplink is active in Band n1, n84 and the separation between the lower edge of the uplink channel in Band n1, n84 and the upper edge of the downlink channel in Band 3 is < 60 MHz. For each channel bandwidth (≤20MHz) in Band 3, the requirement applies regardless of channel bandwidth in Band n1, n84. NOTE 5: Applicable only for n1 UL BW = 25, 30, 40MHz. NOTE 6: Applicable only for n1 UL BW = 50MHz. |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | E-UTRA or NR Band / Channel bandwidth of the affected DL band / MSD |  |  |  |  |  |  |  |  |  |  |  | 
UL band | DL band | 5 MHz (dB) | 10 MHz (dB) | 15 MHz (dB) | 20 MHz (dB) | 25 MHz (dB) | 30 MHz (dB) | 40 MHz (dB) | 50 MHz (dB) | 60 MHz (dB) | 80 MHz (dB) | 90 MHz (dB) | 100 MHz (dB)
n40 | 1 | 8.3 | 8.3 | 8.3 | 8.3 |  |  |  |  |  |  |  | 
n40 | 13 | [21.5] | [21.5] | [21.5] | [21.5] |  |  |  |  |  |  |  | 
NOTE 3: Applicable only for n40 UL BW = 80MHz. |  |  |  |  |  |  |  |  |  |  |  |  | 
E-UTRA or NR Band / SCS / Channel bandwidth of the affected DL band / UL RB allocation of the agressor band |  |  |  |  |  | 
UL band | DL band | SCS of UL band (kHz) | 5 MHz (LCRB) | 10 MHz (LCRB) | 15 MHz (LCRB) | 20 MHz (LCRB)
n403 | 1 | 30 |  | [50] | [50] | [50]
NOTE 3: Applicable only for n40 UL BW = 80MHz. |  |  |  |  |  | 
NOTE 1: The UL configuration applies regardless of the channel bandwidth of the UL band. UL resource blocks allocation in the table shall be further limited to that specified in Table 7.3.1-2 in TS 36.101 [4] or Table 7.3.2-3 in TS 38.101-1 [2]. NOTE 2: The UL resource blocks shall be located as close as possible to the downlink operating band but confined within the transmission bandwidth configuration for the channel bandwidth. NOTE 3: When the maximum UL RB allocation “LCRB” value is less than the maximum transmission bandwidth configuration “NRB” defined in Table 5.3.2-1 in 38.101-1 [2] for the specified UL band SCS, the UL band should be configured using the lowest CBW that is compatible with the maximum specified LCRB value.

## Slide 4: WF
Consider options on how to handle the larger BWs on the aggressor band for the requirement of cross band isolation:
Option 1:
  Consider limited ULBWs of the aggressor band for ENDC combinations with the existing when specifying cross band noise MSD.
    Currently all BWs in each RAT are fair game.
  Possibly introducing a separate table in 38.101-3 for supported ULBWs for ENDC and NRCA combinations.
  Operator still may deploy the larger BW, but UE should not be forced to meet the ENDC/NRCA REFSENS requirement
Option 2:
  Introduce a separate table to List the ULBW and the corresponding UL configuration (allocation and location) per ENDC band combination.
  Consider adjusting the UL RB allocation and location for the larger UL channel BW of the aggressor band in the channel BW to avoid TX image, CIM3 and CIM5 to keep MSD no larger than the existing MSD for the smaller channel BWs.
Option 3:
  Consider the worst case MSD with the corresponding UL RB allocation and location for the larger UL channel BW of the aggressor band, taking TX image, CIM3 and CIM5 into account
Option 4:
  Other options not precluded.
Companies are encouraged to investigate and propose best solution by introducing CR in RAN4#97-e.

## Slide 5: References
R4-2009628, “ENDC crossband noise impact with large NR BW”, RAN4#96-e, Qualcomm Inc. August 2020
R4-2009623, “CR for missing DC_1A_n40A Cross Band Noise MSD for large NR UL BW in 38.101-3”, RAN4#96-e, Qualcomm, August 2020.
R4-2009620, “CR for missing DC_3A_n1A Cross Band Noise MSD for large NR UL BW in 38.101-3”, RAN4#96-e, Qualcomm, August 2020.