## Slide 1: WF on UE RF requirement (for 35 and 45 MHz channel bandwidths)
Skyworks Solutions Inc., ZTE, Huawei, [Qualcomm]
3GPP TSG-RAN WG4 Meeting #96-e R4-2011793 e-Meeting, August 17-28 2020

## Slide 2: Background
New channel bandwidths per band:
  35MHz for NR band n3, n7, n8, n25, n66, n71
  45MHz for NR band n3, n25, n66.
Contributions [1], [2], [3] describe specifications and the different areas impacted by the introduction of 35MHz and 45MHz channel bandwidths
These contribution also discuss specific band aspect that require an update of the requirement, including those that can be scaled according to BW and proposed SU
Finally [3] discusses the possibility of scaling the REFSENS with bandwidth per bands.

## Slide 3: Background on impact on General requirement
6.3.2 Transmit OFF power (related to measurement BW)
6.5.1 Occupied bandwidth (related to Channel BW)
6.5.2.2 Spectrum emission mask (related to Channel BW)
6.5.2.4 Adjacent channel leakage ratio (related to measurement BW)
7.4 Maximum input level (related to Channel BW)
7.5 Adjacent channel selectivity(related to Channel BW)
7.6 Blocking characteristics (related to Channel BW)
7.7 Spurious response (related to Channel BW)
7.8 Intermodulation characteristics (related to Channel BW)

## Slide 4: Background on SU and WF
Background: The table below represents SU proposed for second round:
  Since there is already agreement on 15kHz case (green underline), all measurement BWs for UL requirements can be derived
  Only REFSENS cannot be scaled for the cases where formal agreement is not reached yet
SCS [kHz] | 35 MHz | 45 MHz
 | NRB | NRB
15 | [188] | [243]
30 | [ 92] | [119]
60 | [44] | [58]
WF on measurement BW for ACLR minimum output power and transmit OFF power
Channel bandwidth (MHz) | Minimum output power (dBm) | Measurement bandwidth (MHz)
30 | -38.2 | 28.815
35 | -37.5 | 33.855
40 | -37 | 38.895
45 | -36.5 | 43.755
50 | -36 | 48.615

## Slide 5: WF on SEM
Spectrum emission limit (dBm) / Channel bandwidth |  |  |  |  |  |  |  |  | 
ΔfOOB (MHz) | 5 MHz | ... | 30 MHz | 35 MHz | 40 MHz | 45 MHz | 50 MHz | ... | Measurement bandwidth
± 0-1 | -13 | ... | -13 | -13 | -13 | -13 |  | ... | 1 % channel bandwidth
± 0-1 |  |  |  |  |  |  | -24 | -24 | 30 kHz
± 1-5 | -10 | -10 | -10 | -10 | -10 | -10 | -10 | -10 | 1 MHz
± 5-6 | -13 | ... | -13 | -13 | -13 | -13 | -13 | ... | 
± 6-10 | -25 |  |  |  |  |  |  |  | 
± 10-15 |  |  |  |  |  |  |  |  | 
± 15-20 |  |  |  |  |  |  |  |  | 
± 20-25 |  |  |  |  |  |  |  |  | 
± 25-30 |  |  |  |  |  |  |  |  | 
± 30-35 |  |  | -25 |  |  |  |  |  | 
± 35-40 |  |  |  | -25 |  |  |  |  | 
± 40-45 |  |  |  |  | -25 |  |  |  | 
± 45-50 |  |  |  |  |  | -25 |  |  | 
± 50-55 |  |  |  |  |  |  | -25 |  | 
± 55-60 |  |  |  |  |  |  |  |  | 
± 60-65 |  |  |  |  |  |  |  |  | 
± 65-70 |  |  |  |  |  |  |  |  | 
± 70-75 |  |  |  |  |  |  |  |  | 
± 75-80 |  |  |  |  |  |  |  |  | 
± 80-85 |  |  |  |  |  |  |  |  | 
± 85-90 |  |  |  |  |  |  |  |  | 
± 90-95 |  |  |  |  |  |  |  |  | 
± 95-100 |  |  |  |  |  |  |  |  | 
± 100-105 |  |  |  |  |  |  |  |  | 
The table on the right shows the required addition to the SEM requirement to enable 35 MHz and 45MHZ channel BW (red)
Given the large size of the table and the potential addition of other channel bandwidths it is FFS if the requirement is captured in the same table or another table or split is needed

## Slide 6: WF on ACS
The tables on the right shows the required addition to the ACS requirement to enable 35 MHz and 45MHZ channel BW (red)
Given the large size of the tables and the potential addition of other channel bandwidths it is FFS if the requirement is captured in the same tables or other tables are needed
RX parameter | Units | Channel bandwidth |  |  |  | 
 |  | 30 MHz | 35 MHz | 40 MHz | 45 MHz | 50 MHz
ACS | dB | 25.5 | 24.5 | 24 | 23.5 | 23
RX parameter | Units | Channel bandwidth |  |  |  | 
 |  | 30 MHz | 35 MHz | 40 MHz | 45 MHz | 50 MHz
Power in transmission bandwidth configuration | dBm | REFSENS + 14 dB |  |  |  | 
Pinterferer | dBm | REFSENS + 38 dB | REFSENS + 37 dB | REFSENS + 36.5 dB | REFSENS + 36 dB | REFSENS + 35.5 dB
BWinterferer | MHz | 5 | 5 | 5 | 5 | 5
Finterferer (offset) | MHz | 17.5 / -17.5 | 20 / -20 | 22.5 / -22.5 | 25 / -25 | 27.5 / -27.5
RX parameter | Units | Channel bandwidth |  |  |  | 
 |  | 30 MHz | 35MHz | 40 MHz | 45 MHz | 50 MHz
Power in transmission bandwidth configuration | dBm | -49 | -48 | -47 | -47 | -46.5
Pinterferer | dBm | -25 |  |  |  | 
BWinterferer | MHz | 5 | 5 | 5 | 5 | 5
Finterferer (offset) | MHz | 17.5 / -17.5 | 20 / -20 | 22.5 / -22.5 | 25 / -25 | 27.5 / -27.5
ACS values
Pinterferer & Finterferer (offset) (Case 1)
Pinterferer & Finterferer (offset) (Case 2)

## Slide 7: WF on Blocking
The tables on the right shows the required addition to the blocking requirement to enable 35 MHz and 45MHZ channel BW (red)
Given the large size of the tables and the potential addition of other channel bandwidths it is FFS if the requirement is captured in the same tables or other tables are needed
RX parameter | Units | Channel bandwidth |  |  |  | 
 |  | 30 MHz | 35 MHz | 40 MHz | 45 MHz | 50 MHz
Power in transmission bandwidth configuration | dBm | REFSENS + channel bandwidth specific value below |  |  |  | 
 | dB | 11 | 11.5 | 12 | 12.5 | 13
Table 6. In-band blocking/out-of-band blocking
Table 7. Narrowband blocking
Parameter | Unit | 30 MHz | 35 MHz | 40 MHz | 45 MHz | 50 MHz
Pw | dBm | PREFSENS + channel-bandwidth specific value below |  |  |  | 
 |  | 16 | 16 | 16 | 16 | 16
Puw (CW) | dBm | -55 | -55 | -55 | -55 | -55
Fuw (offset SCS= 15 kHz) | MHz | 15.6075 | 18.0825 | 20.5575 | 23.1375 | 25.7025
Fuw (offset SCS= 30 kHz) | MHz | NA | NA | NA | NA | NA

## Slide 8: WF on Spurious response and Intermodulation
The tables on the right shows the required addition to the Spurious response and Intermodulation requirements to enable 35 MHz and 45MHz channel BW (red)
Given the large size of the tables and the potential addition of other channel bandwidths it is FFS if the requirement is captured in the same tables or other tables are needed
RX parameter | Units | Channel bandwidth |  |  |  | 
 |  | 30 MHz | 35 MHz | 40 MHz | 45 MHz | 50 MHz
Power in transmission bandwidth configuration | dBm | REFSENS + channel bandwidth specific value below |  |  |  | 
 | dB | 11 | 11.5 | 12 | 12.5 | 13
Table 8. Spurious response
Table 9. Intermodulation
RX parameter | Units | Channel bandwidth |  |  |  | 
 |  | 30 MHz | 35 MHz | 40 MHz | 45 MHz | 50 MHz
Pw in Transmission Bandwidth Configuration, per CC | dBm | REFSENS + channel bandwidth specific value below |  |  |  | 
 |  | 11 | 11.5 | 12 | 12.5 | 13

## Slide 9: Impact on band specific requirement (background)
Band | Channel Bandwidth [MHz] | REFSENS (UL configuration, scalability with BW/MSD) | MPR(relative bandwidth criteria) | A-MPR study and requirement
n3 | 35 | UL configuration, not scalable with BW/MSD, | Relative channel bandwidth=2 %, OK | No A-MPR requirement will be specified, same as the case for 40 MHz CBW
 | 45 | UL configuration, not scalable with BW/MSD | Relative channel bandwidth=2.6 %, OK | 
n7 | 35 | UL configuration, Scales with BW/no MSD | Relative channel bandwidth=1.4 %, OK | A-MPR for NS_46 need to be studied, study for 40/50MHz can be reused
n8 | 35 | UL configuration, not scalable with BW/MSD | Relative channel bandwidth=3.9 %, not OK | A-MPR for NS_43 and NS_43U is for Japan only for B18,19 support BW is limited to 15MHz
n25 | 35 | UL configuration, not scalable with BW/MSD | Relative channel bandwidth=1.9 %, OK | A-MPR for NS_03 and NS_03U need to be studied, Mask missing for 35 MHz and 45MHz
 | 45 | UL configuration, not scalable with BW/MSD | Relative channel bandwidth=2.4 %, OK | 
n66 | 35 | Scales with BW/No MSD | Relative channel bandwidth=2 %, OK | A-MPR for NS_03 and NS_03U need to be studied, Mask missing for 35 MHz and 45MHz
 | 45 | UL configuration, Scales with BW/no MSD | Relative channel bandwidth=2.6 %, OK | 
n71 | 35 | UL configuration, not scalable with BW/MSD | Relative channel bandwidth=5.1 %, not OK | A-MPR for NS_35 need to be studied, Mask missing for 35 MHz and 45MHz
Note on relative BW criteria: although the relative BW criteria is not met for 35MHz for band n8 and n71, this channel bandwidth corresponds to the entire band thus the duplex filter may play a role.
Still it is to be noted that there can still be issues for SEM for small ΔfOOB
Also there would be issues if channel BW between 20 and 35MHz would be introduced
Note on NS43/43U: Since this is used in Japan for B18/19 support and that operator spectrum is limited to 15MHz, it is not necessary to study AMPR for 35MHz, even B18+B19 is limited to 30MHz

## Slide 10: WF on band specific requirement
REFSENS: Once 35MHz and 45 MHz SU is agreed for all SCS:
  REFSENS can derived directly from BW scaling for band n7 and 66
  For n66 UL configuration since the duplex is large, it uses full DFT-s-OFDM allocation like for other channel bandwidths:
  For n7 UL configuration since it is constant for BW >30MHz it uses:
    45RB at 15kHz, 20RB at 30kHz and 10RB at 60kHz SCS
  For n3, n8, n25 and n71 de-sense for new channel bandwidths should be studied
A-MPR:
  A-MPR should be studied for n7, n25, n66, n71
  Masks should be defined for the new channel bandwidths for n25, n66 and n71
Support of new channel BW in DC and CA combinations:
  Companies are encouraged to provide their view on how release independence can work: new BCS, release independence from r17…and how this aligns with new channel BW release independence support for the bands.

## Slide 11: References
[1] R4-2010636 Discussion on UE RF requirement for new channel bandwidth of 35MHz and 45MHz, ZTE Corporation
[2] R4-2010504 Overview on introduction of channel bandwidths 35MHz and 45MHz for UE, Huawei, HiSilicon
[3] R4-2010241 UE Requirements for 35MHz and 45MHz channels in FR1, Skyworks Solutions Inc.