## Slide 1: WF on new band combinations for V2X con-current operation
3GPP TSG-RAN WG4 Meeting #96-e
Electronic Meeting, 17th – 28th August, 2020
Agenda item: 10.19
Document for: Approval
R4-2011794
CATT, …

## Slide 2: Background
In RAN#88e meeting, the WI, band combinations for con-current operation of NR/LTE Uu bands/band combinations and one NR/LTE V2X PC5 band, was approved.
In the 1st round, the following issues are discussed as per [2]:
  UE RF architecture
  Filter performance for band n47/47
  IMD falling into band 47/n47
  ΔTIB,c and ΔRIB,c for band 47/n47

## Slide 3: Agreement
Regarding the IMD falling into band 47/n47, the following agreement is made in the 1st round:
Issue 1-3-1: IMD falling into band 47/n47
  No need to consider IMD problem falling into band 47/n47 due to the half-duplex mode.

## Slide 4: UE RF architecture
  Shared antenna architecture or separate antenna architecture
  Option 1: Consider both shared antenna architecture and separate antenna architecture.
  Option 2: Decide the antenna architecture based on the specific band combination.
  Recommendations WF for 2nd round: Decide whether antenna architecture can be specified based on the specific band combination.

## Slide 5: Filter performance
  Filter performance for band n47/47
  Option 1: Use the IL and attenuation values of filter for band 47/n47 proposed in R4-2010931.
  Option 2: Other option is not precluded.
  Recommendations WF for 2nd round: Need further discussion based on more inputs from companies.

## Slide 6: ΔTIB,c and ΔRIB,c
  ΔTIB,c and ΔRIB,c for band 47/n47
  Option 1: RAN4 need to evaluate ΔTIB,c and ΔRIB,c for band 47/n47, e.g. reuse the value of band n79 (ΔTIB,c = 0.8, ΔRIB,c = 0.5)
  Option 2: Decide after the RF architecture is clear.
  Recommendations WF for 2nd round: First to decide the specific RF architecture. Then focus on whether the existing values of band n79 can be reused based on the specified RF architecture and hopefully explore the potential reasons.

## Slide 7: Reference
[1] R4-2009832, Revised basket WID for V2X band combination, CATT, RAN4#96e
[2] R4-2011564, Email discussion summary for [96e][131] NR_LTE_V2X_PC5_combos, Moderator (CATT), RAN4#96e
[3] R4-2010931, General discussion about Rel-17 band combinations for Uu and V2X con-current operation., Huawei, RAN4#96e