## Slide 1: WF on UE RF requirement for 47 GHz band
Qualcomm Incorporated
3GPP TSG-RAN WG4 Meeting # 96-e R4-2011818
Online Meeting, Aug 2020

## Slide 2: Background
Initial discussions in RAN4 are captured in R4-2011568
Topics covered by this WF are:
 | Status summary
Sub-topic#4-1 Coex sim | It looks now only one company is supporting a new coexistence simulation with the updated BS parameters. Following the majority view, is it acceptable to conclude ACLR/ACS in the previous agreement (LS to WP5D) unless further justification to update BS parameters is provided? In other word, can we agree that ACLR is 16 dB and ACS is 22 dB for n262?
Sub-topic#4-2 Max power | .(EIRP EIS, spherical coverage and MBR not handled in this WF) MPR: Majority view is that existing MPR can be reused. One company commented it needs further study. Further analysis is encouraged for the next meeting.
Sub-topic#4-3 NS and A-MPR | Tentative agreements: A-MPR study is not needed until specific regulatory requirement is identified.
Sub-topic#4-4 Other Tx | Huawei proposes to study min output power for n262. To be further discussed. No other Tx requirement has so far been found band specific to n262.
Sub-topic#4-6 Other Rx | No objection to reuse existing IBB requirement is made. No other Rx requirement has so far been found band specific to n262. Tentative agreements: IBB requirement is reused from n259/n260.
Sub-topic#4-7 BC | Many UE vendors propose that BC tolerance should be studied for n262. Further analysis is encouraged for the next meeting. Also See #4-2.
Sub-topic#4-9 CA | Further checking is needed. It is possible that UL CA is discussed later if some issues are identified.
Sub-topic#4-10 UL MIMO | Further checking is needed.

## Slide 3: WF - 1
Co-ex requirements for 47 GHz band can be extended from study results for n260
  ACLR is 16 dB (6.5.2.3)
  ACS and IBB interferers are +22 dB relative to wanted signal (7.5 and 7.6)
  Co-ex emissions requirements in other bands are FFS (6.5.3.1)
  NS definition and AMPR study shall be motivated by regulatory requirement identified in contributions
Companies are encouraged to bring analysis and proposals for:
  PC3 UEs: DEIRP analysis corresponding to beamCorrespondenceWithoutUL-BeamSweeping = 0 in table 6.6.4.2-1

## Slide 4: WF - 2
MPR values might be revisited if motivated by considerations specific to 47GHz
Companies are encouraged to share views on the following items:
  min. output power requirement
  UL CA requirements
  UL MIMO requirements
  Intra-band CA configurations (both uplink and downlink, such as bandwidth class, bandwidth combination sets).