## Slide 1: WF on UE related work for n24
Ligado Networks
3GPP TSG-RAN4 Meeting #96-e R4-2011820
Online, , 17th - 28th Aug 2020

## Slide 2: Background and WF Discussion for Round 2
For NR band n24 UE specifications, Option 1 of the proposals for sub-topics 5-1, 5-2 and 5-3 were agreed to during Round 1 discussions for n24 (R4-2011569).
Agreements were to be captured in the WF document
Additionally, based on the comments, moderator recommended adding the following as part of the agreement for sub-topic 5-3:
  Companies are encouraged to submit and finalize PA and filter parameters at the next meeting.

## Slide 3: Agreements reached in RAN4 #96-e meeting
Agreement on the system parameters for operating band, channel bandwidth, NR-ARFCN ranges and the synchronization raster ranges that were proposed in R4-2010721
Agreement on specifying two Tx-Rx spacings of -101.5 MHz and -120.5 MHz
Given the timeline of the WI, it was agreed that the development of specifications related to linear ramp between 1627.5 – 1632.5 MHz is unnecessary and not required
Agree to finalize simulation assumptions for PA and filter at the next meeting. Companies are encouraged to submit and finalize PA and filter parameters at the next meeting.