## Slide 1: WF on numerologies for FS_NR_52_to_71GHz
Intel, …
R4-200XXXX
3GPP TSG-RAN WG4 #96-e
August 17th – 28th, 2020
Electronic meeting

## Slide 2
Channel Bandwidth – Background
The following inputs were collected for minimum CBW (single carrier)
  50 MHz: 2 companies
  500 – 800 MHz: 3 companies
The following were collected for maximum CBW (single carrier)
  400 MHz: 1 company
  400 – 800 MHz: 1 company
  400 – 2000 MHz: 1 company
  400 – 2160 MHz: 1 company
  1600 MHz: 1 company
  2000 MHz: 4 companies
Channel BW decision depends on SCS
  Currently RAN1 is evaluating system performances with different SCS

## Slide 3
Sub-Carrier Spacing – Background
While some companies do not want to rush and decide SCS in this meeting, the following SCS inputs were collected.
  60 kHz: 1 company
  120 kHz: 6 companies
  240 kHz: 7 companies
  480 kHz: 6 companies
  960 kHz: 6 companies
Other WG situation
  RAN1 is currently evaluating possible SCS as a part of system design and asked RAN4 to provide updated information of phase noise model in 52.6 – 71 GHz.
  SCS is a key system parameter and tightly related to system features

## Slide 4
WF on Channel Bandwidth and Sub-Carrier Spacing
Channel Bandwidth
  Maximum channel bandwidth is in [400 – 2160] MHz
    RAN4 continues to discuss about a maximum channel bandwidth.
  Minimum channel bandwidth is in [50 – 800] MHz.
    Companies are encouraged to provide input in the next meeting.
Sub-Carrier Spacing
  Further evaluation on feasibility of SCS from 120 kHz to 960 kHz in the next meeting.
    Companies are encouraged to evaluate feasibility from RAN4 perspective, i.e.,
      EVM
      Timing requirement
      Etc.
  FFS on 1920 kHz

## Slide 5
References
[1] R4-2009758 On numerology and channel bandwidth in 52.6 - 71 GHz, Intel Corporation
[2] R4-2009798 Discussion on numerology and CBW for above 52.6 GHz, CATT
[3] R4-2009945 Initial considerations on the numerology and channel bandwidth sizes for 60GHz frequency range, Apple Inc.
[4] R4-2010109 Numerology and channel BW on supporting NR from 52.6GHz to 71GHz, CMCC
[5] R4-2010176 On 52.6 to 71 GHz phase noise characteristics and draft LS to RAN1. Ericsson
[6] R4-2010291 Discussion on system parameters for B52.6G, vivo
[7] R4-2010500 Discussion on numerology and channel bandwidth for 52.6 GHz to 71 GHz, Huawei, HiSilicon
[8] R4-2010726 Applicable numerologies and channelization options for above 52.6 GHz, Nokia, Nokia Shanghai Bell
[9] R4-2010946 Discussion on system parameters for 52.6GHz-71GHz, ZTE Corporation
[10] R4-2011440 Numerology considerations for beyond 52GHz, FUTUREWEI
[11] R4-20xxxxx [96e][140] FS_NR_52_to_71GHz Draft summary after 1st round, Qualcomm (Moderator)