## Slide 1: WF on only single switched UL
Agenda item: 7.5.2
Source: Huawei, HiSilicon
3GPP TSG-RAN WG4 Meeting #96-e R4-2011934
Electronic Meeting, 17 August – 28 August, 2020

## Slide 2: Background on “only single switched UL”
Currently, there is no capability to indicate “only single switched UL”.
In Rel-15, for DC_3A_n3A intra-band non-contiguous EN-DC combination, only single switched UL is supported.
In Rel-16, only single switched UL is supported by some ENDC band combinations, such as DC_2A_n2A, DC_5A_n5A, DC_7A_n7A, DC_48A_n48A, DC_66A_n66A, DC_(n)5AA, DC_(n)12AA, DC_(n)38AA, DC_(n)48AA and DC_12A_n71A.
It can be foreseen that more and more ENDC band combinations have to be operated with only single switched UL in the future.
There is no clear definition about “only single switched UL” in current specifications.

## Slide 3: Agreement on only single switched UL
  Network behaviours: There is no restriction on NW’s behavior for only single switched UL operation.
  UE behaviours:
    Indicates whether the UE supports the tdm-PatternConfig for single UL-transmission associated functionality, as specified in TS 36.331
    UE expect to be scheduled with single switched UL and TDM pattern by Network.
    However, UEs which can’t support dual Transmission can drop NR transmission when LTE and NR transmissions collide.
  Solution: The existing capability “singleUL-Transmission” can be reused for these EN-DC band combinations for which only single switched UL is supported.

## Slide 4: Reference
[1] R4-2011719, Clarification on the network and UE behaviors between “Only single switched UL” and “SUO/SUO allowed”, Huawei, HiSilicon