## Slide 1: WF on NR-U RRM (Part 3) Agreements and topics discussed in email thread: [96e][208] NR_unlic_RRM_3
Nokia, Nokia Shanghai Bell
3GPP TSG-RAN WG4 Meeting #96-e R4-2012092
Electronic Meeting, August 17 – August 28, 2020
Agenda Items: 7.1.5.10, 7.1.5.11 and 7.1.5.13

## Slide 2
Agreements in the 1st round
Agreements in the GTW session
Agreements in the 2nd round
Still open for discussion

## Slide 3: Topic #1: Remaining issues in intra and inter-frequency measurements
Issue 1-1-1: Monitoring of QCL beams during cell detection in NR-U
RRM core requirements are defined under assumption what UE monitors the first 2 successive QCL’ed candidate SSB positions (i.e. N1 = N2 = 2)
  FFS if same values apply for cell detection
    Option 1: For cell detection the requirements are defined under assumption that UE monitors at least 1 candidate SSB position in one SSB block burst
    Option 2: Same value applies as for other RRM measurements
The total number of candidate SSBs indexes and number of cell UE shall monitor remains unchanged

## Slide 4: Topic #1: Remaining issues in intra and inter-frequency measurements
Issue 1-1-2: Monitoring of QCL beams during measurements in NR-U
In NR-U work, RAN4 assumes that no explicit or signalled UE capabilities will be defined for the number of candidate SS/PBCH block indexes corresponding to the same SS/PBCH block index the UE should monitor in a given discovery burst transmission window (for RRM) or within the set of configured resources (for RLM/CBD/BFD).
Agreements
• No differentiation between UE in FBE and LBE modes in NR-U RRM Core requirements.
• Different test case will be defined for UE in FBE and LBE modes in NR-U RRM Performance requirements.
Agreements
• RRM core requirements are defined under assumption what UE monitors the first 2 successive QCL’ed candidate SSB positions (i.e. N1 = N2 = 2)
o The total number of candidate SSBs indexes and number of cell UE shall monitor remains unchanged

## Slide 5: Topic #1: Remaining issues in intra and inter-frequency measurements
Issue 1-2-1: UE behavior in RRC_CONNECTED mode when serving cell is unavailable for consecutive SSB bursts
Do not specify additional UE behavior in RRC_CONNECTED mode when serving cell is unavailable for consecutive SSB bursts

## Slide 6: Topic #1: Remaining issues in intra and inter-frequency measurements
Issue 1-3-1: UE behaviour in case of successively exceeding the maximum number of DL LBT failure during measurements
After N unsuccessful measurement attempts of an already identified cell due to exceeding max number of unavailable SMTC occasions, the UE shall stop the measurement attempts on this SSB and perform the detection procedure again like for any other SSB

## Slide 7: Topic #1: Remaining issues in intra and inter-frequency measurements
Issue 1-4-1: Applicability of SMTC2 signaling to NR-U
Signaling of smtc2 is applicable to unlicensed band.

## Slide 8: Topic #1: Remaining issues in intra and inter-frequency measurements
Issue 1-4-2: Scheduling restriction during SS-RSRP, SS-RSRQ and SS-SINR when deriveSSB_IndexFromCell is not enabled.
If deriveSSB_IndexFromCell is not enabled the UE is not expected to transmit PUCCH/PUSCH/SRS on all symbols within DRS window duration

## Slide 9: Topic #1: Remaining issues in intra and inter-frequency measurements
Issue 1-4-3: Definition of scheduling restrictions during SS-RSRP and SS-SINR measurements
When the UE performs intra-frequency measurements in unlicensed spectrum, the following restrictions apply due to SS-RSRP or SS-SINR measurement
  - The UE is not expected to transmit PUCCH/PUSCH/SRS on SSB symbols configured to be measured, and on 1 data symbol before each consecutive SSB symbols configured to be measured and 1 data symbol after each consecutive SSB symbols configured to be measured within SMTC window duration if deriveSSB_IndexFromCell is enabled. If the high layer in TS 38.331 signaling of smtc2 is configured, the SMTC periodicity follows smtc2; Otherwise SMTC periodicity follows smtc1.
  - The UE is not expected to transmit PUCCH/PUSCH/SRS on all symbols within SMTC window duration if deriveSSB_IndexFromCell is not enabled. If the high layer in TS 38.331 signaling of smtc2 is configured, the SMTC periodicity follows smtc2; Otherwise SMTC periodicity follows smtc1.
When intra-band carrier aggregation in unlicensed spectrum is performed, the scheduling restrictions due to a given serving cell should also apply to all other serving cells in the same band on the symbols that fully or partially overlap with the aforementioned restricted symbols.

## Slide 10: Topic #1: Remaining issues in intra and inter-frequency measurements
Issue 1-4-4: Definition of scheduling restrictions during SS-RSRQ measurements
o When the UE performs intra-frequency measurements in unlicensed spectrum, the following restrictions apply due to SS-RSRQ measurement
  - The UE is not expected to transmit PUCCH/PUSCH/SRS on SSB symbols configured to be measured, RSSI measurement symbols, and on 1 data symbol before each consecutive SSB configured to be measured/RSSI symbols and 1 data symbol after each consecutive SSB configured to be measured/RSSI symbols within SMTC window duration if deriveSSB_IndexFromCell is enabled. If the high layer signaling of smtc2 is configured(in TS 38.331), the SMTC periodicity follows smtc2; Otherwise the SMTC periodicity follows smtc1.
  - The UE is not expected to transmit PUCCH/PUSCH/SRS on all symbols within SMTC window duration if deriveSSB_IndexFromCell is not enabled. If the high layer in TS 38.331 signaling of smtc2 is configured, the SMTC periodicity follows smtc2; Otherwise SMTC periodicity follows smtc1.
o When intra-band carrier aggregation in unlicensed spectrum is performed, the scheduling restrictions due to a given serving cell should also apply to all other serving cells in the same band on the symbols that fully or partially overlap with the aforementioned restricted symbols

## Slide 11: Topic #1: Remaining issues in intra and inter-frequency measurements
Issue 1-4-5: Scheduling restrictions in inter-band CA
FFS: In FR1 inter-band CA, the scheduling restriction due to one CC shall not apply to other CCs on the other bands.

## Slide 12: Topic #1: Remaining issues in intra and inter-frequency measurements
Issue 1-5-1: UE behavior when receiving the MAC CE deactivation command for semi-persistent CSI reporting, in case of UL LBT failure for sending the ACK
o Option 1: At least from MAC (RAN2) layer perspective, UE follows the actions related to MAC-CE activation/deactivation command immediately after decoding the MAC-CE command regardless of whether UE is able to send HARQ-ACK feedback or not.
o Option 2 :If UE cannot transmit HARQ-ACK on MAC-CE deactivation due to UL CCA failure, UE continues to be in its previous state, i.e., it should measure and report L1-RSRP until it successfully transmits HARQ-ACK.

## Slide 13: Topic #1: Remaining issues in intra and inter-frequency measurements
Issue 1-6-1: Measurement capability
Same as licensed MO merging requirement on same NR carrier frequency layer, the principle to merge MOs on same NR-U carrier frequency layer is that those MOs would not need different measurement efforts from UE.
o Proposal 2: UE won’t merge NR-U MOs on the same frequency layer from PCell and PSCell if any of the following conditions is met,
- different RSSI measurement resources or
- different deriveSSB-IndexFromCell indications or
- different SMTC configurations or,
- different ssb-PositionQCL-Common-r16 indications or cell list of ssb-PositionQCL or,
- different rmtc-Config-r16 indication.

## Slide 14: Topic #2: RSSI and CO measurements
Issue 2-1-1: Intra-frequency RSSI measurement definition
No additional condition is needed for the intra-frequency measurement definition

## Slide 15: Topic #2: RSSI and CO measurements
Issue 2-1-2: Need for measurement gaps in RSSI measurements
Measurement gaps are needed for RSSI/CO measurements when RSSI BW is not fully within the active DL BWP of the UE.

## Slide 16: Topic #2: RSSI and CO measurements
Issue 2-2-1: RSSI measurement BW
Candidate options:
o Option 1 (Ericsson, Apple, Intel and Nokia): RSSI measurement bandwidth is the LBT bandwidth
o Option 2 (MediaTek, Qualcomm): The discussion can take place in the performance work

## Slide 17: Topic #2: RSSI and CO measurements
Issue 2-3-1: RSSI measurement period when measurement gaps are not required
  SMTC and RMTC are overlapping
    The RSSI and CO measurement periods depend on:
      max(reportInterval, rmtc-Period*CSSFoutside_gap,i) in non-DRX when measurement gaps are not required,
      max(reportInterval, max(rmtc-Period, DRX)*CSSFoutside_gap,i ) in DRX when measurement gaps are not required,
      CSSFoutside_gap,i takes into account the overlap between SMTC and RMTC
  SMTC and RMTC are not overlapping
    RSSI/CO measurement period is scaled with Nintra-MO, and corresponds to:
      Nintra-MO.max(reportInterval, rmtc-Period) when DRX is not used
      Nintra-MO.max(reportInterval, rmtc-Period, DRXcycle length) when DRX is used
      where Nintra-MO , reportInterval, and rmtc-Period is defined as the number of measurement objects that can be measured without gaps, configured reporting interval, and configured RMTC period, respectively.

## Slide 18: Topic #2: RSSI and CO measurements
Issue 2-3-2: RSSI measurement period when measurement gaps are required
When measurement gap is required, RSSI/CO measurement period corresponds to:
  max(reportInterval, max(rmtc-Period, MGRP)* CSSFwithin_gap,i) when DRX is not used
  max(reportInterval, max(rmtc-Period, MGRP, DRXcycle length )* CSSFwithin_gap,i) when DRX is used
  where CSSFwithin-gap,i is determined in clause 9.1.5.2 for measurement conducted within measurement gaps."

## Slide 19: Topic #2: RSSI and CO measurements
Issue 2-3-3: Scaling factor for DRX ≤ 320ms
Agreement: For RSSI Measurements, do not use the scaling factor of 1.5 when DRX ≤ 320ms.

## Slide 20: Topic #2: RSSI and CO measurements
Issue 2-3-4: CSSF definition outside measurement gaps
CSSF outside measurement gaps needs also to be adapted to account for RSSI/CO measurements.

## Slide 21: Topic #2: RSSI and CO measurements
Issue 2-4-1: RAN4 to define scheduling restrictions during RSSI/CO measurements
RAN 4 to define scheduling restrictions during RSSI/CO measurements

## Slide 22: Topic #2: RSSI and CO measurements
Issue 2-4-2: Differentiate the scheduling restriction during RSSI measurements when deriveSSB_indexFromCell is enabled or not
For scheduling restrictions during RSSI/CO measurements, do not differentiate the cases in which deriveSSB_indexFromCell is enabled or not

## Slide 23: Topic #2: RSSI and CO measurements
Issue 2-4-3: Exact definition of scheduling restriction during RSSI/CO measurements
  When the UE performs intra-frequency RSSI/CO measurements in unlicensed spectrum, the following restrictions apply due to RSSI/CO measurements
    The UE is not expected to transmit PUCCH/PUSCH/SRS on RSSI measurement symbols configured by RMTC.
  When intra-band carrier aggregation in unlicensed spectrum is performed, the scheduling restrictions due to a given serving cell should also apply to all other serving cells in the same band on the symbols that fully or partially overlap with the aforementioned restricted symbols.
  FFS: whether it is necessary to include the restriction on 1 data symbol before the first RSSI measurement symbol configured by RMTC, and 1 data symbol after the last RSSI measurement symbol configured by RMTC

## Slide 24: Topic #2: RSSI and CO measurements
Issue 2-4-4: Define scheduling restriction during RSSI measurements when the configured SCS in RMTC is different from the data SCS
Do not define scheduling restriction when the RMTC window duration if the SCS configured in RMTC is different from the SCS of data.