## Slide 1: WF on NR V2X RRM requirements
LG Electronics
3GPP TSG-RAN WG4 #96e
Electronic Meeting, 17-28 Aug., 2020
R4-2012104

## Slide 2
WF on Core maintenance
Interruption to WAN due to V2X Sidelink Communication(Sync.vs Async)
  Apply asynchronized requirement due to lack of synchronization mechanism between Uu and SL interface
Interruption to WAN for switching between LTE SL and NR SL
  Further discuss whether or not define this requirement by taking RF chain retuning and common local oscillator into account with a separated RX/TX chain.
Whether to differentiate the different type of NR communication in interruption requirement due to synchronization reference source change
  Not differentiate
Whether to define interruption requirement on LTE SL due to NR SL sync source is changed
  Further discussion whether to send LS to RAN1
  Further discussion whether to define RAN4 interruption requirement

## Slide 3
WF on Performance
Absolute accuracy of L1 SL-RSRP measurement
  Option 1: Define ±4.5dB as measurement accuracy of L1 SL-RSRP
  Option 2: Finalize measurement accuracy requirement once RF session concludes on cable loss issue
RRM requirements related to REFSENS
  Remove square brackets or update NR V2X operating band group and minimum received power in side condition based on agreed REFSENS in RF session

## Slide 4
WF on Work Plan
Work Plan
  RAN4#96-e meeting (’20.August)
    Agree the list of RRM test cases
    Do work-split of test cases for draft CRs
  RAN4#96-ebis & RAN4#97-e meeting (’20.October)
    Discuss the draft CRs with the detailed test configurations and related parameter
  RAN4#98 meeting (’21.March)
    Endorse the final draft CRs.
    Agree the one Big CR for RRM tests based on the endorsed draft CRs.

## Slide 5
WF on Baseline of Test Cases
Baseline of test cases
  LTE V2X RRM test cases can be the baseline to define NR V2X RRM test case.
    Further check which LTE V2X RRM test cases can be reused
  V2X SL {SCS & CBW} in all the RRM test
    {30kHz, 20MHz}, {30kHz, 40MHz}
    Add note:The UE is only required to be tested in one of the supported test configurations.
  Synchronization reference sources in the related RRM test cases
    GNSS, SyncRef UE, gNB
      Apply application rule for gNB
  gNB(FR1 NR Cell) configurations in all the related RRM test
Configuration | Description
1 | 15 kHz SSB SCS, 10 MHz bandwidth, FDD duplex mode
2 | 15 kHz SSB SCS, 10 MHz bandwidth, TDD duplex mode
3 | 30 kHz SSB SCS, 40 MHz bandwidth, TDD duplex mode
Note: The UE is only required to be tested in one of the supported test configurations. | 

## Slide 6
WF on Test for UE transmit timing
Introduce Tests for GNSS, SyncRef UE and gNB as timing reference
Test set-up for GNSS
  One GNSS based synchronization source is configured during the test. The test system emulates and sends the GNSS signal to the UE under test.
  The transmit timing accuracy is verified by the UE transmitting PSSCH
Test set-up for SyncRef UE
  One active SyncRef UE is configured during the test without either serving cell and or GNSS signals. The UE under test is synchronized to the configured active SyncRef UE.
  The transmit timing accuracy is verified by using the transmission timing of PSSCH transmissions.
Test set-up for gNB
  One active cell (PCell) is configured during the test. The UE under test is synchronized to the configured active cell (PCell).
  The transmit timing accuracy is verified by the UE transmitting PSSCH.
  Add applicable rule
    UE supporting SL and Uu is applied

## Slide 7
WF on Test for Initiation/Cease of SLSS Transmissions
Introduce Tests for SyncRef UE and gNB as timing reference
Test set-up for SyncRef UE
  There is one active SyncRef UE in this test without either serving cell and or GNSS signals.
  T1: the PSBCH-RSRP of SyncRef UE is above syncTxThreshOOC and the UE is not expected to be transmitting SLSS.
  T2: the PSBCH -RSRP of SyncRef UE is lowered below syncTxThreshOOC and the UE is expected to initiate SLSS transmissions.
  T3: the PSBCH -RSRP of SyncRef UE is increased back to be above syncTxThreshOOC and the UE is expected to cease SLSS transmissions.
Test set-up for gNB
  There is one active cell in this test.
  T1: the SS-RSRP of the PCell is above syncTxThreshIC and the UE is not expected to be transmitting SLSS.
  T2: the SS-RSRP of the PCell is lowered below syncTxThreshIC and the UE is expected to initiate SLSS transmissions.
  T3: the SS-RSRP of the PCell is increased back to be above syncTxThreshIC and the UE is expected to cease SLSS transmissions
  Add applicable rule
    UE supporting SL and Uu is applied

## Slide 8
WF on Test for Selection / Reselection of V2X Synchronization Reference Source
Introduce Tests when GNSS/gNB is configured as the highest priority.
Test set-up for GNSS
  Option 1 : 3 SyncRef UEs
    SyncRef UE1 (sync to gNB directly), SyncRef UE2 (sync to GNSS in-directly) and SyncRef UE3 (sync to GNSS directly).
  Option 2 : 2 SyncRef UEs
    SyncRef UE1 (sync to GNSS in-directly) and SyncRef UE2 (sync to GNSS directly).
  Decide one option in next meeting.
Test set-up for gNB
  No active cell in this test, GNSS signal is reliable and 2 active SyncRef UEs (SyncRef UE 1 and SyncRef UE 2) in this test.
  T1: Both SyncRef UE 1 and SyncRef UE 2 are powered off and the V2X UE will select GNSS as synchronization source.
  T2: SyncRef UE 1 is powered ON and the V2X UE will select SyncRef UE 1 as the synchronization source.
  T3: A higher priority SyncRef UE 2 is additionally powered ON and the V2X UE will reselect to the higher priority SyncRef UE 2 as the synchronization source.
  Add applicable rule
    UE supporting SL and Uu is applied

## Slide 9
WF on Test for L1 SL-RSRP measurements
Introduce Test for V2X UE Autonomous Resource Selection/Reselection
Test set-up
  Revise option 1 regarding RAN1 spec., ‘at least to be included in set SA, and the value of can be configured as {20%, 35%, 50%}.
  Option 1
    Active UE and subchannel allocation: there are 50 active UEs in the system, first 10 UEs occupies subchannel 0, the next 10 occupies subchannel 1, the next 10 occupies subchannel 2, following the allocation until all the 50 active UEs are allocated. Now the 5 subchannels configured for UE to be tested are each occupied by 10 UEs.
    The 10 UEs in the same subchannel take turns to access the channel, same as LTE but LTE has 20 UEs in one subchannel.
    UEs on subchannel 0/1/3/4 always transmit in high RSRP above the threshold (corresponding to 20dB SNR). UEs on subchannel 2 transmit with high RSRP in T1 and low RSRP in T2 (corresponding to 5dB SNR as PSCCH SNR in LTE).
    Reuse RSRP threshold in LTE, with the SNR in the previous bullet, to derive SL-RSRP and S-RSSI.
  Other options are not precluded

## Slide 10
WF on Test for L1 SL-RSRP measurements
Decide whether or not introduce Test for Resource Re-evaluation and Resource Pre-emption after conclusion on feasibility of tests
Need further check followings for Pre-emption Test
  Timeline to guarantee TE having enough time to send high priority reservation to trigger pre-emption:
    Option 1 : Configure the slot bitmap as 10000000000000000000 so that each available slot if far part enough to guarantee that the first transmission and the next reservation are not too close to accommodate TE decoding time and pre-emption timeline defined in RAN1
  How to prevent test UE to randomly select resource after sending SCI
    Option 1: The general resource selection spec violation may not necessary be tested in pre-emption test, if it can not be conveniently embedded in pre-emption test
  Other UE cheating behavior specific to resource pre-emption can be further discussed if companies come up with any other example
Need further check for Re-evaluation Test
  How to avoid the test UE to select the resource and send the initial transmission before sensing procedure?

## Slide 11
WF on Test for Congestion Control measurements
Introduce Test for Congestion Control Measurement
Test set-up
  Event-triggered reporting with Event C1 is used for V2X UE
  4 active sidelink UEs in this test.
  T1: all of active sidelink UEs are powered off.
  T2: all of active sidelink UEs are powered on and transmit PSCCH/PSSCH every 100ms (or 100 slot).

## Slide 12
WF on Test for Interruption
Introduce Test for interruptions to WAN due to V2X Sidelink Communication
Not introduce Test for interruptions due to sync. source change
Not introduce Test for interruptions to WAN due to UE switching between LTE SL and NR SL
Test set-up for interruptions to WAN due to V2X Sidelink Communication
  The test consists of one active cell (PCell) on the serving RF channel 1, and 8 active sidelink UEs transmitting V2X sidelink communication on RF channel 2.
  T1: the UE monitoring the V2X sidelink communication transmission from other active Sidelink UEs on the V2X sidelink communication resources.
  T2: the test system shall send RRC reconfiguration message to the UE and wait for the UE to respond with RRC reconfiguration complete message before transitioning to T3.
  T3: The test system will count the missed ACK/NACKs during T3 to verify the allowed interruptions during V2X sidelink communication
  Add applicable rule
    UE supporting SL and Uu is applied.

## Slide 13
WF on Test for Scheduling availability of UE switching between E-UTRA sidelink and NR sidelink
Test for Scheduling availability of UE switching between E-UTRA sidelink and NR sidelink
  Not introduce this test case

## Slide 14
WF on Work Splits for Test Cases
Tests | Volunteer Company | Comment
Transmit timing accuracy | Huawei | 
Initiation/Cease of SLSS Transmission | LG Electronics | 
Selection / Reselection of V2X Synchronization Reference Source | Xiaomi | 
V2X UE Autonomous Resource Selection/Reselection | Qualcomm | 
V2X UE Resource Pre-emption | Qualcomm | If this test case is agreed
V2X UE Resource Re-evaluation | Mediatek | If this test case is agreed(maybe merged with pre-emption)
Congestion Control measurements | Mediatek | 
Interruptions | Huawei | 
Related Configuration (resource pool, RMC) | Qualcomm | 
Big one CR | LG Electronics | It includes all draft CRs for test cases and related configuration
Company are encouraged to provide draft CR for corresponding test case in Table below in next meeting.

## Slide 15
WF on Spec. Skeleton for Test Cases
  A.9 V2X Tests
  A.9.1 V2X Tests in FR1
  A.9.1.1 V2X UE transmit timing Test
    A.9.1.1.1 Test for GNSS as synchronization reference source
    A.9.1.1.2 Test for SyncRef UE as synchronization reference source
    A.9.1.1.3 Test for FR1 NR Cell as synchronization reference source
  A.9.1.2 Initiation/Cease Test of SLSS Transmission with V2X Sidelink Communication
    A.9.1.2.1 Test for SyncRef UE as synchronization reference source
    A.9.1.2.2 Test for FR1 NR Cell as synchronization reference source
  A.9.1.3 V2X Synchronization Reference Selection/Reselection Test
    A.9.1.3.1 Test for GNSS configured as the highest priority
    A.9.1.3.2 Test for FR1 NR Cell configured as the highest priority
  A.9.1.4 L1 SL-RSRP Measurement Test
    A.9.1.4.1 Test for V2X UE Autonomous Resource Selection/Reselection
    [A.9.1.4.2 Test for V2X UE Resource Pre-emption] or
    [A.9.1.4.2 Test for V2X UE Resource Re-evaluation and Resource Pre-emption]
  A.9.1.5 Congestion Control Measurement Test
  A.9.1.6 Interruption Test
  A.9.1.6.1 Test for Interruptions to WAN due to V2X Sidelink Communication
  A.3.19 V2X sidelink communication
  A.3.19.1 Introduction
  A.3.19.2 Reference resource pool configurations for V2X Sidelink Communication
  A.3.19.3 Reference measurement channels for V2X Sidelink Communication