## Slide 1: Way Forward on SCell Dormancy
Ericsson, ...
3GPP TSG-RAN WG4 Meeting #96-e
Electronic Meeting, August 17 – 28, 2020
R4-2012117
Document for: Approval

## Slide 2: Background
At RAN4#94e, agreements on SCell dormancy were captured in R4-2002238 “WF on UE RRM requirements for dormancy SCell”
At RAN4#94e-Bis, agreements on SCell dormancy were captured in R4-2005329 “Way Forward on SCell Dormancy”
At RAN4#95e, agreements on SCell dormancy were captured in R4-2008607 “Way Forward on SCell Dormancy”

## Slide 3: Background
At RAN4#96e, the following topics were discussed:
Sub-topic 2-1: General
  Issue 2-1-1: Triggering options
  Issue 2-1-2: Optimizations w.r.t. parameter changes
Sub-topic 2-2: Switching of single SCell between dormancy and non-dormancy, triggering inside active time
  Issue 2-2-1: Delay requirement, triggering within first 3 OFDM symbols
  Issue 2-2-2: Validity of DCI-based triggering after first 3 OFDM symbols
  Issue 2-2-3: Delay requirement, triggering after first 3 OFDM symbols
  Issue 2-2-4: Interruption requirement
  Sub-topic 2-3: Switching of single SCell between dormancy and non-dormancy, triggering outside active time
  Issue 2-3-1: Delay requirements, outside DRX active time
  Issue 2-3-2: Interruption requirements, outside DRX active time
  Sub-topic 2-4: CSI and RRM measurements during dormancy
  Issue 2-4-1: Interruptions due to CSI and RRM measurements
  Sub-topic 2-5: Switching of multiple SCells between dormancy and non-dormancy
  Issue 2-5-1: Delay requirements, switching of multiple SCells
  Issue 2-5-2: Interruption requirements, switching of multiple SCells
  Sub-topic 2-6: Requirements for cross carrier scheduled DCI-based BWP switch on single/multiple CCs
  Issue 2-6-1: Whether existing BWP switching requirements can also apply
  Issue 2-6-2: Whether to define requirements for cross carrier scheduled DCI-based BWP switch

## Slide 4: 2-1-1: Triggering options
Agreement:
Remove Timer-based triggering from scope and only support DCI-based triggering.
2-1-2: Optimizations w.r.t. parameter changes
Agreement:
  RAN4 to only introduce generic requirements, and the further need for optimizations w.r.t. parameter change can be discussed in the future release, if needed

## Slide 5: 2-2-1: Delay requirement, triggering within first 3 OFDM symbols
Agreement:
  Additional [1] slot relaxation is applied to compensate for cross carrier scheduling
    In case SCS differs between spCell and SCell, the smaller SCS applies.

## Slide 6: 2-2-2: Validity of DCI-based triggering after first 3 OFDM symbols
Agreement:
  Triggering by means of receiving DCI after first X=3 OFDM symbols in a slot is only valid for UE supporting pdcch-MonitoringAnyOccasionsWithSpanGap or pdcch-MonitoringAnyOccasions.
  The conditions are captured in RAN1 specification, and at least for now we do not repeat them in the RRM specification.

## Slide 7: 2-2-3: Delay requirement, triggering after first 3 OFDM symbols
Agreement:
  RAN4 captures the delay requirement for triggering after first 3 OFDM symbols in a DCI format-agnostic manner
  In case RAN1 introduces restrictions for DCI formats 0_1 and/or 1_1, RAN4 will update the RRM specification accordingly.
  Additional [1] slot relaxation is applied to compensate for cross carrier scheduling
    In case SCS differs between spCell and SCell, the smaller SCS applies.
  Additional Z=1 slot (spCell numerology) relaxation is applied for DCI received after first X=3 symbols in a slot

## Slide 8: 2-2-4: Interruption requirement
Agreement:
  Upon BWP transition in a single SCell into/out of dormancy, RAN4 to define the interruption requirements as follows:
    Interruption length as in Table 8.2.2.2.5-1 applies
    The starting time of interruption is only allowed within the BWP switching delay for transition between dormancy and non-dormancy
    If UE is not capable of per-FR gap, UE is allowed to cause interruption of up to X slots to other active serving cells.
    If UE is capable of per-FR gap, UE is allowed to cause interruption of up to X slots to other active serving cells in the same frequency range
    If UE is capable of per-FR gap, and the BWP switching involves a SCS change, the UE is additionally allowed to cause interruptions of up to X slots to other active serving cells in any frequency range.
    Interruptions are allowed regardless of which parameters change between dormancy and non-dormancy
    During the BWP switching delay plus the interruption length, UE is not expected to transmit ACK/NACK feedback for non-scheduling DCI as well as receive PDSCH and transmit PUSCH scheduled by dormancy indication DCI

## Slide 9: 2-3-1: Delay requirements, outside DRX active time
Agreement:
  For BWP transition in a single SCell into/out of dormancy triggered by DCI 2-6 outside active time, the same set of switch delay requirements shall be applied as for triggering inside active time.
  If RAN1 defines something that makes Dormant BWP switching time/interruption outside DRX active time to always be absorbed into WUS gap, RAN4 revises the specification text accordingly.

## Slide 10: 2-3-2: Interruption requirements, outside DRX active time
Agreement:
  For BWP transition in a single SCell into/out of dormancy triggered by DCI 2-6 outside active time, the same set of interruption requirements shall be applied as for triggering inside active time.
  If RAN1 defines something that makes Dormant BWP switching time/interruption outside DRX active time to always be absorbed into WUS gap, RAN4 revises the specification text accordingly.

## Slide 11: 2-4-1: Interruptions due to CSI and RRM measurements
Agreement:
  For Interruptions due to SSB-based measurements and/or CSI-RS reception,
    If P-CSI reporting in dormant SCell is not configured or configured with a periodicity of CSI-ReportConfig for a domant SCell larger than [Z=160]ms:
      Interruptions due to SSB reception are allowed with up to [X=0.5]% probability of missed ACK/NACK with the following conditions
        UE is only allowed to cause interruptions immediately before and after an SSB burst
        Each interruption shall not exceed requirement in Table 8.2.2.2.2-1 if victim cells are not in the same band as the aggressor SCell
        Each interruption shall not exceed requirement in Table 8.2.2.2.2-2 if victim cells are in the same band as the aggressor SCell.
      For CSI-RS reception,
        UE is allowed to cause interruptions immediately before and after consecutive CSI-RS resources associated with CSI-ReportConfig
        Additionally, if there are configured periodic CSI-RS resources not for CSI acquisition (e.g. TRS, BM), interruptions are allowed with up to [Y=0.5]% probability of missed ACK/NACK immediately before and after the consecutive CSI-RS resources not associated with CSI-ReportConfig
        Each interruption shall not exceed requirement in Table 8.2.2.2.2-1
      Whether or not interruption happens to cells across FRs is determined by whether UE is capable of per-FR gap or not as defined in the legacy requirement of interruptions during measurements on deactivated SCC
      Otherwise:
        SSB and CSI-RS reception in the dormant SCell shall not cause interruption to active Cells
  Values of Z, X and Y are to be revisited at next RAN4 meeting

## Slide 12: 2-5-1: Delay requirements, switching of multiple SCells
Agreement:
  Delay requirements for switching of multiple SCells between dormancy and non-dormancy shall be based on corresponding delay requirements for switching of multiple SCells between non-dormant BWPs, i.e., TMultipleBWPswitchDelay or TMultipleBWPswitchDelay+Z for simultaneous BWP switching case.
  The further need for optimizations can be discussed in the future release, if needed

## Slide 13: 2-5-2: Interruption requirements, switching of multiple SCells
Agreement:
  Interruption requirements for switching of multiple Scells between dormancy and non-dormancy shall be based on corresponding interruption requirements for switching of multiple SCells between non-dormant BWPs, i.e., the interruption as defined for single CC dormancy switch is allowed for each dormancy switch.
  Interruption is allowed regardless of which parameters change between dormancy and non-dormancy
  The further need for optimizations can be discussed in the future release, if needed

## Slide 14: 2-6-1: Requirements for cross carrier scheduled DCI-based BWP switch on single/multiple CCs
Agreement:
  Existing Rel-15/Rel-16 BWP switching requirements cannot apply for cross carrier scheduled DCI-based BWP switch on single/multiple CCs

## Slide 15: 2-6-2: Requirements for cross carrier scheduled DCI-based BWP switch on single/multiple CCs
Agreement:
  RAN4 to define requirements for cross carrier scheduled DCI-based BWP switch on single/multiple CCs in Rel-16

## Slide 16: For next RAN4 meeting
  Sub-topic 2-4: CSI and RRM measurements during dormancy
  Issue 2-4-1: Interruptions due to CSI and RRM measurements
    Interested companies are invited to revisit tentative values X=0.5, Y=0.5 and Z=160ms.
  Sub-topic 2-6: Requirements for cross carrier scheduled DCI-based BWP switch on single/multiple CCs
    Define requirements for cross carrier scheduled DCI-based BWP switch on single/multiple CCs in R16.