## Slide 1: 3GPP TSG-RAN WG4 Meeting #96-e Electronic Meeting, 17-28 Auguest, 2020
Intel
WF on requirements for PRS-RSRP measurements
R4-2012133

## Slide 2: Measurement period for PRS RSRP
The principle to define measurement period of PRS RSRP can be:
  If the number of required PRS-RSRP samples is larger than the number of samples of RSTD or UE Rx-Tx, then:
    when configured with UE Rx-Tx time difference, PRS-RSRP measurement period requirements can be:
      max(TPRS-RSRP,TUE Rx-Tx), where TPRS-RSRP and TUE Rx-Tx are the measurement periods for PRS-RSRP and UE Rx-Tx, when configured without other measurements
    when configured with RSTD, PRS-RSRP measurement period requirements can be :
      max(TPRS-RSRP,TRSTD), where TPRS-RSRP and TRSTD are the measurement periods for PRS-RSRP and RSTD, when configured without other measurements
    If PRS-RSRP is not configured together with any of UE Rx-Tx or RSTD, the PRS-RSRP measurement is defined as TPRS-RSRP
  If the number of required PRS-RSRP samples is not larger than the number of samples of RSTD or UE Rx-Tx, then:
    when configured with UE Rx-Tx time difference, PRS-RSRP measurement period requirements can be:
      TUE Rx-Tx where TUE Rx-Tx are the measurement periods for UE Rx-Tx, when configured without other measurements
    when configured with RSTD, PRS-RSRP measurement period requirements can be :
      TRSTD,where TRSTD are the measurement periods for RSTD, when configured without other measurements
  If PRS-RSRP is not configured together with any of UE Rx-Tx or RSTD, the PRS-RSRP measurement is defined as TPRS-RSRP
    when configured with UE Rx-Tx time difference, PRS-RSRP measurement period requirements can be same as that of UE Rx-Tx time difference measurement
    when configured with RSTD, PRS-RSRP measurement period requirements can be same as that of RSTD measurement
    when not configured with either UE Rx-Tx or RSTD, measurement period requirements of RSTD can be reused for PRS-RSRP measurement.
  Notes: The exact number of required samples for a successful PRS-RSRP measurement report can be same as that of for RSTD or UE Rx-Tx. If any issues identified for this number during the performance part (e.g. the lager number is needed to grantee the correct PRS RSRP measurement) RAN4 can revise this number absolutely.

## Slide 3: Measurement capability
RAN4 will refer to RAN2 positioning capabilities in RAN4 requirements
RAN4 will not separately define measurement capability in terms of number of PRS layers, TRPs, resource sets and resources that UE shall be able to measure
  [Moderator Notes: According to the majorities’ view, the minimum capability for PRS RSRP report can be covered by RAN1’s capability defined. ]

## Slide 4: Side condition
For DL-AoD, the side condition of PRS RSRP can be specified
  Option 1: Serving cell/TRP side conditions need to be specified (in addition to neighbour cells) as
    Option 1-1: -6 dB
    Option 1-2. -3 dB
  Option 2: For the reference cell/TRPs side conditions ned to be specified (in addition to neighbour cells) and neighbour cell/TRPs
    Same as that for the reference cell in PRS-RSTD
  Option 3 :for neighbor cell/TRPs ONLY.
  Option 4: serving cell/TRP and reference cell/TRP need to be specified (in addition to neighbour cells)

## Slide 5: Measurement accuracy requirements for PRS RSRP
Number of samples for PRS RSRP measurement accuracy:
  FFS, consider that PRS occasion is not defined by RAN4
  Option 1: 1 sample including resource repetitions within the PRS occasion
  Option 2: depends on
    the number of slot repetitions (note: two closest repetitions within the same PRS period can be separated by up to 32 slots), and
    the number of comb patterns per slot
Types of requirements
  Option 1: Define absolute accuracy requirements ONLY
  Option 2: Define relative accuracy requirements ONLY
  Option 3: Define both absolute and relative accuracy requirements

## Slide 6: PRS RSRP measurement under cell change
When configured together with UE Rx-Tx, the UE behavior rules for PRS-RSRP are the same as for these for UE Rx-Tx (agreed in [R4-1915854])
When configured together with RSTD, the UE behavior rules for PRS-RSPR measurement under cell change are the same as for RSTD (the rules for RSTD were agreed in [R4-1915854]):
  The UE shall continue RSTD measurement after each serving cell change for:
    intra-frequency handover,
    inter-frequency handover.
When not configured together with either UE Rx-Tx or RSTD, the UE behavior rules for PRS-RSPR measurement under cell change are the same as for RSTD (the rules for RSTD were agreed in [R4-1915854]).