## Slide 1: WF on impact of NR positioning measurements on RRM
Ericsson
3GPP TSG-RAN WG4 Meeting # 96-e
Electronic Meeting, August 17-28, 2020
Agenda: 7.7
R4-2012135

## Slide 2: New MG Patterns
Introduce following 2 new MG patterns:
New MG patterns can only be configured when the UE is configured with PRS measurements.
MGL (ms) | MGRP (ms)
10 | 80
20 | 160

## Slide 3: Applicability of new MG Patterns
Whether new MG patterns is applicable for only PRS measurements or for both PRS and RRM measurements?
Status: no consensus
Candidate options:
  Option 1:
    New MG patterns are applicable only for PRS measurements i.e. new gaps cannot be shared with RRM measurements.
  Option 2:
    New MG patterns are applicable for PRS and all RRM measurements i.e. new gaps can be shared between PRS and RRM measurements.
  Option 3:
    New MG patterns are applicable for PRS and NR/LTE RRM measurements i.e. new gaps are not shared between PRS and 2G/3G RRM measurements.
  Option 4:
    New MG patterns are applicable for PRS and RRM measurements;
    the UE is required to meet requirements for PRS measurements performed in the new MG gap pattern; and
    while the new MG pattern is configured for the PRS measurements the UE is not required to meet requirements for RRM measurements which need gaps.

## Slide 4: New MG Pattern Capabilities
New MG patterns is defined as per-UE or per-UE and per-FR capabilities?
Status: no consensus
Candidate options:
  Option 1:
    Defined as per-UE and per-FR capabilities
  Option 2:
    Defined as only per-UE capability

## Slide 5: New MG Patterns
If new gaps are shared between PRS and RRM measurements then use the existing CSSF for sharing new MG pattern between RRM and PRS measurements?
Status: no consensus
Candidate options:
    Yes
    No

## Slide 6: New MG Patterns
If existing CSSF is used then rules for new MG sharing between RRM and PRS measurements?
Status: no consensus
Candidate options:
  Option 1:
    Equal split of gaps between PRS and all RRM measurements
  Option 2:
    NR positioning measurements are counted together with inter-frequency and inter-RAT measurement objects and
    gap sharing of NR positioning should be based on the same principle of LTE-PRS, i.e., scarce PRS (corresponding to long periodicities) should be prioritized over other candidates for measurement in the same gap instance.
  Option 3:
    If PRS periodicity >= 80 ms, then PRS measurement is prioritized over other candidates for measurement in the same gap instance;
    Otherwise, Equal split of gaps between PRS and all RRM measurements

## Slide 7: SRS transmission during DRX inactive
Periodic and semi-persistent positioning SRS transmissions during DRX inactive time are NOT allowed in Rel-16.