## Slide 1: WF on System simulation assumptions for deriving side conditions
Ericsson
3GPP TSG-RAN WG4 Meeting #96-e
Electronic Meeting, August 17 - 28, 2020
Agenda Item: 7.7.2.3
R4-20xxxx

## Slide 2: Back round
The Side conditions for gNB accuracy requirements are under discussion [1]
Sub-topic 2-3 Issue 2-3-2: derive side conditions (e.g. SINR)
  Option 2:
    Based on system simulations
[1] R4-2012048 Email discussion summary for [96e][217] NR_pos_RRM_Part_3

## Slide 3: Side conditions for gNB accuracy requirements FR1 (1)
Input:
  Channel model: AWGN and TDL-B (with a medium delay spread)
  FR1: 4GHz carrier, 5 MHz, 10 MHz, 100MHz BW, 30kHz SCS
  Hexagonal grid, 3 sectors per site, 7 macro sites, ISD = 500m Wrap-around is applied
  1, 5, 10 UEs per cell as a start. Equal amount of UEs per cell.
  2 UE Tx antenna, 2 BS Rx antenna
  The BS with smallest path lost (PL) is the serving BS
  Simplified power control (depends only on the PL)
  Perfect TA so that the serving BS receive all member UE SRSs at the same time
  SRS are configured per serving cell, with no regard to other cells.
  UE TX power = 23dBm
  BS RX noise figure = 5 dB
  Antenna model based on: TR 38.855 - Study on NR positioning support

## Slide 4: Side conditions for gNB accuracy requirements FR2 (2)
Input:
  Channel model: AWGN and TDL-B (with a medium delay spread)
  FR2: 40GHz carrier, 200MHz BW (128 PRBs), 120kHz SCS (option 100 MHz)
  Hexagonal grid, 3 sectors per site, 7 macro sites, ISD = 500m Wrap-around is applied
  1, 5, 10 UEs per cell as a start. Equal amount of UEs per cell.
  2 UE Tx antenna, 2 BS Rx antenna for (number of Antennas for fading channel FFS)
  The BS with smallest path lost (PL) is the serving BS
  Simplified power control (depends only from the PL)
  Perfect TA so that the serving BS receive all member UE SRSs at the same time
  SRS are configured per serving cell, with no regard to other cells.
  UE TX power = 23dBm
  BS RX noise figure = 7 dB
  Antenna model based on TR 38.855 - Study on NR positioning support

## Slide 5: Side conditions for gNB accuracy requirements (3)
SRS configurations:
  Symbol size =4
  Comb. Number =4
  Cyclic shift Max. Number =12
  Intra-cell, Offsets in Comb. and Cyclic shift keep orthogonal.
  Inter-cell, Offsets in Comb. and Cyclic shift is randomized.
Output: Serving cell and neighboring cell Ês/IoT [dB] CDF figures.

## Slide 6: Antenna Parameter
Appication | Frequency Range |  | FR1 |  |  |  | FR2 |  |  | 
 | Envirement |  | Scenarion 1 500 m |  | Scenario 2 |  | Scenarion 3 200 m |  | Scenario 4 | 
 | Donor or Service Antenna |  | BS-Rx | UE-Tx | BS-Rx | UE-Tx | BS-Rx | UE-Tx | BS-Rx | UE-Tx
Radiation Element | Front to Back Ratio | Am | 30 dB | 25 dB |  |  | 30 dB | 25 dB |  | 
 | Side lobe suppression | SLA | 30 dB | 25 dB |  |  | 30 dB | 25 dB |  | 
 | Half Power Beam Width Horizontal |  | 65° | 90° |  |  | 65° | 90° |  | 
 | Half Power Beam Width Vertical |  | 65° | 90° |  |  | 65° | 90° |  | 
 | Dirctivity (for information) | DE | 9,2 dBi |  |  |  | 8 dBi | 5 dBi |  | 
Antenna Model Parameter | Antenna configuration (M, N, P, Mg, Ng) |  | 8, 8, 2, 1, 1 | 1, 2, 2, 1, 1 |  |  | 4,8,2,2,2 | 2,4,2,1,2 |  | 
 | Number of ports (for information) |  |  |  |  |  |  |  |  | 
 | Vertical radiating element spacing dV | dV | 0,8 λ | 0,5 λ |  |  | 0,5 λ | 0,5 λ |  | 
 | Horizontal radiating element spacing dH | dH | 0,5 λ | 0,5 λ |  |  | 0,5 λ | 0,5 λ |  | 
 | Down tilt angle electical |  | 10° | 0° |  |  | 0° | 0° |  | 
 | Dow tild angele mechanical |  | 0° | 0° |  |  | 0° | 0° |  | 
Antenna Parameter per Port | Directivity (for information) |  | 20 dBi | 18 dBi |  |  |  |  |  | 
 | Antenna losses |  | 1,8 dB | 1,8 dB |  |  | 1 dB | 1dB |  | 
 | Gain |  | 18 dBi | 0 dBi |  |  | 17 dBi | 27 dBi |  | 
Note: | Mg = number of antenna panels in elevation, Ng – number of antenna panels in azimuth, M = number of antenna elements/subarrays in elevation, N= number of antenna elements/subarrays in azimuth, P = number of polarizations. |  |  |  |  |  |  |  |  | 

## Slide 7: Antenna model