## Slide 1: WF on Completing Rel-16 eMIMO RRM Core Requirement
Samsung, …
3GPP TSG-RAN WG4 Meeting # 96-e
Electronic Meeting, 17 – 28 Aug, 2020
R4-2012146

## Slide 2: Agreement from RAN4#96 Chairman Notes from 1st Round
Topic #2: DL/UL Beam Indication with Reduced Latency and Overhead
Issue 2-1-1: The necessity of RRM requirement for MAC-CE based Pathloss RS activation procedure:
Agreement
MAC-CE based pathloss RS activation procedure:
  RAN4 specify known/unknown PL RS condition, and specify delay requirement when target PL RS is known.
No performance test should be defined in Rel-16 to capture this requirement in 38.133 if RAN4 can’t confirm the testability of the pathloss RS activation procedure.
Issue 2-1-2: If RAN4 conclude “yes” to Issue 2-1-1, how to specify requirement:
Agreement
Delay requirement for MAC-CE based Pathloss RS activation procedure:
  For PL RS known case, n + +
Issue 2-1-3: If RAN4 conclude “yes” to Issue 2-1-1, expected UE behavior before Pathloss RS is applied:
Agreement
No requirement should be defined during the transition period of the applicable timing, i.e., between 1 to 5 measurement samples, for activating/updating PL RS.
RAN4 further study and conclude the timeline to apply old PL RS by RAN4#96:
  FFS: UE shall apply old pathloss reference signals until the slot n + + , upon receiving PDSCH carrying MAC-CE activation in slot n.

## Slide 3: Agreement from RAN4#96 Chairman Notes from 1st Round (cont.)
Topic #3: Multi-TRxP Transmission
Issue 3-1-2: Whether or not to specify how UE determine the reference timing of which TRxP is used for defining MRTD/MTTD requirements in intra-band EN-DC/CA
Agreement
For multi-TRxP transmissions, RAN4 shall not to specify how UE to determine the reference timing of which TRxP is used for defining MRTD/MTTD requirements in intra-band EN-DC/CA.

## Slide 4: Agreement from RAN4#96 Chairman Notes from GTW Session (25th Aug)
Topic #2: DL/UL Beam Indication with Reduced Latency and Overhead
For expected UE behaviour before Pathloss RS is applied:
Agreement
UE shall apply old pathloss reference signals until the slot n + + , upon receiving PDSCH carrying MAC-CE activation in slot n.
Topic #3: Multi-TRxP Transmission
Agreement
For Rel-16 eMIMO multi-TRxP transmission,
    No RRM core requirement impact identified on MRTD/MTTD values specified in Rel-15;

## Slide 5: WF on Multi-TRxP Transmission
For Rel-16 eMIMO multi-TRxP transmission,
    It is RAN4 common understanding that MRTD/MTTD requirements in clauses 7.5.3, 7.6.3 and 7.6.4 is sufficient for support the deployment with multi-DCI based and single-DCI based multi-TRxP transmission.