## Slide 1: WF on test case for DL interruption due to Tx switching between two uplink carriers
Huawei, HiSilicon
3GPP TSG-RAN WG4 Meeting #96-e
Electronic Meeting, 17-28 Aug., 2020
      R4-2012150
Document for: Approval

## Slide 2: Agreement
No test cases are defined for the following cases:
    SUL+TDD
    TDD+TDD CA with the same UL-DL pattern
    TDD+TDD EN-DC with the same UL-DL pattern
The following test cases shall be defined to verify the DL interruption due to UE dynamic switching between two uplink carriers:
  DL Interruptions at UE switching between LTE 1Tx carrier and NR 2Tx carrier in inter-band ENDC case.
  DL Interruptions at UE switching between NR uplink carrier 1 and NR uplink carrier 2 in inter-band uplink CA case.

## Slide 3: Agreement
Test case for DL Interruptions at UE switching between LTE 1Tx carrier and NR 2Tx carrier in inter-band ENDC case:
    DL Interruptions at UE switching between LTE 1Tx carrier and NR 2Tx carrier in inter-band ENDC case, herein the interruptions on victim LTE serving cells and victim NR serving cells are both verified.
    Test configurations
    UE antenna configuration
Config | Description
1 | LTE FDD, NR 30kHz SSB SCS, 40 MHz bandwidth, TDD duplex mode
PCell (LTE carrier 1) | 1x2
PSCell (NR carrier 2) | 2x2

## Slide 4: Agreement
Test case for DL Interruptions at UE switching between NR uplink carrier 1 and NR uplink carrier 2 in inter-band uplink CA case:
    Test configurations
    UE antenna configuration
PCell (NR carrier 1) | 1x2
PSCell (NR carrier 2) | 2x2
Config | Description
1 | NR carrier 1: 15 kHz SSB SCS, 10 MHz bandwidth, FDD duplex mode; NR carrier 2: 30 kHz SSB SCS, 40 MHz bandwidth, TDD duplex mode;
2 | NR carrier 1 30 kHz SSB SCS, 40 MHz bandwidth, TDD duplex mode; NR carrier 2 30 kHz SSB SCS, 40 MHz bandwidth, TDD duplex mode; Note: TDD CA combination configuration with different UL/DL patterns

## Slide 5: Way Forward
How to verify the symbol-level DL interruption in test
  Test case for verifying Radio Link Monitoring Scheduling Restrictions can be as an reference.
  This test verifies that UE can correctly receive the PDCCH scheduled on the symbols right before the DL interruption so that it sends ACK/NACK correctly.
  Interruption location happens from symbol #[14-(Interruption length+2)] to the end of last GP symbol assuming 2 symbols for SRS transmission in special slot.
  Detailed parameters are FFS, e.g., MRTD
  Other test schemes are not precluded

## Slide 6: Work split
Index | Test cases | Assigned company | Big CR responsibility
1 | Test case for DL Interruptions at UE switching between LTE 1Tx carrier and NR 2Tx carrier in inter-band ENDC case | Huawei | Huawei
2 | Test case for DL Interruptions at UE switching between NR uplink carrier 1 and NR uplink carrier 2 in inter-band uplink CA case (FDD+TDD) | China Telecom | 
3 | Test case for DL Interruptions at UE switching between NR uplink carrier 1 and NR uplink carrier 2 in inter-band uplink CA case (TDD+TDD with different UL/DL pattern) | CMCC |