## Slide 1: WF on NR RRM enhancements – multiple SCell activation
Apple, …
R4-2012164
3GPP TSG-RAN4 Meeting #96-e
Online, 17-28 Aug., 2020
Agenda item: 7.13
Document for: Approval

## Slide 2: Tx beam assumption of FR1 intra-band contiguous CA (Issue 2-1 in R4-2012160)
Agreement in RAN4 #96e:
  FFS
    whether UE shall assume that the transmitted signals from the serving cells should have the same downlink spatial domain transmission filter on one OFDM symbol on the contiguous CCs in the same band in FR1, for RRM requirements in RRC connected state

## Slide 3: Principle to decide test case coverage (Issue 2-2-1 in R4-2012160)
Agreement in RAN4 #96e:
  P1: test the multiple SCell activation for unknown to-be-activated SCells, and test the multiple SCell activation for mixed unknown and known to-be-activated SCells.
  P2: only test the multiple SCell activation under EN-DC and NR-DC mode.
  P3: only test the multiple SCell activation under non-DRX mode and have different test requirements for both per-FR MG capable UE and per-UE capable UE.
  P4: only test the multiple SCell activation with periodic CSI-RS for CSI reporting for FR2 to-be-activated SCells.

## Slide 4: Test case list (Issue 2-2-2 in R4-2012160)
Agreement in RAN4 #96e:
  the test case list for Rel-16 multiple SCell activation of eRRM is:
    TC 1: EN-DC of LTE+FR1 NR without DRX with single MAC CE
      2 FR1 unknown to-be-activated SCells, where
        first FR1 unknown SCell is intra-band contiguous to active FR1 NR PSCell (meet the exception condition of N1 counting)
        second FR1 unknown SCell is inter-band to active FR1 NR PSCell
    TC 2: EN-DC of LTE +FR1 NR (the existing activated serving cell) without DRX (test both per-FR MG capable UE and per-UE MG capable UE) with single MAC CE
      1 FR2 known to-be-activated SCell and 1 FR2 unknown to-be-activated SCell
      Both to-be-activated SCells are configured with periodic CSI-RS for CSI reporting
    TC 3: NR-DC without DRX (test per-FR MG capable UE) with dual MAC CEs
      one inter-band FR1 unknown to-be-activated SCells + one FR2 unknown to-be-activated SCells with periodic CSI-RS for CSI reporting