## Slide 1
3GPP TSG-RAN WG4 Meeting #96-e R4-2012182
Electronic Meeting, 17-28 Aug., 2020
Agenda Item: 7.15.1&7.15.2
WF on RRM for NR HST
CMCC

## Slide 2: Background
The following WFs were approved:
  R4-1912781 WF on RRM for NR HST, RAN4#92BIS
  R4-1915887 WF on RRM for NR HST, RAN4#93
  R4-2002253 WF on RRM for NR HST, RAN4#94-e
  R4-2005358 WF on RRM for NR HST, RAN4#94-e-bis
  R4-2008627 WF on RRM for NR HST, RAN4#95-e

## Slide 3: Cell re-selection
  Whether to enhance the measurement requirements for inter-RAT layers of higher priority
    No enhancement to cell re-selection requirements for inter-RAT layers of higher priority

## Slide 4: Release independent
Rel.16 NR HST RRM enhanced requirements are release independent from Rel-15

## Slide 5: Measurement accuracy
Rel-15 SS-SINR accuracy for FR1 is reused for NR HST when -3dB≤SSB Ês/Iot ≤5 dB
Rel-15 measurement accuracy of RSRP and RSRQ are reused for high speed scenario

## Slide 6: Test cases list
Test scenario | Test cases | Test parameters
1. NR SA | NR-NR intra-frequency reselection for FR1 | DRX cycle: 320ms SMTC period: 20ms
2a. ENDC 2b. NR SA | NR-NR intra-frequency event triggered reporting tests without gap under DRX without SSB index reading for FR1 intra-frequency case | DRX cycle: 640ms SMTC period: 20ms
4. NR SA | NR-EUTRA inter-RAT cell re-selection | DRX cycle: 320ms SMTC period: 20ms
5. NR SA | NR-EUTRA inter-RAT event triggered reporting test under DRX in FR1 | DRX cycle: 320ms SMTC period: 20ms MGRP: 40ms MGL: 6ms
6. E-UTRAN | EUTRA-NR inter-RAT cell re-selection | DRX cycle: 320ms SMTC period: 20ms
7. E-UTRAN | EUTRA-NR inter-RAT event triggered reporting for FR1 with SSB time index detection when DRX is used | DRX cycle: 320ms SMTC period: 20ms MGRP: 40ms MGL: 6ms
8a. ENDC 8b. NR SA | SSB based L1-RSRP measurement when DRX is used | DRX cycle: 320ms SMTC period: 20ms
The propagation condition for the test cases of NR HST is AWGN/AWGN 1944 (15kHz SCS) and AWGN 3334(30kHz SCS) Hz

## Slide 7: CR split
Work-split of test cases for draft CRs
 | Responsibility
Test cases for NR -NR cell reselection | CMCC
Test cases for NR -NR cell identification in connected mode | Ericsson
Test cases for NR-EUTRA cell reselection | QC
Test cases for NR-EUTRA cell identification in connected mode | Huawei
Test cases for EUTRA-NR cell reselection | vivo
Test cases for EUTRA-NR cell identification in connected mode | Huawei
Test cases for L1-RSRP | Nokia, Nokia Shanghai Bell
Big CR sourcing company: CMCC