## Slide 1: 3GPP TSG-RAN WG4 Meeting #96-e Electronic Meeting, August 17 – 28, 2020
Ericsson, […]
Way forward on RRM performance requirements for MTC
R4-2012192

## Slide 2: RSS based neighbour cell measurement conditions in IDLE and CONNECTED mode
Introduce capability signaling to indicate whether the UE is able to measure on neighbor cell RSS that is in the same NB that UE monitors.

## Slide 3: New test cases to be introduced in release 16
Type of test | RRC state | Coverage level | Test conf. | Duplex mode | Assigned company
DL quality reporting | IDLE | Normal and enhanced coverage | AL = 24, RP > 1 for normal coverage; AL=24, RP>1 for enhanced coverage AWGN channel, MSG3 based reporting (4 bits) | FDD, HD-FDD, TDD | Qualcomm
DL quality reporting | CONNECTED | CEModeA and CEModeB | AL < 24, RP = 1 for CE Mode A AL = 24, RP > 1 for CE Mode B AWGN channel, MAC CE based reporting (4 bits) | FDD, HD-FDD, TDD | Qualcomm
MPDCCH improvement | CONNECTED | CEModeA and CEModeB | Verify test improved MPDCCH when out-of-sync is triggered, In non-DRX scenario | FDD, HD-FDD, TDD | Ericsson
Mobility enhancement | IDLE | Normal and enhanced coverage | Test to verify that relaxed serving cell monitoring is fulfulled | FDD, HD-FDD, TDD | Ericsson
Mobility enhancement: cell reselection test | IDLE | Normal and enhanced coverage | Verify the cell reselection requirements when UE performs measurements based on RSS based RSRP | FDD, HD-FDD, TDD | Huawei
Mobility enhancement: measurement accuracy test | Connected | CEModeA, and CEModeB | Verify RSS based RSRP measurement accuracy requirements | FDD, HD-FDD, TDD | Huawei