## Slide 1: WF on Restriction of Rel-15 FR1 SCell activation delay requirement
Qualcomm Incorporated, …
R4-2012240
3GPP TSG-RAN4 Meeting #96-e
Online, 17-28 Aug., 2020
Agenda item: 4.7.3
Document for: Approval

## Slide 2: Background
In RAN4#96e, RAN4 established a common understanding that the current FR1 SCell activation requirements have the following issues.
  ‘TCI indication’ is NOT included in SCell activation procedure.
  Time for ‘L1-RSRP measurement and report’ is NOT included in ‘unknown’ SCell activation requirement
Note that the above observation doesn’t mean that it will always lead to malfunction.

## Slide 3: Proposal
In RAN4#97e, a Rel-15 CR to clarify FR1 SCell activation requirements (8.3.2 of TS38.133) can be further discussed to incorporate following understanding.
  If ‘ssb-PositionInBurst’ indicates only one SSB is being actually transmitted, the current requirement is not expected to create an issue
  If ‘ssb-PositionInBurst’ indicates multiple SSBs and TCI indication is provided in same MAC PDU with SCell activation, the current requirement is not expected to create an issue
  If ‘ssb-PositionInBurst’ indicates multiple SSBs but no TCI indication is provided in the same MAC PDU with SCell activation, FFS on whether the current requirements can be applied
  Other scenarios can be further investigated to determine whether/how to clarify the requirement