## Slide 1: WF on NR-U RRM (Part 1) all agreements in RAN4#96-e in email thread: [96e][206] NR_unlic_RRM_1
Ericsson
3GPP TSG-RAN WG4 Meeting #96-e R4-2012249
Electronic Meeting, 17 – 28 August, 2020
Agenda Items: 7.1.5.1, 7.1.5.3, 7.1.5.4, 7.1.5.5, 7.1.5.6

## Slide 2
Agreements from the 1st round
Agreements from the GTW session
Agreements from the 2nd round

## Slide 3: General
RAN1 LS response on SSB monitoring capabilities
  RAN4 assumption on signaling of UE SSB monitoring capabilities
    In NR-U work, RAN4 assumes that no explicit or signalled UE capabilities will be defined for the number of candidate SS/PBCH block indexes corresponding to the same SS/PBCH block index the UE should monitor in a given discovery burst transmission window (for RRM) or within the set of configured resources (for RLM/CBD/BFD)
  Differentiation between UE in FBE and LBE modes
    No differentiation between UE in FBE and LBE modes in NR-U RRM Core requirements
    Different test case will be defined for UE in FBE and LBE modes in NR-U RRM Performance requirements
  Parameter Q
    Do not further discuss the case when a UE is not provided with the parameter Q (this case does not exist, according to RAN1)

## Slide 4: General (cont.)
RAN1 LS response on SSB monitoring capabilities (cont.)
  Whether to capture the number of candidate SSB positions in NR-U core requirements
    RRM core requirements are defined under assumption what UE monitors the first 2 successive QCL’ed candidate SSB positions (i.e. N1 = N2 = 2)
      FFS if same values apply for cell detection
        Option 1: For cell detection the requirements are defined under assumption that UE monitors at least 1 candidate SSB position in one SSB block burst
        Option 2: Same value applies as for other RRM measurements
      The total number of candidate SSBs indexes and number of cell UE shall monitor remains unchanged

## Slide 5: General (cont.)
NR-U terminology
  Further clarification for “X not available at the UE”
    The term “X not available at the UE” refers to when X is configured by gNB but the first two (FFS for cell detection, see also the previous slide) successive candidate SSB positions for the same SS/PBCH block index within the discovery burst transmission window (for RRM)/the set of configured resources (for RLM/CBD/BFD) are not available at the UE due to DL CCA failures at gNB during the corresponding … period, where
      X shall be replaced depending on the requirement with:
        RLM-RS SSB in RLM requirements,
        BFD-RS SSB in BFD requirements,
        CBD-RS SSB in CBD requirements,
        SSB in L1-RSRP measurement requirements,
        SMTC in measurement requirements other than RSSI requirements and L1-RSRP,
        SSB in TCI state switching requirements,
        SMTC in SCell activation, PSCell addition/release, HO, RRC re-establishment, RRC release with redirection requirements, etc.
    and … shall be replaced with what is appropriate:
        evaluation,
        detection,
        identification,
        activation, etc.

## Slide 6: General (cont.)
NR-U terminology (cont.)
  Further clarification for “Y unavailable for transmission”
    For each NR-U requirement using the term “Y unavailable for transmission”, add a clarification in the introduction, general part or in the beginning of the NR-U requirement according to the format:
      The term “Y unavailable for transmission” refers to when the Y is configured by gNB but not transmitted by the UE during the corresponding period due to UL CCA failure at the UE, where
      Y shall be replaced depending on the requirement with: PRACH, HARQ, etc.
  Ericsson volunteers to bring a CR in RAN4#97-e (October) to align the NR-U terminology among different NR-U requirements

## Slide 7: Handover
The delay uncertainty (TIU) due to RACH transmission in HO
  The delay uncertainty (TIU) due to RACH transmission in HO (same approach is proposed also for RRC re-establishment and RRC release with redirection) is defined as follows:
TIU = (1+ L3)*TSSB,RO + 10 ms
where:
    TSSB,RO is the SSB to PRACH occasion association period as defined on TS 38.213,
    L3 is the number of consecutive SSB to PRACH occasion association periods during which no PRACH occasion is available for PRACH transmission due to UL CCA failure

## Slide 8: RRC Re-Establishment
Delay uncertainty (TPRACH_CCA) due to RACH transmission in RRC re-establishment
  The delay uncertainty (TPRACH_CCA) due to RACH transmission in RRC re-establishment (same approach is proposed also in HO and RRC release with redirection) is defined as follows:
TPRACH_CCA = (1+ K3)*TSSB,RO + 10 ms
where:
    TSSB,RO is the SSB to PRACH occasion association period as defined on TS 38.213,
    K3 is the number of consecutive SSB to PRACH occasion association periods during which no PRACH occasion is available for PRACH transmission due to UL CCA failure
Carriers to identify
  The requirements for the RRC re-establishment delay shall consider the time for identification on carriers with and without CCA

## Slide 9: RRC Connection Release with Redirection
Delay uncertainty (TRACH_CCA) due to RACH transmission in RRC connection release with redirection
  The delay uncertainty (TRACH_CCA) due to RACH transmission in RRC connection release with redirection (same approach is proposed also in HO and RRC re-establishment) is defined as follows:
TRACH_CCA = (1+ L2)*TSSB,RO + 10 ms
where:
    TSSB,RO is the SSB to PRACH occasion association period as defined on TS 38.213,
    L2 is the number of consecutive SSB to PRACH occasion association periods during which no PRACH occasion is available for PRACH transmission due to UL CCA failure
Delay uncertainty (TRACH_CCA) due to RACH transmission in RRC connection release with redirection, with Type 2C UL channel access procedure
  The following is also included in the RACH delay uncertainty in RRC release with redirection:
  L2 = 0 for Type 2C UL channel access procedure as defined in TS 37.213

## Slide 10: SCell Activation
Interruption window length
  For a single interruption, interruption window length at SCell activation does not depend on LBT failures
Interruption window starting point
  The starting point of an interruption window on PCell or any activated SCell in MCG for NR standalone mode, or on PSCell or any activated SCell in SCG for EN-DC mode, shall not occur before slot n+1+ and not occur after slot n+1+ , where TX is:
  TFirstSSB + (L1)* Trs, for known SCell activation when SCell measurement cycle is equal to, or smaller than, 160ms;
  TFirstSSB_MAX + L2,1* TSMTC_MAX for known SCell activation when SCell measurement cycle is greater than 160ms;
  TFirstSSB_MAX + L3,1* TSMTC_MAX for unknown SCell activation

## Slide 11: SCell Activation (cont.)
Multiple interruption windows
  For intra-band CA, while the SCell being activated is unknown or known with measurement cycle >160ms, up to (1+L) interruption windows are allowed during SCell activation, where L is the number of occasions that at least one SSB from SCells already activated or SCell being activated in the same band is not available before the first successful SSB transmissions subject to TSMTC_max
  For inter-band CA: FFS
  Inter-band CA:
    Option 1: for inter-band CA, the interruption is the same as for intra-band case
    Option 2: for inter-band CA, the interruption is not the same as for intra-band case, while multiple interruptions are still needed
    Option 3: for inter-band CA, the interruption is not the same as for intra-band case and a single interruption applies

## Slide 12: SCell Activation (cont.)
Extended THARQ for UEs with/without enhancedDynamicHARQ-codebook-r16 and oneShotHARQ-feedback-r16 capabilities
  The related issues have been discussed a lot in previous meetings. The extension applies regardless the capabilities
Conditions for CSI reporting during SCell activation
  When P/SP-CSI-RS is used for CSI report during the SCell activation, it is assumed one of the RRC parameters CO-DurationPerCell-r16, SlotFormatIndicator, and CSI-RS-ValidationWith-DCI-r16 is configured for a UE and the UE supports the corresponding capability, except for the cases when the UE cancels the reception [TS 38.213]

## Slide 13: SCell Activation (cont.)
SCell activation requirements with respect to configuring sCellDeactivationTimer
  Do the SCell activation requirements apply for the case when sCellDeactivationTimer is not configured?
    Option 1: The SCell activation requirements for NR-U do not apply when the sCellDeactivationTimer is not configured.
    Option 2: The sCell activation delay requirement applies regardless of the sCellDeactivationTimer being configured or not.
  Do the SCell deactivation requirements apply for the case when sCellDeactivationTimer is not configured?
    Option 1: The SCell deactivation requirements for NR-U do not apply when the sCellDeactivationTimer is not configured.
    Option 2: No new specification is needed for SCell deactivation requirements when SCellDeactivationTimer is not configured.
  UE behaviour with respect to a configured sCellDeactivationTimer in SCell activation/deactivation
    Option 1: If RAN4 is to define requirements only when sCellDeactivationTimer is configured, necessary clarification is needed that UE shall not stop sCellDeactivationTimer before UE successfully transmits the HARQ feedback for the deactivation command.
    Option 2: No such clarification is needed, even if the requirements apply only when sCellDeactivationTimer is configured

## Slide 14: Active TCI State Switching
UE behavior and requirements for RRC-based active TCI state switching
  Do not specify UE behaviour for LRRC,known,max, L1RRC,unknown,max, and L2RRC,unknown,max , but the requirements shall apply up to LRRC,known,max, L1RRC,unknown,max, and L2RRC,unknown,max
UE behavior and requirements for MAC-CE based active TCI state switching
  Do not specify UE behaviour for LMAC,known,max, L1MAC,unknown,max, and L2MAC,unknown,max , but the requirements shall apply up to LMAC,known,max, L1MAC,unknown,max, and L2MAC,unknown,max