## Slide 1: 3GPP TSG-RAN WG4 Meeting #96-e Electronic Meeting, 17-28 August, 2020
Intel
WF on requirements for PRS-RSRP measurements
R4-2012263

## Slide 2: Measurement period for PRS RSRP
When configured with UE Rx-Tx time difference, PRS-RSRP measurement period requirements can be same as that of UE Rx-Tx time difference measurement
When configured with PRS-RSTD, PRS-RSRP measurement period requirements can be same as that of RSTD measurement
When not configured with either UE Rx-Tx or RSTD, measurement period requirements of RSTD can be reused for PRS-RSRP measurement.
Note: The agreements above are valid for the case when the number of samples for PRS-RSRP measurements = [4]. Agreement can be revisited if more samples are needed for PRS-RSRP measurements.

## Slide 3: Measurement capability
RAN4 will refer to RAN2 positioning capabilities in RAN4 requirements
RAN4 will not separately define measurement capability in terms of number of PRS layers, TRPs, resource sets and resources that UE shall be able to measure

## Slide 4: Side condition
For DL-AoD, the side condition of PRS RSRP can be specified
  Option 1: Serving cell/TRP side conditions need to be specified (in addition to neighbour cells) as
    Option 1-1: -6 dB
    Option 1-2. -3 dB
  Option 2: Reference cell/TRPs side conditions need to be specified (in addition to neighbour cells)
    Same as that for the reference cell in PRS-RSTD
  Option 3 :for neighbor cell/TRPs ONLY.
  Option 4: serving cell/TRP and reference cell/TRP need to be specified (in addition to neighbour cells)

## Slide 5: Measurement accuracy requirements for PRS RSRP
Number of samples for PRS RSRP measurement accuracy:
  FFS, consider that PRS occasion is not defined by RAN4
Types of requirements
  Option 1: Define absolute accuracy requirements ONLY
  Option 2: Define relative accuracy requirements ONLY
  Option 3: Define both absolute and relative accuracy requirements

## Slide 6: PRS RSRP measurement under cell change
When configured together with UE Rx-Tx, the UE behavior rules for PRS-RSRP are the same as for these for UE Rx-Tx (agreed in [R4-1915854])
When configured together with RSTD, the UE behavior rules for PRS-RSPR measurement under cell change are the same as for RSTD (the rules for RSTD were agreed in [R4-1915854]):
  The UE shall continue RSTD measurement after each serving cell change for:
    intra-frequency handover,
    inter-frequency handover.
When not configured together with either UE Rx-Tx or RSTD, the UE behavior rules for PRS-RSPR measurement under cell change are the same as for RSTD (the rules for RSTD were agreed in [R4-1915854]).