## Slide 1: WF on R16 NR RRM enhancements - BWP switching on multiple CCs
Intel Corporation
3GPP TSG-RAN WG4 Meeting #96-e R4-2012271 Electronic Meeting, 17-28, Aug. , 2020

## Slide 2: Simultaneous BWP switching on multiple CCs (1)
Delay requirements for DCI/timer based BWP switch
; D is incremental delay for BWP switch processing on additional CCs
D:
  Agreement in GTW session : adding D=200us for type 2 UE capability
- Definition of N:
  Agreement in GTW session : For UE which is capable of per-FR gap, and no BWP switch involves SCS change, N is the number of simultaneous BWP switching on CCs within the same frequency range; For UE which is not capable of per-FR gap, or the BWP switches on multiple CCs involves SCS changing, N is the number of simultaneous BWP switching on both FR.

## Slide 3: Simultaneous BWP switching on multiple CCs (2)
Delay requirements for RRC based BWP switch
;
Agreement in GTW session:
For type 1 UE, DRRC = 0ms; For type 2 UE, DRRC = D

## Slide 4: Partial Overlap BWP switching on multiple CCs (1)
Delay requirement for Timer based BWP switch
Agreement in GTW session:
if UE is capable of per-FR gap and the timer based BWP switch happens in two frequency range, UE handles timer-based BWP switch sequentially
TMultipleBWPswitchDelayTotal = TDelay + TMultipleBWPswitchDelay
Where:
TDelay is the time required to complete the ongoing timer-based BWP switching on other CCs.
TMultipleBWPswitchDelay is the timer-based BWP switch delay on current single CC defined in clause 8.6.2 or simultaneously triggered on multiple CCs defined in clause 8.6.2B.1.

## Slide 5: Partial Overlap BWP switching on multiple CCs (2)
Delay requirement for RRC based BWP switch
Agreement in GTW session:
  Additional waiting time for RRC based BWP switch is upper bounded by the multiple BWP switch time in CG1.
  Note: UE is not precluded to process the 2nd RRC message before the first RRC based BWP switch completes and this is up to UE implementation (no spec impact)