## Slide 1
3GPP TSG-RAN WG4 Meeting #96-e R4-2012290
Electronic Meeting, Aug. 17 – 28, 2020
Agenda Item: 7.14.1.3 and 7.14.1.4
WF on CSI-RS L3 measurement capability
Apple

## Slide 2: Issue 1-1-1: Whether CSI-RS and SSB for mobility configured in the same MO are counted as 2 layers
  SSB and CSI-RS for mobility configured in the same MO should be considered as 2 layers.
    FFS the condition to merge SSB and CSI-RS into one frequency layer in future release, if agreed.

## Slide 3: Issue 1-1-2: Whether multiple MOs can be counted as one frequency layer
  Only one MO corresponding to one frequency layer is considered in R16 for requirements definition
  Send LS to RAN1 and RAN2 and ask to increase the number of configurable CSI-RS resources per MO from 96 to 192

## Slide 4: Issue 1-1-3: How to count SSB frequency layers
  Number of SSB layers should include SSB for mobility and that as associatedSSB for CSI-RS mobility；
  the ssbfrequency is counted only once if the ssbfrequency for mobility and associated SSB are the same, or ssbfrequency and SMTC in multiple MOs are the same.

## Slide 5: Issue 1-1-4: Number of frequency layers to be monitored
  UE shall be able to measure at least
    1 SSB intra-frequency layer and 1 CSI-RS intra-frequency layer per serving cell
    7 SSB inter-frequency layers and 7 CSI-RS inter-frequency layers
    8 NR inter-frequency layers including SSB and CSI-RS in total,
    13 NR inter-frequency and inter-RAT layers in total

## Slide 6: Issue 1-2-1: Number of cells to be monitored
  The cells to be monitored based on CSI-RS can be the same set or a subset of the cells monitored based on SSB.

## Slide 7: Issue 1-3-1: Number of CSI-RS resource/beams to be monitored
The number of CSI-RS resource/beams to be monitored can be at least
  For intra-frequency measurement for FR1: 32
  For intra-frequency measurement for FR2: 32
  For inter-frequency measurement for FR1: 14
  For inter-frequency measurement for FR2: 24

## Slide 8: Issue 1-3-2: Neighbor cell CSI-RS resource measurement in FR2
For each FR2 band, UE is required to measure neighbour cell CSI-RS on one CSI-RS layer, whose associated SSB should be on the same SSB layer as the one where UE is required to measure neighbour cell SSB

## Slide 9: Issue 1-4-1: Whether to introduce minimum separation between two slots
With time domain restriction introduced for CSI-RS resource configurations, it is agreed not to introduce UE capability for minimum separation between two slots in Rel-16
  It is not a typical configuration that the last CSI-RS symbol in slot n is consecutive with the first CSI-RS symbol in slot n+1.
  The measurement requirements apply provided that the maximal number of CSI-RS resources in any duration that equal to the length of a slot is no larger than maxNumberCSI-RS-RRM-RS-SINR
  RRM test cases are to be defined with configurations where CSI-RS resources in any two consecutive slots are separated by at least 7 symbols

## Slide 10: Issue 2-5-1: New UE capability on the simultaneous reception of CSI-RS and SSB/Data
  On simultaneous reception of CSI-RS and SSB (from the serving or neighbor cells)
    Do not introduce new UE capability on the simultaneous reception of CSI-RS and SSB
    Core/performance requirements in TS38.133 are specified based on the assumption that UE does not support simultaneous reception of CSI-RS and SSB
  Remove “FG[12-1]: UE capability on the simultaneous reception of CSI-RS of neighbor cell and SSB of serving cell”
  Clarify in TS38.133 that UE behavior is not specified if 3 mixed numerologies are configured simultaneously.

## Slide 11: Issue 2-6-1: Searcher assumption for CSI-RS based measurement
  The minimum RRM core and performance requirements in TS38.133 should be specified based on the assumption that CSI-RS based L3 measurement and SSB based L3 cell detection/measurement share two measurement engines, a.k.a. searcher in SSB discussion.
    For measurement outside MG, up to two frequency layers, including SSB based intra-frequency layer, SSB based inter-frequency without gap and CSI-RS based intra-frequency, per time instance can be measured.
    The related RRM requirements should not preclude the scenarios where UE implements dedicated searchers for CSI-RS and/or more than two searchers

## Slide 12: Issue 2-6-2: CSSF outside of gap (for intra-frequency CSI-RS based measurement)
  CSSF outside of gap is specified based on the assumption that CSI-RS and SSB based measurement share two measurement engines, a.k.a. searcher in SSB discussion.
  Note：Number of SSB layers should include SSB for mobility and that as associatedSSB for CSI-RS mobility；
    the ssbfrequency is counted only once if the ssbfrequency for mobility and associated SSB are the same, or ssbfrequency and SMTC in multiple MOs are the same.

## Slide 13: Issue 2-6-3: CSSF within gap
  Define the CSSF within gap assuming CSI-RS and SSB should be considered as different frequency layers.
  When per-UE gap is configured, It is a general assumption that only single frequency layer, e.g. CSI-RS or SSB frequency layer, can be measured within each gap instance
  When per-FR gap is configured, It is a general assumption that only single frequency layer, e.g. CSI-RS or SSB frequency layer, can be measured within each gap instance per FR
  For intra-frequency CSI-RS resources:
    If intra-frequency CSI-RS resource is partially overlapped with MG, no measurement within gap is assumed
    If intra-frequency CSI-RS resource is fully overlapped with MG, CSSFwithin_gap,i applies.
  For inter-frequency CSI-RS resources:
    CSSFwithin_gap,i applies.
  Note：Number of SSB layers should include SSB for mobility and that as associatedSSB for CSI-RS mobility；
    the ssbfrequency is counted only once if the ssbfrequency for mobility and associated SSB are the same, or ssbfrequency and SMTC in multiple MOs are the same.