## Slide 1: WF on impact of NR positioning measurements on RRM
Ericsson
3GPP TSG-RAN WG4 Meeting # 96-e
Electronic Meeting, August 17-28, 2020
Agenda: 7.7
R4-2012298

## Slide 2: New MG Patterns
Introduce following 2 new MG patterns:
New MG patterns can only be configured when the UE is configured with PRS measurements.
MGL (ms) | MGRP (ms)
10 | 80
20 | 160

## Slide 3: Applicability of new MG Patterns
New MG patterns are applicable for PRS and NR/LTE RRM measurements i.e. new gaps are not shared between PRS and 2G/3G RRM measurements.

## Slide 4: New MG Pattern Capabilities
New MG patterns are defined as per-UE capability.

## Slide 5: New MG sharing between RRM and PRS measurements
Existing CSSF is used for sharing new MG pattern between NR/LTE RRM and PRS measurements.

## Slide 6: SRS transmission during DRX inactive
Periodic and semi-persistent positioning SRS transmissions during DRX inactive time are NOT allowed in Rel-16.