## Slide 1: WF on the introducing the new testing methodology on EDT testing
Nokia, Nokia Shanghai Bell
R4-2012567
3GPP TSG-RAN WG4 Meeting #96-e
Electronic Meeting, August 17th – 28th 2020

## Slide 2: References
[1] R4-2009048 WF on modifying the ED threshold, Nokia, Nokia Shanghai Bell
[2] R4-2010731 On energy detection threshold for LAA and eLAA in conformance specification Nokia, Nokia Shanghai Bell
[3] R4-2010732 CR to 37.107 with correction of EDT level Rel-15, Nokia, Nokia Shanghai Bell
[4] R4-2010733 CR to 37.107 with correction of EDT level Rel-16, Nokia, Nokia Shanghai Bell
[5] R4-2010734 CR to 36.141 with correction of EDT level Rel-13, Nokia, Nokia Shanghai Bell
[6] R4-2010735 CR to 36.141 with correction of EDT level Rel-14, Nokia, Nokia Shanghai Bell
[7] R4-2010736 CR to 36.104 with correction of EDT level Rel-13, Nokia, Nokia Shanghai Bell
[8] R4-2010737 CR to 36.104 with correction of EDT level Rel-14, Nokia, Nokia Shanghai Bell

## Slide 3: Background (1/3)
RAN4#96e continued discussion on energy detection threshold (EDT) for LAA/eLAA in conformance specification. For this meeting some contributions and CRs were submitted in [2-8]. Previous RAN4#95e meeting outcome was captured in WF on modifying the ED threshold [1].
The issue is that performance part of channel access procedure test, that is described in TS 37.107 in subclause 6.1.4.2 point 6) the interfering signal shall be at the fixed level of (-72 dBm + 4 dB)/20MHz:
The 3GPP ED threshold test is not testing the eNB’s transmit power or EIRP, but determines the transmit power of the interferer in the test setup. With fixed level of (-72 dBm + 4 dB)/20MHz specified in TS 37.107 it is not possible for some cases to use real interferer level that is allowed by regulatory, as this level may be different then -72 dBm.

## Slide 4: Background (2/3)
LAA/eLAA test procedure for energy detection threshold is describe in TS 37.213 v16.0.0 in subclause 4.1.5 with following formula for Xthresh_max :
:

## Slide 5: Background (3/3)
:
Original proposal in [2] was to reuse directly formula from TS 37.213 specification (presented on slide 4) into conformance specification TS 37.107.
However, to simplify specification and to ensure to not increase numer of conformance tests, another solution present on next slide is proposed. With such proposal there should not be any additional effort for conformance test for vendors that declare existing now in specification testing with -72dBm +4dB.
For specific cases testing with other level declared by vendor could be done as well to satisfied some regulatory requirements.

## Slide 6: Way forward
  Following modification is proposed to allow usage of declared by vendor the transmit power of the interferer in the test setup:
    X is FFS
      Option 1: X= 72 +4dB + MAX(0, 23 – Total Conducted Tx Power [in dBm]) 1
      Option 2: Y X together with NOTE 1: The specific value Y X is declared by the vendor.
      Option 3: other value not excluded
  To correct EDT level test and to agree changes:
    From Rel-15 onwards, consequently update should be introduced only to TS 37.107 (Rel-15 and Rel-16)
:
Table 6.1.5-1: Channel access test requirements for PDSCH (from TS 37.107)
Parameter | Unit | Value
LBT measurement bandwidth | MHz | 10, 20
Maximum energy detection threshold | dBm/20MHz dBm/10MHz | -72 + 4dB Or [X] + 4 dB - -75 + 4dB
Maximum channel occupancy time | ms | 8
NOTE 1: The specific value is declared by the vendor. |  |