## Slide 1: WF on selecting CLTA height
Huawei
R4-2012589
3GPP TSG-RAN WG4 Meeting # 96-eis
Electronic Meeting, 17 – 28 Aug., 2020

## Slide 2: Background
In the last meeting [R4-2008740) the following was agreed was agreed:
  Proposal 1: The CLTA description is modified to allow a practical implementation when different operating bands require vastly different height antennas.

## Slide 3: Proposals (1 of 2)
There have been a number of proposals how to limit the CLTA height:
Huawei (R4-2011301)
  The half-power vertical beam width of the CLTA equals the narrowest declared (D.3) vertical beamwidth ±3° Or Test object vertical radiating length ±30%
CATT (R4-2009779)
  The half-power vertical beam width of the out of band CLTA equals .
  Where,
  h is the test object vertical radiating length in meter.
  θ is the narrowest declared (D.3) vertical beam width of test object antenna.
  foperatingband is the centre frequency of operating band of test object antenna.
  fcoLocatedband is the centre frequency of co-located band.

## Slide 4: Proposals (2 of 2)
Ericsson (R4-2009967)
  The CLTA length shall be matched to the EUT length for out-of-band co-location testing
Nokia (R4-2011391)
  The half-power vertical beam width of the CLTA equals
    BeWθ/X * foperating/fco-located if foperating > fco-located
    or
    X*BeWθ * foperating/fco-located if foperating > fco-located , or
  X is TBD.

## Slide 5: Way Forward
CLTA is modified based on one of the following:
Option 1
(with possible
enhancements if
necessary)
Parameter | In-band CLTA | Out-of-band CLTAs
Vertical radiating dimension (h) | Test object vertical radiating length ±30% | Test object vertical radiating length ±30% (Note 2)
Horizontal beam width | 65° ± 10° | 65° ± 10°
Vertical beam width | N/A | The half-power vertical beam width of the CLTA equals the narrowest declared (D.3) vertical beamwidth ±3° (Note 2)
Polarization | Match | Match to in-band
Conducted interface return loss | > 10 dB | > 10 dB
NOTE 1: If a multi-column or multi-band antenna is used the column closest to the NR BS shall be selected while other columns are terminated during testing. NOTE 2: Either vertical radiating dimension or beam width definition may be used depending on the availability of CLTA |  | 
Option 2 (with possible enhancements if necessary)
  The half-power vertical beam width of the out of band CLTA equals
  Where,
  h is the test object vertical radiating length in meter. The value 2.5m may be further discussed.
  θ is the narrowest declared (D.3) vertical beam width of test object antenna.
  foperatingband is the centre frequency of operating band of test object antenna.
  fcoLocatedband is the centre frequency of co-located band.