## Slide 1: WF on the measurement interval and observation time for frequency/time correction for 2.5kHz and 0.37kHz
ZTE,…
R4-2012604
3GPP TSG-RAN WG4 #96e
17th Aug. - 28th Aug. 2020

## Slide 2: Background
In 36.211, it states:
For subframes using Δf=2.5 kHz, , or , subframe is defined as two slots, and , of length each.
For subframes using , subframe is defined as one slot, , of length .
For transmissions using Δf=1⁄((82944T_"s" ) )≈0.37 "kHz" , a slot has a length of 92160T_"s" =3" ms" . There are 13 slots, numbered in increasing order from 0 to 12, in a 40 ms period starting at n_"f" " mod " 4=0 with slot 0 starting at 30720T_"s" in the 40 ms period

## Slide 3: Agreement for 2.5KHz SCS
Sub-topic 1-1:The basic unit of EVM measurement and measurement intervals for EVM measurement
· The basic unit of EVM measurement for 2.5KHz
o 1ms
· measurement intervals for 2.5KHz
o 10ms
Sub-topic 1-2 Observation period for freq and timing error estimation
· Observation period for 2.5KHz
o 1ms
Sub-topic 1-3 EVM window length
· EVM window for 2.5KHz
Table E.5.1-2c EVM window length for extended CP for 2.5 kHz sub-carrier spacing
Channel Bandwidth [MHz] | FFT size | Cyclic prefix in FFT samples | EVM window length W | Ratio of W to total CP (Note 1)[%]
1.4 | 768 | 192 | 168 | 87.5
3 | 1536 | 384 | 348 | 90.6
5 | 3072 | 768 | 746 | 96.9
10 | 6144 | 1536 | 1500 | 97.7
15 | 9216 | 2304 | 2268 | 98.4
20 | 12288 | 3072 | 3024 | 98.4
Note 1: These percentages are informative. |  |  |  | 

## Slide 4: WF for 0.37KHz SCS
Sub-topic 1-1:The basic unit of EVM measurement and measurement intervals for EVM measurement
· The basic unit of EVM measurement for 0.37KHz
o Option 1:3ms [Huawei, ZTE]
o Option 2: 6ms [Nokia]
agreement: option 1
· measurement intervals for 0.37KHz
o 10ms [Nokia, ZTE]
o Other [Huawei]
agreement: option 1
Sub-topic 1-2 Observation period for freq and timing error estimation
· Observation period for 0.37KHz
o 6ms [Nokia, ZTE]
o 3ms [Huawei]
agreement: option 1
Sub-topic 1-3 EVM window length
Table E.5.1-2d EVM window length for extended CP for 0.37 kHz sub-carrier spacing
Channel Bandwidth [MHz] | FFT size | Cyclic prefix in FFT samples | EVM window length W | Ratio of W to total CP (Note 1)[%]
1.4 | 5184 | 576 | 504 | 87.5
3 | 10368 | 1152 | 1044 | 90.6
5 | 20736 | 2302 | 2230 | 96.9
10 | 41472 | 4604 | 4498 | 97.7
15 | 62208 | 6906 | 6796 | 98.4
20 | 82944 | 9208 | 9060 | 98.4
Note 1: These percentages are informative. |  |  |  | 

## Slide 5: WF for other
Sub-topic 1-4 modifications on 1.25KHz in TS36.104 spec.
o Yes
o No
agreement: Yes,
Reason: Observation period 1ms for freq and timing error estimation for 1.25KHz is not correct.
Sub-topic 1-5 UE doesn’t have to support all of the SCS, if UE support MBMS. (The clarification is needed)
o Yes
o No
Recommended agreement: No
Reason: The existing spec don't the implication that UE supporting MBMS needs to support all of SCSs, if needed, clarification could be done in the next meeting.

## Slide 6: Agreement
· UE doesn’t have to support all of the SCS, if UE support LTE MBMS. RAN4 will clarify it in the specification from Rel-14.

## Slide 7: References:
  [1]R4-2010730,Discussion on EVM measurement details for 2.5kHz and 0.37kHz SCSs, Nokia
  [2]R4-2010943,Impacts on BS RF requirement of new introduced numerology, ZTE Corporation
  [3]R4-2010944,CR to 36.104: Introduction of LTE based 5G terrestrial broadcast numerologies
  [4]R4-2010945,CR to 36.101: Introduction of LTE based 5G terrestrial broadcast numerologies