## Slide 1: Way Forward on NR-U UE demodulation requirements
Qualcomm
3GPP TSG-RAN4 Meeting #96-e
August 17 – 28, 2020
Agenda Item: 7.1.6.1/2
Tdoc Num: R4-2012610

## Slide 2: Test Scope
Semi-static Channel Access Devices v/s Dynamic Channel Access Devices
Prioritize test cases agnostic to semi-static and dynamic channel access devices.
FFS: Define additional test cases dedicated to FBE/LBE devices.

## Slide 3: Test Scope
Prioritize tests with fixed COT duration
  Option 1: Yes
  Option 2: No
Prioritize tests with fixed DRS window duration
  Option 1: Yes
  Option 2: No
FFS: Deprioritize tests with COT duration larger than SMTC duration for dynamic channel access devices

## Slide 4: Test Scope
Test Scenarios
  Option 1: Only Scenario A
  Option 2: Only Scenario C
  Option 3: Both Scenario A and Scenario C
For reference:
  Scenario A (Carrier aggregation between licensed band NR (PCell) and NR-U (SCell))
  Scenario C (Stand-alone NR-U (PCell))

## Slide 5: Test Scope
PDCCH demodulation requirements covering DCI 2-0
  Option 1: Yes
  Option 1a: Yes, if the payload size is aligned with scenarios defined for PDSCH
  Option 2: No
  Option 3: No, cover it together with PDSCH requirements

## Slide 6: Simulation Assumptions
Use LTE LAA PDSCH requirements as starting point.
Use Burst Transmission Model for LAA (36.101-4, B.8) as a starting point.
Use 20 MHz LBT BW.

## Slide 7: Simulation Assumptions
Model LBT Failure
  Option 1: Yes
  Option 2: No
SSB LBT Failure
  Option 1: Yes
  Option 2: No
Do not define tests with sub-band LBT failure.

## Slide 8: Simulation Assumptions
COT Duration
  Option 1: 1ms
  Other options not precluded;
DRS Window Duration
  Option 1: 1ms;
  Other options not precluded;
Q factor for SSB
  Option 1: = 1

## Slide 9: Simulation Assumptions
PDSCH Type
  Option 1: Type A
  Option 2: Type B
  Option 3: Type A for full slot and Type B for partial allocation
Do not multiplex SSB and Data.

## Slide 10: Simulation Assumptions
PDSCH Type B duration in symbols (if agreed to use PDSCH Type B)
  Option 1: 2 or 7
  Option 2: Any random value
  Option 3: Any fixed value excluding (2,4,7)
PDSCH Type B starting position (if agreed to use PDSCH Type B)
  Option 1: Within first 3 symbols
  Option 2: Any possible symbols after the success of LBT
  Option 3: Within first 7 symbols