## Slide 1: Way Forward on NR-U BS demodulation requirements
Ericsson
3GPP TSG-RAN WG4 Meeting #96-e
Electronic Meeting, 17 - 28 August 2020
Agenda: 7.1.6.1
R4-2012611
Document for: Approval

## Slide 2: Background
Agreed email discussion summary
R4-2012542 Email discussion summary for [96e][328] NR_unlic_Demod

## Slide 3: General

## Slide 4: Test scope: test Scenario
Test Scenarios
  Option 1
    Scenario A (Carrier aggregation between licensed band NR (PCell) and NR-U (SCell))
    Scenario B (Dual connectivity between licensed band LTE (PCell) and NR-U (PSCell))
    Scenario C (Stand-alone NR-U (PCell))
  Option 2
    Scenario C (Stand-alone NR-U (PCell))
  Option 3
    Define demodulation requirements only for Scenario A (LAA), but these requirements can be applied for other scenarios. Meanwhile, only define requirements for single carrier and don’t define requirements for intra-band CA.

## Slide 5: Test scope: wideband operation mode
Define requirements for Wideband Operation 2.
  Note: The Wideband Operation 2 modes are defined in R4-1911610, R4-1905206, where
    Mode 1 related to a single Wideband carrier, where the UE transmits only if all CCA is successful in all of the carrier’s LBT subbands
    Mode 2 relates to a single Wideband carrier, where the UE transmits only if CCA is successful in all contiguous LBT subbands where it is scheduled
Consideration for Wideband Operation 1
  Option 1: Do not define requirements for Wideband Operation 1
  Option 2: Define requirements for Wideband Operation with applicability rule between Operation 1 and Operation 2
  FFS

## Slide 6: Test scope: LBT failure model
Whether to model LBT failure in UL demodulation requirements
  Don’t model LBT failure in UL demodulation requirements
Whether to consider sub-band LBT failure
  Do not consider sub-band LBT failure

## Slide 7: Test scope: Intra-cell guard band
Whether to consider intra-cell guard band in wideband operation 2 (if agreed to define requirements for wideband operation 2)
  Don’t consider intra-cell guard band in wideband operation 2.
  Define requirements for the test cases scheduling intra-cell guard band PRBs which are between continual successful CCA LBT bands for UL transmission.

## Slide 8: Simulation assmptions
Bandwidth for PUSCH/PUCCH
  Define requirements for 20MHz
  FFS for 60MHz.
Duplex and SCS
  TDD 15kHz and 30kHz

## Slide 9: PUSCH

## Slide 10: Test scope
Define requirements for PRB-Interlaced PUSCH Resource Allocation
Whether to define PUSCH requirements for NR-U 2-step RACH MsgA
  Do not define additional requirements for NR-U 2-step RACH MsgA
Whether to define PUSCH requirements for UL multi TTI PUSCH scheduling
  Do not define requirements for UL multi-TTI PUSCH scheduling
Whether to define UCI multiplexed on PUSCH performance requirements
  Option 1: Yes
    Option 1a: Introduce the CG-UCI multiplexing on PUSCH performance requirements
  Option 2: No
  FFS

## Slide 11: Simulation assumptions
Number of interlaces for PRB-interlaced PUSCH Resource Allocation
  Option 1: Single interlace
  Option 2: More than 1 interlace
  FFS

## Slide 12: PUCCH

## Slide 13: Test scope and Simulation assumptions
Define requirements for PRB-Interlaced PUCCH Resource Allocation
PUCCH enhance format
  Option 1: Format 0/1/2/3
  Option 2: Format 0/2
  FFS.
Number of interlaces for PRB-interlaced PUCCH Resource Allocation
  Option 1: Single Interlace
  Option 2: 2 interlaces.
    Not applicable to all PUCCH formats;
  FFS

## Slide 14: PRACH

## Slide 15: Test scope and simulation configuration
Whether to define requirements for Wideband PRACH
  Define requirements for wideband PRACH
PRACH format
  FFS

## Slide 16: SRS

## Slide 17: Test scope
Whether to define SRS performance requirements
  Do not define requirements for SRS