## Slide 1: WF on IAB-MT Pcmax, power control and dynamic range
CATT
3GPP TSG-RAN WG4 Meeting # 96-e Electronic Meeting, 17-28 Aug., 2020
R4-2012616

## Slide 2: Background
The following contributions were provided and discussed in RAN4#96e
  R4-2010111, Discussion on IAB-MT Pcmax, CMCC
  R4-2010147, Discussion on remaining issues for IAB-MT Tx power related requirements, Samsung
  R4-2010293, TP to TR 38.809 Completing IAB-MT power related requirements, Nokia, Nokia Shanghai Bell
  R4-2010724, TP to TS 38.174: Output power requirements, Nokia, Nokia Shanghai Bell
  R4-2010950, Further discussion on IAB-MT power requirement, ZTE Corporation
  R4-2011032, IAB-MT maximum output power for FR1, Ericsson
  R4-2011293, TP to TS 38.174 -IAB TX dynamic range, Huawei

## Slide 3: LA IAB-MT MOP and scaling factor agreements
MOP for LA IAB-MT type 1-H: 24 dBm per TAB connector
MOP for LA IAB-MT type 1-O: 24 + 10*log10(NTXU,counted)
Scaling factor for LA IAB-MT type 1-H: NTXU,counted = min(NTXU,active , 8×Ncells)
Scaling factor for LA IAB-MT type 1-O: NTXU,counted = min(NTXU,active , 8×Ncells)
  Note: Applied the same method for Tx emission and Rx emission as well

## Slide 4: Pcmax agreements
The following factors are not included in the Pcmax definition.
  PowerClass, ΔPPowerClass, MPR/A-MPR, Pemax, and Interband CA, SUL and SRS related.
Pcmax definition:
  Option 1: Pcmax = Pdeclared
    Pdeclared includes the declared back off power.
      Further work on the definition of Pdeclared in TP R4-2012618.
    FFS whether accuracy needed or not, if needed, it can be referred to the existing specified values ; further discuss this in conformance phase.
    Pdeclared is EIRP based for IAB-MT type 1-H, IAB-MT type 1-O and 2-O
    Applied for IAB-MT class: for both local-area IAB-MT and wide-area IAB_MT
    Pcmax is only a definition, not a requirement to be tested.

## Slide 5: Power control agreements
Power control requirements are not defined for WA IAB-MT.
Absolute power tolerance is not defined for LA IAB-MT.
Relative power tolerance for LA IAB-MT
  Further work on TP R4-2012618 with the requirements with [ ]/values as TBD
  These values can be further discussed and modified in conformance phase if needed
Aggregated power tolerance for LA IAB-MT
  Include the requirements in the core specification
  Further work on TP R4-2012618 with the requirements with [ ] /values as TBD
  FFS whether need to have test cases which can be further discussed in conformance phase considering test tolerance and dynamic range requirements
  Further discuss the non-contiguous transmissions time period value [21ms] in response to 0 dB commands

## Slide 6: PHR agreements
PHR mapping will be discussed in RRM session.
  If there’re some related RF issues, they can be discussed in the maintenance stage.

## Slide 7: Dynamic range agreements
Both X and Y will be captured in the core spec, the final wording for the side condition is captured in TP R4-2012621.