## Slide 1: WF on remaining issue on Reference sensitivity and FRC for IAB-MT
Huawei
DRAFT R4-2012627
3GPP TSG-RAN WG4 Meeting # 96-e
Electronic Meeting, 17 – 28 Aug., 2020

## Slide 2: Agreements (From GTW session)
Issue 1-1: SNR for REFSENS (IAB-MT)
  Agreement: Using SNR =-1 dB for IAB_MT sensitivity.
Issue 1-2-1: FRC-necessity on 15 kHz SCS in FR1
  Agreement: Exclude 15kHz SCS for IAB-MT FR1 FRC at current moment as no demand from operators
Issue 1-2-2: FRC-general parameters with different views
  FRC: Keep MCS, PRB allocation, SCS and CHBW information in FRC for core requirements; further discuss other detailed parameters in conformance phase.
    If any further information needed for core requirements, we can include them in conformance phase pending on further discussion.
  See following slides
Issue 1-3: FR1 IAB-MT RX dynamic range
  Agreement: no RX dynamic range to be defined for IAB-MT of FR1

## Slide 3: FRCs in 38.174
Based on discussion, R4-2011034 table 2 and 3 Only the top 5 rows are needed
Reference channel | G-FR1-Axx-1 | G-FR1-Axx-2 | G-FR1-Axx-3 | G-FR1-Axx-4 | G-FR1-Axx-5 | G-FR1-Axx-6
Subcarrier spacing (kHz) | 15 | 30 | 60 | 15 | 30 | 60
Allocated resource blocks | 25 | 11 | 11 | 106 | 51 | 24
CP-OFDM Symbols per slot (Note 1) | 9 | 9 | 9 | 9 | 9 | 9
Modulation | QPSK | QPSK | QPSK | QPSK | QPSK | QPSK
Code rate (Note 2) | 1/3 | 1/3 | 1/3 | 1/3 | 1/3 | 1/3
Payload size (bits) | 1672 | 736 | 736 | 6912 | 3368 | 1608
Transport block CRC (bits) | 16 | 16 | 16 | 24 | 16 | 16
Code block CRC size (bits) | - | - | - | - | - | -
Number of code blocks - C | 1 | 1 | 1 | 1 | 1 | 1
Code block size including CRC (bits) (Note 3) | 1688 | 752 | 752 | 6936 | 3384 | 1624
Total number of bits per slot | 5400 | 2376 | 2376 | 22896 | 11016 | 5184
Total symbols per slot | 2700 | 1188 | 1188 | 11448 | 5508 | 2592
NOTE 1: DL-DMRS-config-type = 1 with DL-DMRS-max-len = 1, DL-DMRS-add-pos = pos2 with = 2, = 6 and 9 as per Table 7.4.1.1.2-3 of TS 38.211 [3]. NOTE 2: MCS index 4 and target coding rate = 308/1024 are adopted to calculate payload size for receiver sensitivity and in-channel selectivity NOTE 3: Code block size including CRC (bits) equals to in sub-clause 5.2.2 of TS 38.212 [4]. |  |  |  |  |  | 
Table 2: FRC parameters for FR1 reference sensitivity level for IAB-MT.

## Slide 4: FRC’s in 38.174
Based on discussion, R4-2011034 table 2 and 3 Only the top 5 rows are needed
Reference channel | G-FR2-Axx-1 | G-FR2-Axx-2 | G-FR2-Axx-3
Subcarrier spacing (kHz) | 60 | 120 | 120
Allocated resource blocks | 66 | 32 | 66
CP-OFDM Symbols per slot (Note 1) | 9 | 9 | 9
Modulation | QPSK | QPSK | QPSK
Code rate (Note 2) | 1/3 | 1/3 | 1/3
Payload size (bits) | 4224 | 2088 | 4224
Transport block CRC (bits) | 24 | 16 | 24
Code block CRC size (bits) | - | - | -
Number of code blocks - C | 1 | 1 | 1
Code block size including CRC (bits) (Note 3) | 4248 | 2104 | 4248
Total number of bits per slot | 14256 | 6912 | 14256
Total symbols per slot | 7128 | 3456 | 7128
NOTE 1: DM-RS configuration type = 1 with DM-RS duration = single-symbol DM-RS, additional DM-RS position = pos2 with l0 = 2, l = 6 and 9 as per Table 7.4.1.1.2-3 of TS 38.211 [3]. NOTE 2: MCS index 4 and target coding rate = 308/1024 are adopted to calculate payload size. NOTE 3: Code block size including CRC (bits) equals to K' in sub-clause 5.2.2 of TS 38.212 [4]. |  |  | 
Table 3: FRC parameters for FR2 reference sensitivity level for IAB-MT.