## Slide 1: WF on power saving demodulation
Agenda Item: 7.6.4
Document for: Approval
Source: CATT
3GPP TSG-RAN WG4 #96e R4-2012645
Electronic Meeting, 17-28 Aug, 2020

## Slide 2: Background
Joint PDCCH-WUS and PDCCH test has been discussed in previous RAN4 meetings. The following WF was agreed in RAN4#95-e meeting
  RAN4 will further discuss detailed test set-up (simulation assumption) considering test feasibility and also need to be checked from RRM aspect.
  Make decision on whether introducing test cases in Q3 2020.
In RAN4#96-e meeting, it has been concluded under Email thread 214 in the 1st round that no additional RRM test case related to WUS will be defined.

## Slide 3: Background
In RAN4#96-e meeting, 3 test solutions were discussed on PDCCH-WUS/PDCCH testing.
Option 1 Joint PDCCH-WUS/PDCCH test
  Configure UE not to wake up when missing DCI format 2_6 in DRX-OFF period
  “Wake-up indication” in DCI format 2_6 is set to ‘1’
  Transmit PDCCH-WUS in DRX-OFF period and PDCCH in DRX-ON period with the SNR reference value
    No Power boosting for normal PDCCH
  Verify that BLER of PDCCH meets the following performance requirement
    Pm-dsg_total = PPDCCH-WUS + (1- PPDCCH-WUS) PPDCCH = 1.099% or 1%
Option 2
  ps-WakeUp is not configured and “Wake-up indication” in DCI format 2_6 is set to ‘1’
  drx-LongCycleStartOffset is set to ms10.
  Two search space sets for transmission of DCI format 2_6 is configured for UE, but there is only one position selected randomly to transmit DCI format 2_6 before each DRX on duration.
  Avoid the impact of normal PDCCH to PDCCH-WUS by setting high enough power level for normal PDCCH during the test.
  Transmit PDCCH-WUS in DRX-OFF period (opportunity for DRX) and PDCCH in DRX-ON period (On duration).
  Verify that BLER of PDCCH meets the performance requirement. (0.1%)

## Slide 4: Background
Option 3
  “PSWakeUpOrNot” should be set as “UE not wakeup” or not configured.
  Before every DRX active time, TE sends “1” indication in PDCCH-WUS once per 2 DRX cycles and sends “0” indication in PDCCH-WUS once per 2 DRX cycles.
  TE check whether UE behavior in the next DRX on-duration is under expectation or not, i.e. if UE sends periodic CSI during On-duration after TE sends PDCCH-WUS indication, or if UE does not send periodic CSI during On-duration after TE cancel the PDCCH-WUS transmission, ACK_WUS = ACK_WUS + 1; otherwise NACK_WUS = NACK_WUS + 1.
  Verify that PPDCCH-WUS meets the following performance requirement of 0.1%

## Slide 5: GTW session agreement (25th Aug. 2020)
RAN4 agree to introduce demodulation test cases for PDCCH-WUS in Rel-16.
The purpose of such test case was to verify UE supporting PDCCH-WUS feature/function designed in RAN1/RAN2.
Further discuss among option 1/option2 needed considering test time issue.
RAN4 also aware that with option 1/option 2, UE behaviour following PDCCH-WUS indication “0” is not verified.

## Slide 6: Way forward
Test solutions
  Option 1/2 listed in Slides#3 will be used for power saving test.
  Make a decision in next RAN4 meeting.
Test complexity aspects
  DRX cycle
  Use short DRX cycle of 10ms to reduce test time.
  It should be noted that using 10ms is only for test purpose and has no relation to real deployment.
  Number of error samples
  TBD error samples will be used.
  Note: Currently RAN5 uses 1000 error samples which is time consuming. Need feedback from TE vendors whether 100 error samples are feasible.

## Slide 7: Simulation assumptions (1/2)
Parameter |  | Unit | Value
Carrier configuration | Offset between Point A and the lowest usable subcarrier on this carrier |  | 0
DL BWP configuration #1 | Cyclic prefix |  | Normal
 | RB offset | RBs | 0
Common serving cell parameters | Physical Cell ID |  | 0
 | SSB position in burst |  | 1
 | SSB periodicity | ms | 20
PDCCH DCI format 2_6 configuration | Slots for PDCCH monitoring |  | Each slot
 | Number of PDCCH candidates |  | 1
 | Frequency domain resource allocation for CORESET |  | Start from RB = 0 with contiguous RB allocation
 | TCI state |  | TCI state #1

## Slide 8: Simulation assumptions (2/2)
Parameter | Value | 
 | PDCCH-WUS | PDCCH
DCI format | 2_6 | 1_0, 1_1
Bandwidth | 10MHz | 
SCS | 15kHz | 
Number of BS antennas | 1Tx, 2Tx | 
Number of UE antennas | 2Rx, 4Rx | 
DM-RS channel estimation | Realistic | 
Channel model | TDLA30-10, TDLC300-100 | 
DCI length (excluding 24bits CRS) | 12 bits, 36 bits, 30bits | 39bits, 52bits
Aggregation level | 8, 16 | 4, 8
CORESET symbol | 2 | 
CORESET bandwidth | 48RB | 
Mapping type | Interleaved(size2), Not Interleaved | Interleaved(size2), Not Interleaved
REG bundle size | 6 | 

## Slide 9: References
[1] R4-2009721
[2] R4-2009811
[3] R4-2010101
[4] R4-2010478
[5] R4-2010718
[6] R4-2010995