## Slide 1: Way Forward on ultra-low BLER requirements
R4-2012646
Moderator (Ericsson)

## Slide 2: Agreements in first round
Test tolerance for BS requirement: Adopt 0.3dB
No ultra-low BLER requirements for the following features within this WI (high BLER requirements for these features to be discussed separately in thread 319):
  PDCCH enhancements
  Multi-TRP for URLLC
  PUSCH repetition type B
  UCI enhancements

## Slide 3: Agreements in second round
FR2:
  Not introduce FR2 requirements in Rel-16 for URLLC with ultra-BLER.
CQI:
  From GTW:
    Work assumption: Introduce ultra-BLER static CQI test cases under the assumption that test time is similar as Fixed MCS test cases ; further discuss how to ensure reasonable test time with below possible options:
      -Decrease confidence level (from 99.999% ~95%)
      -Early pass/fail criteria
    Note both options adopted not excluded.
  How to define the requirement:
    Median CQI, BLER for median CQI and median CQI+1 or median CQI - 1

## Slide 4: Agreements in second round
Test applicability for the BS:
  If both 15kHz and 30kHz SCS are supported, the manufacturer can declare/decide which one is tested.
BS test methodology:
  Captured in Annex
  Applicable for 10^-5 BLER and 99.999% CL only
  Asymmetric per step risks should be used, as in RAN5 LTE (TS 36.521-1, G.7.10) and RAN5 NR (TS 38.521-4 G.2.10).
  Include a table of decision co-ordinates

## Slide 5: Agreements in second round
No requirement for 10^-6 BLER in rel-16
Note on X in BS spec:
  1dB is added to the test requirement to facilitate early test pass. The BLER delivered by the device during the test will be lower than the test requirement, which enables compliance to the requirement to be demonstrated with a number of observed block errors lower than a certain threshold.

## Slide 6: Open issues
CQI:
  Confidence level, early pass/fail criteria as discussed in GTW session
  Applicability rule for fixed MCS and CQI testing
    To be discussed further once CQI requirement/test is resolved
Detailed description of the test methodology in the BS conformance specification
  RAN5 description should be a starting point
  Companies are encouraged to provide proposed text for the next meeting; please co-ordinate with the editors for the 38.141-1 and 38.141-2 CRs for ultra-low BLER
  Companies are encouraged to contribute on the per step risk and the decision co-ordinates table in particular for the next meeting

## Slide 7: Agreed simulation assumptions (UE)
Parameter |  | Value
Frequency range |  | FR1
Transform precoding |  | Disabled
Duplex mode |  | FDD/TDD
Antenna configuration |  | 1x2, ULA low 1x4, ULA low
PDSCH configuration | Mapping type | Type A
 | Starting symbol (S) | 2
 | Length (L) | 12
 | PUSCH aggregation factor | 1
PDSCH DMRS configuration | DMRS Type | Type 1
 | DM-RS duration | Single-symbol DM-RS
 | Number of additional DMRS | 1
Number of HARQ Transmissions |  | 1
PT-RS |  | Disabled
Propagation condition |  | AWGN
MCS Table |  | Table 3, MCS14
SCS and BW |  | FDD:15KHz, 10MHz TDD:30KHz, 40MHz
Frequency domain resource |  | Full BW
TDD pattern |  | 7D1S2U (S=6:4:4)
Testing metric |  | Target BLER: 10-5

## Slide 8: Agreed simulation assumptions (BS)
Parameter |  | Value
Frequency range |  | FR1
Transform precoding |  | Disabled
Antenna configuration |  | 1x2, ULA low
PUSCH configuration | Mapping type | Type A and Type B
 | Starting symbol (S) | 0
 | Length (L) | 14
 | PUSCH aggregation factor | 1
PUSCH DMRS configuration | DMRS Type | Type 1
 | DM-RS duration | Single-symbol DM-RS
 | Number of additional DMRS | 1
Number of HARQ Transmissions |  | 1
PT-RS |  | Disabled
Propagation condition |  | AWGN
MCS Table |  | Table 3, MCS 5
SCS and BW |  | 15 kHz for 5, 10 MHz 30 kHz for 10,40 MHz
Frequency domain resource |  | Full Bandwidth
TDD pattern |  | 15 kHz SCS: 3D1S1U, S=10:2:2 30 kHz SCS: 7D1S2U, S=6:4:4
Testing metric |  | Target BLER: 10-5